## Slide 1: Antennas & Receivers in Radio Astronomy
Jay Blanchard
Notes: Sergio
So now that Rick has introduced the fundamentals, we can dive in to real systems and how they behave, starting with ..

## Slide 2: Purpose & Outline
Purpose: describe how realizable antenna elements can affect the quality of images produced by an aperture synthesis array
Antennas
  Fundamentals (antenna types and terminology)
  Reflector antenna mounts and optics
  Aperture efficiency
  Pointing
  Polarization
Receivers and Noise Temperature
Based on slides from:
Rob Selina
Mark McKinnon
Craig Walker
And others!
Notes: Transmissive and reflective analysis analogy.

## Slide 3: Antenna Electronics Block Diagram
Low-Noise
Amplifiers
Digitizers
Local Oscillator
Freq. Converters
Antennas
Correlator
Analog to Digital Converter Input:
Electric Current
~1mW
Limited Frequency
Sky EM
Frequency Down-conversion
(when needed)
Signal Amplification
G ~ 80 dB (x108 in power)
EM to Electric Current, w/ Gain
Notes: EM wave -> LNA
Field collection (amp), impedance match to waveguide input
Electrical RF signal
Digitization
G=(kT_sys*BW)/P_out
Heterodyne

## Slide 4: Effects of Antenna Properties on Data
Antenna amplitude pattern causes amplitude to vary across the source.
Antenna phase pattern causes phase to vary across the source.
Polarization properties of the antenna can modify the apparent polarization of the source.
Antenna pointing errors can cause time varying amplitude and phase errors.
Variation in noise pickup from the ground can cause time variable amplitude errors.
Deformations of the antenna surface can cause amplitude and phase errors, especially at short wavelengths.
Notes: Intensity distribution on sky
Antenna has own amplitude/phase distribution.
Multiply together

## Slide 5: Antenna Types
Purpose of an antenna: capture radiation from an object and couple it to a receiver for detection, digitization, and analysis
Wire antennas
  Dipole, Yagi, Helix, or small arrays of each type
Reflector antennas
Hybrid antennas
  Wire reflectors
  Reflectors with dipole feeds
Notes: 300 MHz = 1m

## Slide 6: Dipole Antenna
Incoming EM wave ‘pushes’ electrons to each end.
Electrons build up on each end.
Current flow as the wave moves.
Sets up a standing voltage wave.
Receiver at center.
Credit chetvorno

## Slide 7: Beam Patterns
Half wave dipole
Credit Timmons 2022
Credit COMSOL
Parabolic
Yagi
Credit Phaebua 2021

## Slide 8: Horn Antenna
Used to detect CMB!
Still in use for RA today.
Easy to build
Provides illumination of the main dish/subreflector.

## Slide 9: Terminology & Definitions - I
Effective collecting area, A(n,q,f) m2
On-axis response, A0 = hA
= aperture efficiency
Normalized pattern (primary beam)
A(n,q,f) = A(n,q,f)/A0
Beam solid angle (field of view)
WA= ∫∫ A(n,q,f) dW
all sky
Notes: Frequency and direction coordinates (spherical). Theta offset from boresight (polar), phi is azimuth around it.
Radiation power received over a given bandwidth and solid angle is given by … Intensity as a function of frequency and direction.
“antenna receiving/reception pattern” (power pattern)
“beam solid angle of the power pattern” integral over the full sky

## Slide 10: Terminology & Definitions - II
A0 WA = l2 Effective area (gain) & solid angle (field of view)
  Can have large effective area or large solid angle, but not both at the same time
Antenna sidelobes and backlobes
  Increase system temperature due to ground pick up
  Make antenna susceptible to RFI
  Sidelobes can limit image dynamic range by detecting strong background sources
What determines the beam shape? …
Notes: Wavelength squared goes as effective area times beam solid angle. Physically impossible.

## Slide 11: Illumination-Beam Shape Comparisons
Antenna’s far-field radiation pattern (beam) is related to the Fourier transform of its aperture distribution (illumination pattern)
Credit: Hunter
q3dB = 1.02/D
First null = 1.22/D
D = diameter in wavelengths
Notes: ‘Illumination’ Engineering convention – transmit and receive analogy

## Slide 12: Antenna Mounts: Altitude over Azimuth
Advantages
  Cost
  Gravity performance
Disadvantages
  Zone of avoidance
  Beam rotates on sky
Notes: Key enabler was two-axis servo control electronics.
180 deg spin or over-the-top example
Gravity – only elevation dependent.

## Slide 13: Alt-Az: Beam Rotation on the Sky
Parallactic angle
Notes: Move counterclockwise in our reference frame
Response changes due to orientation in beam. Especially relevant for a polarized source.

## Slide 14: Antenna Mounts: Equatorial
Advantages
  Tracking accuracy
  Beam doesn’t rotate
Disadvantages
  Cost
  Gravity performance
  Sources on horizon at pole
Notes: GB Specs? 140’ (43m)
Normal pointed at Polaris
Earth spins east, telescope spins west
1965

## Slide 15: Antenna Optical Configurations
Cassegrain
Naysmyth
Prime Focus
Offset Cassegrain
Beam Waveguide
Dual Offset
GMRT
VLA
VLBA
ALMA
NRO
ATCA
CARMA
GBT
SKA
ngVLA
Notes: ALMA? Offset Cass
Nobeyama
Australia telescope compact array

## Slide 16: Optical Configurations, Pros & Cons - I
Prime Focus
  Can be used over entire frequency range of the reflector
  Over-illumination (spillover) can increase system temperature due to ground pick-up
  Number of receivers and access to them is limited
Multiple reflector Cassegrain systems
  More space, easier access to receivers, reduced ground pick-up
  Any spillover is on cold sky; better for low system noise
  Can limit low frequency capability. Feed horn too large
  Over-illumination by feed horn can exceed the gain of the primary reflector’s sidelobes
    Strong sources a few degrees from the antennas’ main bean may limit image dynamic range

## Slide 17: JVLA Feed Horns
Credit: Ruff & Hayward

## Slide 18: Optical Configurations, Pros & Cons - I
Prime Focus
  Can be used over entire frequency range of the reflector
  Over-illumination (spillover) can increase system temperature due to ground pick-up
  Number of receivers and access to them is limited
Multiple reflector Cassegrain systems
  More space, easier access to receivers, reduced ground pick-up
  Any spillover is on cold sky; better for low system noise
  Can limit low frequency capability. Feed horn too large
  Over-illumination by feed horn can exceed the gain of the primary reflector’s sidelobes
    Strong sources a few degrees from the antennas’ main bean may limit image dynamic range

## Slide 19: Optical Configurations, Pros & Cons - II
Offset optics (Gregorian or Cassegrain)
  Unblocked aperture:
    higher aperture efficiency, lower sidelobes, less scatter / lower system temperature
  Practical low-frequency feed designs.
  Support structure of offset geometry is more complex and expensive
  No rotational symmetry – more expensive panel tooling due to multiple panel sizes

## Slide 20: Aperture Efficiency
rms error s
On axis response: A0 = hA, Efficiency: h = hsf . hbl . hs . ht . hmisc
hsf = Reflector surface efficiency
Due to random imperfections in reflector surface
hsf = exp(-(4ps/l)2) e.g., s = l/16 , hsf = 0.5 (Ruze)
hbl = Blockage efficiency. Caused by subreflector and its support structure
hs = Feed spillover efficiency. Fraction of power radiated by feed intercepted by subreflector
ht = Illumination taper efficiency. Outer parts of reflector illuminated at lower level than inner part
hmisc= Reflector diffraction, feed position phase errors, feed match and loss
Notes: Check Ruze math.
1m, 300 MHz, 6 cm rms
1cm, 30 GHz, 600 um

## Slide 21: Surface Errors
Correlated surface errors can produce an error scatter pattern
  Pattern width determined by size-scale of correlations (e.g. panel size)
  Level could exceed that of sidelobes
ALMA surface panel
adjustment: phase map
Notes: Mm – bands? (scale in um)

## Slide 22: Antenna Gain - I
Antenna gain (on-axis response) varies with elevation, primarily due to the redistribution of gravitational forces within the antenna backup structure
credit: Hunter

## Slide 23: Antenna Gain - II
Gravitational distortions and elevation-dependent gain can be compensated with an active surface
GBT active surface: 2004 surface panels, 2209 surface actuators
20 GHz
Credit: Prestage & Maddalena
Notes: Richard, Ron.

## Slide 24: Antenna Pointing: Practical Considerations
Subreflector mount
Quadrupod
El encoder
Reflector structure
Alidade structure
Rail flatness
Az encoder
Foundation

## Slide 25: Antenna Pointing
“Blind” pointing: ALMA - 2”; VLA - 20”; VLBA – 15”
Pointing performance can be improved by measuring pointing errors via frequent observations of a nearby calibration source
  Offset or reference pointing: ALMA – 0.6”; VLA -10”;VLBA-5”
Desired accuracy: Dq < q3dB /20
Large intensity variations at
beam edge with Dq < q3dB /10
credit: Hunter

## Slide 26: Antenna Polarization Properties
Instrumental polarization can:
  cause an unpolarized source to appear polarized
  alter the apparent polarization of a polarized source
Two components of instrumental polarization
  constant or variable across the beam
Sources of instrumental polarization
  Antenna structure:
    Symmetry of the optics
    Reflections in the optics
    Curvature of the reflectors
  Circularity of feed radiation patterns
  Quality of FE polarization separation (constant across the beam)

## Slide 27: Polarization Beam Patterns
Co-polarization pattern
Cross-polarization pattern
ALMA Band 3 (100GHz)
Credit: Hunter

## Slide 28: Front End Polarization Separation - I
Dual-polarization receivers needed for best sensitivity and polarization observations
Two types of devices in use: OMT and wire grid
Waveguide-type Orthomode Transducer (OMT)
  After the feed horn; longer wavelength
ALMA Band 3 OMT
ALMA Band 2+3 OMT (inside)
VLA S-band OMT
(Gonzalez and Shinichiro, NAOJ)
Notes: Modified Boifot double-ridged waveguide junction; septum

## Slide 29: Front End Polarization Separation - II
Quasi-optical: Wire Grid
  Before the feed horn; shorter wavelength
  Grid reflects one polarization, passes the other
Credit: Hunter

## Slide 30: Jones Calculus
Jones vector describes fully polarized light in an easy way
Allows for Jones Matrixes to do e.g. rotations.
Partially polarizes light requires Mueller calculus.
Stokes Parameters.

## Slide 31: Receivers: Noise Temperature
Reference the received power to the equivalent temperature of a matched load at the input to the receiver
Rayleigh-Jeans approximation to Planck radiation law for a blackbody
Pin = kBT  (W)
kB = Boltzman’s constant (1.38*10-23 J/oK)
When observing a radio source, Ttotal = TA + Tsys
  Tsys = system noise when not looking at a discrete radio source
  TA = source antenna temperature

## Slide 32: Receivers: SEFD
Tsys = Treceiver + Tground + Tsky
Tsky = Tatm×(1 − e−t sin(elv)) + TCMB + TRB
TA = AS/(2kB) = KS
S = source flux (Jy)
SEFD = system equivalent flux density
SEFD = Tsys/K (Jy)
Band (GHz) |  | Tsys | SEFD
1-2 | .50 | 21 | 236
2-4 | .62 | 27 | 245
4-8 | .60 | 28 | 262
8-12 | .56 | 31 | 311
12-18 | .54 | 37 | 385
18-26 | .51 | 55 | 606
26-40 | .39 | 58 | 836
40-50 | .34 | 78 | 1290
EVLA Antenna Sensitivities
Notes: SEFD – source flux that would be needed to double system temperature
k_b – J/K (watt*sec)
k_b - W/Hz/K
Jy = 10^(-26) w/m^2/Hz
K_b = 1.38e3 Jy*m^2/K

## Slide 33: Receivers: Noise Temperature

## Slide 34: Receivers: SEFD
Tsys = Treceiver + Tground + Tsky
TA = AS/(2kB) = KS
S = source flux (Jy)
SEFD = system equivalent flux density
SEFD = Tsys/K (Jy)
Band (GHz) |  | Tsys | SEFD
1-2 | .50 | 21 | 236
2-4 | .62 | 27 | 245
4-8 | .60 | 28 | 262
8-12 | .56 | 31 | 311
12-18 | .54 | 37 | 385
18-26 | .51 | 55 | 606
26-40 | .39 | 58 | 836
40-50 | .34 | 78 | 1290
EVLA Antenna Sensitivities
Notes: SEFD – source flux that would be needed to double system temperature
k_b – J/K (watt*sec)
k_b - W/Hz/K
Jy = 10^(-26) w/m^2/Hz
K_b = 1.38e3 Jy*m^2/K

## Slide 35: JVLA Receivers – RF Sections
Credit: Harden & Hayward

## Slide 36: JVLA Receiver Performance
Credit: Hayward

## Slide 37: ALMA Receivers
credit: Hunter
Receivers are dual linear polarization

## Slide 38: ALMA Front End Cryostat

## Slide 39: Closing Thoughts
Antenna amplitude/phase pattern causes amplitude/phase to vary across the source.
Polarization properties of the antenna can modify the apparent polarization of the source.
Antenna pointing errors can cause time varying amplitude and phase errors.
Deformations of the antenna surface can cause amplitude and phase errors, especially at short wavelengths.
Even state-of-the-art receivers add thermal noise that is often larger than the source signal.
Receiver gain and noise can fluctuate with time and physical temperature.
However, knowledge of the system and its behaviors enables you to compensate/correct many of these effects through Calibration.
Notes: Jy = 10^(-26) w/m^2/Hz

## Slide 40: Additional Information
General: Synthesis Imaging in Radio Astronomy II: ed. Taylor, Carilli, & Perley
  https://leo.phys.unm.edu/~gbtaylor/astr423/s98book.pdf
ALMA antennas and receivers: ALMA Technical Handbook
  https://almascience.nrao.edu/proposing/technical-handbook
EVLA receivers:
  http://www.aoc.nrao.edu/evla/admin/projbook/chap5.pdf
ngVLA Antennas & Receivers:
  https://ngvla.nrao.edu/page/projdoc