## Slide 1
Error Recognition
Natalie Butterfield
With thanks to Amanda Kepley, Greg Taylor, Amy Kimball, Aaron Lawson, Sergio Garza, Devaky Kunneriath, Ilsang Yoon, Todd Hunter, Sumit Sarbadhicary, Ryan Loomis, Erica Keller, Drew Medlin, James Khor
Notes: (introduce me and talk title) - mention thanks to co-authors,
When I was an early graduate student, I sat in this audience and saw a version of this talk by Greg Taylor, and it actually ended up being one of my most visited talks of the Imaging workshop. In this talk we will cover a variety of bad data examples both in visibility data and imaging and I hope you all will be able to refer to these slides as you grow as radio astronomers.

## Slide 2
Understanding your data is key for doing good science!
Most ALMA/VLA data today is run through a calibration (and potentially imaging) pipeline and QA process.
It’s still useful to be able to recognize issues in your data.
  The pipelines and QA are very good, but sometimes issues sneak through.
  Age of F/S lane you may be the first to see the pipeline results!
  You may have more stringent science requirements than what is checked by standard QA.
  Sometimes you have to calibrate the data from scratch, so you need to be able to ID problems on your own.
Your data = your responsibility.
  Don’t just blindly accept results!
Notes: QA=Quality Assurance

## Slide 3
Focus will be on VLA and ALMA data and CASA
These techniques are generally applicable for all interferometric data.
Other data reduction packages have similar plotting functionality.

## Slide 4
Many useful plots are in pipeline weblogs!
VLA Weblog
ALMA Weblog
Notes: Many of the plots shown in this talk are available in the weblogs.
Pulled figures from weblog examples
Theres a tutorial on VLA and ALMA weblogs later today

## Slide 5
Common sources of issues with interferometric data (not exhaustive)
Non-ideal
calibrators
Atmosphere
Mis-behaving
antennas
Mis-behaving
correlator
Astronomer
RFI
Visibilities:
  Time
  Frequency
  UV distance
Images
Notes: -Non-ideal calibrators – user error or source has changed
-Atmosphere- changing weather
-RFI which we heard about last week
-Misbehaving antennas – don’t go into detail about why they are misbehaving only that they are not performing as expected
-misbehaving correlator - When correlating the signal
Roughly group the sources of error into 4 categories
Time based; frequency based; UV distance
Image errors (Algorithm based)

## Slide 6
Looking at both visibility data and images can help uncover issues.
FT
FT
FT
FT
Point
Plane
2 Points
Ripples
Narrow Gaussian
Wide Gaussian
Wide Gaussian
Narrow Gaussian
Notes: -When looking at the data and trying to figure out where the errors are coming from it’s good to look at both the visibility data and the images
-Reason why is that some features are easier to spot in one vs the other
-Here some examples showing some of the common fourier transforms which you have seen last week:
-Point source fourier transforms to a plane …(say the rest)
-these can help uncover issues; for example, 2 point sources are not obvious in the top but easier to spot as ripples –we will see an example of this later

## Slide 7
Calibrator sources have known properties and thus are good for identifying problems.
Flux calibrator:
  Used to set flux scale of observations (i.e., Jy).
  Source with a well-known flux density.
  Source may be extended and thus require the use of models to derive an accurate flux calibration.
Bandpass calibrator:
  Used to calibrate frequency response of the system.
  Brighter the better.
  Often the same as the flux calibrator, but not always.
Gain calibrator (also known as phase or secondary calibrator)
  Used to derive complex gains (amplitude and phase) vs. time.
  Located near (~few degrees) the target.
  Point sources strongly preferred.
Notes: Cals should have known properties
-3 main calibrators
-briefly go over cals for completeness but this should be familiar from last week and the tutorials yesterday

## Slide 8
What does an ideal calibration look like?
see Josh’s Thursday talk on calibration for more information
Visibility domain:
  Bandpass amplitude changes smoothly with frequency and phases are close to zero.
  Gain calibrator has consistent amplitude with time with phases close to zero.
  Flux calibrator amplitude should be consistent with expected value. May have structure.
Image domain
  Calibrated images have the structure you expect (e.g., point source or extended)
  High S/N detections of calibrators
  Lack of artifacts and sidelobes
  Flux density of calibrators is as expected.
Notes: Visibility domain is how you can identify which antennas or time stamps or baselines might be bad data,
but sometimes it is easier to see errors in the imaging domain as we will see later in this talk

## Slide 9
The CASA task plotms can be used to examine visibility data and calibration tables.
Most commonly used tabs
2nd most commonly used tabs
Zoom
Print data point information
Home
See https://casadocs.readthedocs.io for more info
Notes: You have probably seen plotms yesterday in the tutorials. Most of the plots shown in this talk were generated in plotms using different selection criteria
(go over labels)
-go over how to select datapoints
-if loading a cal table, use the green buttons to navigate the different plots

## Slide 10
Amplitude and phase vs. time
Good to check for time-based issues:
  Telescope not quite on source
  Misbehaving antennas
  Shadowing
  RFI
Calibrations should have a constant amplitude with time that is consistent with the known flux density.
Phases should be zero (point source).
Averaging by antenna and channel suggested.
Notes: -this is after the apply cal
--Averaging by antenna and channel are suggested – Ill show an example of this plot without averaging
VLA often has dropouts at beginning of scans while it’s getting on-source [xxx get example of this]

## Slide 11
A word about averaging
Often will need to average data to increase S/N
No averaging
Notes: Here is an example without averaging.
If we don’t average the data it doesn’t seem very meaningful
Average over the orthogonal axis (time -> freq) or (freq -> time)
-since we are plotting time, we want to average over frequency (ie channel)

## Slide 12
A word about averaging
Average on axes orthogonal to the plot
X-axis is time,
so averaging over
all channels
Notes: Average over the orthogonal axis (time -> freq) or (freq -> time)
Averaging improves the S/N considerably

## Slide 13
A word about averaging
Average in the orthogonal direction to the plot
Averaging over
all channels
(zoom in)
Notes: Top plot now zoomed in  see that

## Slide 14
A word about averaging
Average by antenna (fundamental calibration quantity)
Averaging
over all channels
and per antenna
(zoom in)
This looks weird!
Notes: If plotting multiple antennas want to average per antenna
Our solutions are often antenna based (per antenna) so we we want to average over antenna to look for outliers

## Slide 15
Looking at calibration tables can be helpful!
Uncalibrated data
Calibrated data
Looks like DV04 has something funny going on
Caltable
Discontinuity
“Typical” Antenna
Notes: This is a demonstration of looking at the calibration tables
Top is uncalibrated data, which show there is a discontinuity –this is picked up in the cal table –looks nothing like the other antennas (which are consistent with time)
When you calibrate it it flattens out which is great,
2016.1.01400.S

## Slide 16
Amplitude and phase vs. time
Sometimes antenna phases will change too rapidly due to hardware issues
Prevents phase vs. time solution.
If that antenna is your reference antenna, then these bad solutions can propagate to the other antennas.
Solution: flag bad antenna and exclude it as a refant
Bad antenna as refant
refant
Changed refant to good antenna
refant
Notes: Here is another caltable showing phase v time.
-looks fine in the middle but what is this going on here (highlight jumps, not good) – we want to flag these data points and remove them
-now discuss refant

## Slide 17
Amplitude and phase vs. frequency plots
Good to check for frequency-based issues:
  RFI
  Correlator issues
  Spectral lines (either atmospheric or science lines)
Suggested averaging by all scans and either per antenna or all baselines.
Calibrators should have the correct amplitudes.
  But older flux density measurements may no longer be accurate due to changes in calibrator flux densities.
Phases generally near zero, although flux calibrators may show structure.
VLA
S-band
Bandpass calibrator
Notes: Now look at amp/phase vs freq plot
-good for looking at frequency based issues (I will show on the next slide some of these issues)
-since we are plotting freq – average over time
(read points)
(now discuss fig)
-can observe the spectral index

## Slide 18
Flagged bad spectral window
Amplitude and phase vs. frequency plots
RFI
VLA
S-band
Bandpass calibrator
RFI
Bad spw
Automated RFI flagging with
tfcrop and rflag
Notes: -RFI is observed
-possible edge channel artifacts
-some possible bad data around 3.5-4 GHz – can colorize by antenna to see if this antenna based or a bad baseline

## Slide 19
Amplitude and phase vs. frequency plots
Correlator issues show up particularly well in amplitude/phase vs. frequency plots.
Example of one type of deformatter issue at the VLA.
  At the telescope the electronic signal is converted to an optical one to go down the optical fibers.
  At the correlator the signal is deformatted to an electronic signal.
  Some times this doesn’t happen as it should and you get strong amplitude/phase slopes with frequency.
Features like this are generally caught by telescope support teams or QA.
This doesn’t look good!
Notes: Correlator issues are typically freq based issues
-many different types of correlator issues, this is just one example
(go over example points) deformatted -> converted back
(observed in the cal tables)
-features caught by team but good to know what they look like)
Not all correlator problems look like this
- in case anyone asks: bad deformatters is something that the telescope support team identifies, and if they don't spot it the DAs working on calibration QA certainly will. So these things happen from time to time (not too rare) but get fixed pretty quickly; almost certainly they'd be fixed by the time the data gets to the user. (In other words... this is not something that needs to be reported back from the user.)

## Slide 20
Amplitude and phase vs. frequency plots
Can also reveal the effects of atmospheric lines
More important for ALMA than VLA
Atmospheric
model
Noise higher near
atmospheric
line
Science cube shows higher noise
there as well.
Notes: Noise increase at these frequencies.

## Slide 21
Amplitude and phase vs. frequency plots
Averaged
visibilities
Spectrum
From cube
You can average target source visibilities together to see if you have line emission and determine continuum subtraction ranges.
Faster than imaging the cube.
The visibility spectrum won’t correspond exactly to the line cube spectrum except for point sources at phase center.
Notes: -quick way to see if you have spectra lines in your obs is to average target visibilites. -- use to identify line free channels for continuum subtraction.
-difference is due to the emission not being at the phase center

## Slide 22
Amplitude vs. uvdistance plots
Good to check for baseline-based issues:
  RFI
  Source structure
Averaging by channel and time (possibly over scans) suggested.
Calibrators should have the correct amplitudes.
Point sources should be straight, horizontal lines (recall your FT pairs).
  Amplitude = source flux density
  Phase = 0deg
ALMA Band 7
Phase calibrator
Colored by correlation
Notes: -ALMA example
-RFI- spectral line talk, RFI is worse at shorter baselines due to the cross correlation
-phase cal should be a point source – therefor a horizontal line
-source amp isn’t changing over freq – not always true especially at low freq

## Slide 23
Amplitude vs. uvdistance plots
VLA S-band
Phase calibrator
Colored by spw
If source flux changes across band, can have different amplitudes for different spectral windows.
But phase calibrator still looks point like (i.e., straight horizontal line)
NB: UVwave is just the UVdistance expressed as number of wavelengths.
Notes: Offsets is due to the spectral index across different spws. Why the high freq windows extend further out in the UVWave distance
Each window is a straight line

## Slide 24
Amplitude vs. uvdistance plots
VLA S-band
Flux calibrator
Colored by spw
Band 7 ALMA
Callisto
Disk!
Flux calibrator
slightly extended
Flux calibrator
is a resolved disk
FT
See Rick Perleys talk on visibilities examples!
Notes: -they don’t have to be straight lines in uv space – here are some examples of flux cals that aren’t point sources
-callisto – beginning to see a Bessel function in the uv space – which Fourier transforms to a disk.
(FT image)
-if you have a sharp disk that fourier transforms to a Bessel function

## Slide 25
Real vs. imaginary
Gain calibration should be point source at phase center.
  Assuming picked good calibrator and calibration is good.
Real component ~ amplitude of gain calibrator
Imaginary component ~ 0 (since it’s a point source)
Bad antenna!
Notes: -fun plot in plotms, not included in the weblogs, but can highlight bad antennas
Very distinctive plot as things pop out real quick
(bring up second plot)
Example of a bad antenna

## Slide 26
Common sources of issues with interferometric data (not exhaustive) – A Cheat Sheet
Non-ideal
calibrators
Atmosphere
Mis-behaving
antennas
Mis-behaving
correlator
Astronomer
error
RFI
Time
Frequency
UV distance
Frequency
Time
Real vs. Imaginary
Time
Frequency
Frequency

## Slide 27
Now let’s switch to the imaging side!
Credit: Pasetto et al., Sophia Dagnello, NRAO/AUI/NSF.
Credit: ALMA(ESO/NAOJ/NRAO); C. Brogan, B. Saxton (NRAO/AUI/NSF)
Notes: (read title) – Some issues are better seen in the imaging stage
-now I am going to talk about error recognition in the imaging stage

## Slide 28
CARTA can be used to examine images.
The tutorials include interacting with data!
https://cartavis.org/

## Slide 29
Calibration errors can affect your images.
Point source observed with VLA
13x5min observation over 10 hrs
no errors:
max 3.24 Jy
rms 0.11 mJy
Notes: Now we are going to talk about how calibration errors can affect your images.
(go over points)
-thermal noise (non-patterned noise) in here but no antenna based error

## Slide 30
Calibration errors can affect your images.
10% amplitude error for all antennas for 1 time period
rms 2.0 mJy
6-fold symmetric pattern due to VLA “Y”.
Image resembles dirty beam.
Notes: If we add in a 10% amp error for all antennas at one time stamp
-> We get this 6-fold…

## Slide 31
Calibration errors can affect your images.
10 deg phase error for one antenna at one time
rms 0.49 mJy
20% amplitude error for one antenna at one time
rms 0.56 mJy
anti-symmetric ridges
Imaginary = sin (phi)
symmetric ridges
Real = cos(phi)
+
––
+
Notes: If we take the errors and reduce it to one antenna at one time – either a 10 deg phase error for one antenna at one time or a 20% amp error…
-we get these similarly sized calibration errors
The thing to remember is that the artifacts are slightly different
-if it’s a phase error (that the imaginary part) its sine – anti symmetric (+/-)
-if its an amp error (that’s the real part) so it’s a cosine so its symmetric

## Slide 32
Calibration errors can affect your images.
10 deg phase error for one antenna all times
rms 2.0 mJy
20% amplitude error for one antenna all times
rms 2.3 mJy
rings – odd symmetry
Imaginary = sin(phi)
rings – even symmetry
Real = cos(phi)
+
––
+
+
Notes: If we take these errors for one antenna at one time and extending them to one antenna for all times -- we get these arcs
-here you can see the tracks that we make through uv-space
-but the symmetry will be the same as the artifacts we saw on the previous slide
(pause) – these example slides will be very helpful in identifying errors in your images associated with bad data.
-ok, so you have noticed an error in your image – how do you identify which antenna is problematic? You go back to the visibilities

## Slide 33
A real life example
Bad
antenna
Significant
image
artifacts
Dirty image
Post-clean residuals
Notes: Real life example of a bad antenna in both phase and amplitude (freq and phase; freq and amp)
1. dirty image shows swirly artifacts
2. when you clean you still see this artifacts
3. Looks like a super position of the phase and amp error we saw on the previous slide
(enter for pop up) -we would have spotted this in the real v. imaginary plot (same example)

## Slide 34
Another real life example
Bad baseline leading to stripes across VLASS image
Remember that point source off phase center has a phase.
Size of ripple inversely related to length of bad baseline.
Orientation of the ripple related to u-v orientation of baseline.
FT
Notes: -Another real life example of a bad baseline causing strips across VLASS image
1. Point-source is off center that give us a phase error
2. the size of the ripple is inversely related to the length of the baseline
3. must be a longer baseline to cause the narrower ripples
4. solution is to flag that baseline and re-image

## Slide 35
Another real life example
VLA 6 prong “Y-pattern” visible in psf
Image
psf
Notes: -Another real life example of a bad baseline causing strips across VLASS image
Psf shows the y-pattern that we saw in the earlier example
An amplitude error

## Slide 36
Clean can diverge.
More likely for data with high sidelobes and complex emission.
Will let you know in the log if has diverged.
Image usually has “grating” like artifacts.
Check your mask and model. Are you only including believable emission?
Trigger major cycles more often (using cycleniter or cyclefactor) to reconcile the model and data more frequently.
Grating-like artifacts
Notes: One of the more common issues with bright emission. Can look like ripples but is usually localized
-issue with your clean boxes
2019.1.00263.S MOUS: uid://A001/X1465/X3467 source: G34.26+0.15 (target) cubes spw 25 and 31

## Slide 37
Clean can diverge.
More likely for data with high sidelobes and complex emission.
Will let you know in the log if has diverged.
Image usually has “grating” like artifacts.
Check your mask and model. Are you only including believable emission?
Trigger major cycles more often (using cycleniter or cyclefactor) to reconcile the model and data more frequently.
Can also cause “bright” spots
Notes: One of the more common issues with bright emission. Can look like ripples but is usually localized
-issue with your clean boxes
2019.1.00263.S MOUS: uid://A001/X1465/X3467 source: G34.26+0.15 (target) cubes spw 25 and 31

## Slide 38
Clean can diverge.
Clean was truncated due to divergence  Check the casalogger!
image
residuals
Also produced a “hole” in the PB coverage
Notes: Clean was truncated in this example and resulted in a “hole” in the primary beam coverage
-check the logger! It will tell you if clean diverged

## Slide 39
Clean can diverge.
Errors can also be seen in the mask and residuals
image
residuals
psf
mask
Notes: Errors can be seen in the mask and residuals
2. (pop up) This one was from high weights affecting data:
3. flagging the affected timerange solved this particular issue

## Slide 40
Keep an eye out for aliasing!
Dirty image of a multiple pointing mosaic. Beams should look circular
Aliasing
Primary beam should look circular!

## Slide 41
Non-optimal parameters can affect your images.
Cell size good.
Image size good.
Cell size too big.
Image size good.
Cell size too big.
Image size too small.
Non-optimal choices in imaging parameters can affect the resulting image.
Generally want 5-7 pixels across beam (err on the side of more rather than fewer)
Image full primary beam (or mosaic).
For more, see the ALMA Primer Video on cell and image size: https://www.youtube.com/watch?v=OC3IWpRRtEQ
Notes: Now gotten to the part of the talk where your decision impacts the data
(1st panel) All this structure is real
-image too small -> alias flux from other regions in the field and placing them in the image. That’s why it looks different from the middle panel

## Slide 42
Sources outside primary beam may contribute to image.
Artifacts from source
outside imaged area
Source now in imaged area and can be cleaned.
Notes: Source outside the FOV causing artifacts -> solution is to make a larger image area to clean source.

## Slide 43
Gridder and deconvolver choices depend on the imaging case.
Generally wide fields (λB ~ D2) and wide fractional bandwidths (>10%) require special treatment e.g.
  Multi-frequency synthesis
  W-project
  AW-project
Sources with extended emission may benefit from multiscale clean.
See Friday talks on widefield and wideband imaging for more detail.
Also see https://casaguides.nrao.edu/index.php?title=VLA_CASA_Imaging-CASA6.5.4
Multiscale
Multiscale
MTMFS
Multiscale
W-project
Multiscale
MTMFS
W-project
Notes: I want to mention that you need to pay attention to your gridder and deconvolution choices – This was covered earlier, but including this slide for completeness
-choices can effect your image and artifacts in your image –leave it at that since this was cover earlier
Taken from: https://casaguides.nrao.edu/index.php?title=VLA_CASA_Imaging-CASA6.5.4

## Slide 44
Improper cleaning can produce poor images.
Clean is an iterative process.
Masks are often used to guide clean in building a model image.
A rule of thumb is to include all “real” astronomical features in the clean mask.
For hogbom clean, you generally want to leave buffer of several beams between the emission and the mask.
  Other deconvolution methods might benefit from a less restrictive (i.e., broader) mask.
Stop cleaning when your residuals look noise like.
  Cleaning too deeply will end up including the noise in your model.
  Cleaning too shallowly will miss real emission
Notes: Imaging talk on Friday. You likely saw this type of imaging window yesterday in the tutorials
-show an example in the following slides on this clean method

## Slide 45
Masking: a Goldilocks (“just right”) approach
Real emission just outside mask!
Initial mask gets most of the emission.
But a mask is needed to avoid picking up sidelobes
Notes: -now lets walk through the different iterations of tclean

## Slide 46
Clean depth: another Goldilocks approach
Major cycle 0
Major cycle 1
Major cycle 2
Major cycle 3
Major cycle 4
Getting close
Stop here
Stop clean when your residuals ~ the noise.
But note that this is a case where you would be able to do better using multi-scale.
To automatically mask emission, use AUTO-MULTITHRESH in tclean (Kepley+ 2020, PASP).
Notes: -probably want to use multiscale in this case as you have extended emission

## Slide 47
Missing emission leads to “bowls” in images.
See Plunkett et al (2023) for more on how to correct this!
Robust=2 VLA D config
VLA+Effelsberg from Beck (1998)
“Bowl”
Preliminary images from the Local Group L-Band Survey (https://www.lglbs.org/).
TP data can help fill in this missing information!
Additional Slides at end showing error recognition in ALMA-TP data
https://iopscience.iop.org/article/10.1088/1538-3873/acb9bd
Notes: Another common imaging artifact is due to missing flux
-preliminary data of M31, you can see the ring – visible bowls of where we are missing emission
Here's the image (its a screenshot of my ds9). Same scale for both. Left is robust=2 VLA D config, and right is VLA+Effelsberg from Beck (1998).

## Slide 48
Imsize & cell size
Algorithm choices
Common sources of issues with interferometric data (not exhaustive) – A Cheat Sheet
Non-ideal
calibrators
Atmosphere
Mis-behaving
antennas
Mis-behaving
correlator
Astronomer
RFI
Time
Frequency
UV distance
Frequency
Time
Real vs. Imaginary
Artifacts in images
Time
Frequency
Artifacts in images
Frequency
Masking & cleaning
Bowls in emission

## Slide 49
Take-aways
Doing great science means understanding the underlying data!
VLA and ALMA weblogs have many useful plots.
Both the visibility data and images are useful for finding errors.
Helpful visibility plots:
  Amplitude/phase vs. time – time dependent problems
  Amplitude/phase vs. frequency – frequency dependent problems
  Amplitude vs. uvdistance – structure in sources
  Real vs. imaginary – bad antennas/baselines
10 deg phase error for one antenna = 20% amplitude error.
Double check your imaging parameters are appropriate, especially: cell, imsize, gridder, and deconvolver.
Questions about your data? Ask your friendly neighborhood helpdesk!
  ALMA: help.almascience.org
  VLA: help.nrao.edu

## Slide 51
Many useful plots are in pipeline weblogs!
ALMA Weblog
TP Weblog
Now focusing on Total Power

## Slide 52
Contamination in OFF positions
Contamination in OFF position can cause issues!
- Extragalactic objects in all bands: an offset of 10 arcminutes from the target in horizontal coordinates. PIs may request a larger offset if necessary. - Galactic objects (Band 3 - 6): a fixed position from the ALMA off-position catalog within 5 degrees of the science target - Galactic objects (Band 7 and 8): a fixed position from the ALMA off-position catalog within 3 degrees of the science target
ON-OFF=(Source emission)
Defining OFF positions

## Slide 53
Good Baseline Fit
A good baseline fit will be flat across the spectral window
Lots of different variations in poor baseline fitting
This could happen when the OFF position is more than 3 degrees
Another example is with broad lines in narrow windows (with little continuum to fit the baseline
One more common example of a poor baseline fit are ripples
Example of a good baseline fit

## Slide 54
Poor Baseline Fits
A good baseline fit will be flat across the spectral window
Lots of different variations in poor baseline fitting
This could happen when the OFF position is more than 3 degrees
Another example is with broad lines in narrow windows (with little continuum to fit the baseline)
One more common example of a poor baseline fit are baseline ripples/resonances

## Slide 55
Poor Baseline Fits
Tend to be towards bright sources
  e.g., planet/solar system objects
200-300 MHz ripple
  Could be standing waves that are amplified by bright signals
More common in broad continuum windows
Currently under investigation
Baseline ripples
https://help.almascience.org/kb/articles/why-is-there-a-spectral-baseline-ripple-in-total-power-observations-of-bright-targets
Knowledgebase article

## Slide 56
TP Continuum
Continuum imaging is not currently supported with the SD pipeline
All TP images (FDM and TDM) are imaged as spectral cubes
TDM windows (i.e., continuum windows) are fine in the spectral set up but the SD pipeline does not image them as continuum, it will image them as data cubes (see example below).
Example of a TDM window
Notes: Implementing single dish receivers (& antennas) that have both excellent spectral line performance and excellent continuum performance is complex and expensive, and priority was placed on spectral line science cases in the design.

## Slide 57
Comparison of a TDM vs FDM window in TP
Example of a FDM window
Example of a TDM window
Notes: Implementing single dish receivers (& antennas) that have both excellent spectral line performance and excellent continuum performance is complex and expensive, and priority was placed on spectral line science cases in the design.

## Slide 58
Bright/Dark spots in TP images
How to spot the bug in the weblog:
Check the 'Max Intensity Map' in the hsd_imaging stage: this can be seen in 'per antenna' maps, one would see strange bright spots only in one (or some) antenna, but not in all images.
Check the 'profile maps' per panel: one would see a couple of more noisy baselines, whose location and affected antenna are consistent with the bright/dark spot seen in 'max intensity map’.
The solid confirmation would be to check the weight maps in the PL working directory.
What triggers this issue in the SDpipeline:
When data is flagged in only one polarization, the weighting of the flagged data is set to 1

## Slide 59
Bright/Dark spots in TP images
How to spot the bug in the weblog:
Check the 'Max Intensity Map' in the hsd_imaging stage: this can be seen in 'per antenna' maps, one would see strange bright spots only in one (or some) antenna, but not in all images.
Check the 'profile maps' per panel: one would see a couple of more noisy baselines, whose location and affected antenna are consistent with the bright/dark spot seen in 'max intensity map’.
The solid confirmation would be to check the weight maps in the PL working directory.
What triggers this issue in the SDpipeline:
When data is flagged in only one polarization, the weighting of the flagged data is set to 1

## Slide 61
Imsize & cell size
Algorithm choices
Common sources of issues with interferometric data (not exhaustive) – A Cheat Sheet
Non-ideal
calibrators
Atmosphere
Mis-behaving
antennas
Mis-behaving
correlator
Astronomer
RFI
Time
Frequency
UV distance
Frequency
Time
Real vs. Imaginary
Artifacts in images
Time
Frequency
Artifacts in images
Frequency
Masking & cleaning
Bowls in emission

## Slide 62
An example from my own research
Is this a possible spectral line?

## Slide 63
An example from my own research
Sure looks like an absorption line when I image it.
But a strong radio recombination absorption line at these frequencies (8GHz) would be weird.

## Slide 64
An example from my own research
Wait, what does the bandpass calibrator look like?
Looks like there’s a bad bandpass solution in these spectral windows.
Subsequent inspection showed this is due to RFI during bandpass calibrator scan.
So not a line, just poor calibration.

## Slide 65
Looking at both visibility data and images can help uncover issues.
FT
Disk
Bessel Function
2D
1D
1D
2D
Notes: [NEED TO ADD SOME F
Recall basic FT relationships [xxxx add in some figures here. Generate myself or get them from Josh Goodeve?
  Point source:
  Two point source: rippling
  Gaussian:
  Disk
IGURES HERE!!!]