## Slide 1
Optical Interferometry using Radio Astronomy Techniques
  New method real-time, non-invasive micron-size source characterization
  New method in sub-nanometer wave-front sensing
Fourier optics, Huygens principle, and Young’s two slits
Carilli (NRAO), Nikolic (Cavendish), Thyagarajan (CSIRO), Torino, Iriso (ALBA)
Copyright © 2024 AUI, U. Cambridge, CELLS, CSIRO. All Rights Reserved

## Slide 2
van Cittert – Zernike Theorem
The cross-multiplication, or coherence, between the electromagnetic voltages measured at spatially distinct locations (’apertures’) = Fourier transform of the intensity distribution
ui,j = (Bi,j / 𝜆) rad-1
FT
Aperture plane (complex)
v
u
Image plane
x
y
Vi,j = Ai,j e-i𝝓i,j
𝛉 = 𝛌/B = 1/u
Orientation and spatial frequency set by geometry of baseline (ui,j)
Brightness determined by amplitude of visibility (Ai,j = coherence)
Position of fringe determined by phase (𝝓i,j)
Image
.

## Slide 3
Coherent amplification of voltages, E
Geometric delays set by electronics
Complex cross multiply and average to visibilities = FT(source structure)
Images made from Fourier transform of visibilities
Radio measurements are visibilities = aperture plane
𝜃
Vi,j = Ei x Ej* = Ai,j e-i𝝓i,j
o

## Slide 4
Optical: aperture mask + focusing optics => image of fringe
𝛉 = 𝛌/B
0
1
Complex visibilities = FT(image)
  Autocorrelation = I0 + I1 = all photons in image
  I01 = photons in u,v sample 0-1
  V01 = visibility or mutual coherence = I01 / (I0 + I1)
Michelson 1891
  V01 = (Smax – Smin)/(Smax + Smin)
Vi,j = Ai,j e-i𝝓i,j = FT(Image)
v = B/𝛌 = 𝛉-1
1-0
v
u

## Slide 5
3 Hole Mask
Auto = I0 + I1+ I2
V01 = I01 / (I0 + I1)
V12 = I12 / (I1 + I2)
V20 = I20 / (I2 + I0)
Auto
u
Challenge 1
Deriving Vij requires knowing I0, I1, I2 separately = ‘Illumination pattern of aperture’
v

## Slide 6
5 Hole Mask
3 Hole Mask
Challenge 2
Phase = Position
Phase fluctuations => Decoherence/blurring
1ms frames
Closure Phase in Image Domain
Shape-Orientation-Size conservation

## Slide 7
𝛅L
Self-Calibration: joint fit complex voltage gains and source structure
Start: measurements, 𝑉mi,j and simple source model, 𝑉si,j
Invert equation to derive complex element-based voltage gains, 𝐺i
Derive new source model from the gain-corrected 𝑉mi,j through model fitting or imaging and deconvolution
Iterate to convergence: more measurements than free parameters ([𝑁(𝑁 − 1)]/2 cross correlations vs. N gains plus source parameters)
Gain amp, ai = aperture plane illumination
Gain phases, 𝛉i ∝ photon path-length delay through system: 𝛅L = 𝛌 × 𝛉i/360o
= Wavefront sensor!
VLA 8 GHz
Self-cal has never been done in optical interferometry!

## Slide 8
Circumference = 270m
Electron energy = 3 GeV
Photons IR to X-ray
  >1010 optical photons/ms
ALBA Synchrotron Light Source Barcelona, Spain

## Slide 9
e- gun
Insertion Ring
Storage Ring
Bending magnet
Undulator or wiggler
Photon Beam lines = experiments
  X-ray crystallography
  X-ray spectroscopy
  X-ray lithography
  Infrared spectroscopy
  Optical interferometry
Key performance metric: Gaussian e- beam size
smaller => better

## Slide 10
Xanadu: ALBA optical synchrotron radiation beam line
Experiments
7 hole mask
2mm diameter holes
Baselines 5mm to 24mm (3.7”)
Wavelength = 400nm
30 frames = 1ms every 1sec
Rotating mirror for WFS tests

## Slide 11
Non-redundant 7 hole Mask: JWST Template
u
v

## Slide 12
Selfcal Gamp stable ~ 1%
Voltage gains differ by up to 30%
1.11
1.23
1.24
1.19
1.19
1.31
1.00
Coherences > 60%
Stable < 1%
Gaussian model self-calibration in CASA
amplitudes = illumination

## Slide 13
Gaussian model fitting
Real-time 2D Electron Beam Shape to ≤ 1% accuracy
Without SC 66 40 5o
7ap 59.0 ± 0.1 23.5 ± 0.3 16 ± 0.2o
Gaussian model fit to coherences

## Slide 14
Wavefront Sensing
Surface of constant phase of EM wave: 𝛅L = 𝛌 × 𝛉i/360o
1-6, 2-5
Vis phase before Self-cal
After Self-cal
rms = 28o = 31nm
rms ~ 1.2o = 1.3nm
Mean = static pathlength differences (’metrology’)
Variations (millisec) = vibrations and turbulence (‘adaptive optics’)
  𝛅𝚽 is correlated between baselines => systematic 𝛅L, not noise
  rms after self-cal much lower => measuring frame 𝛅L to high significance

## Slide 15
Wavefront Sensing
Self-cal gain phase solutions encode path-length delay through system to each hole wrt reference hole: 𝛅L = 𝛌 × 𝛉i/360o
Rotating mirror tests
Wavefront tilts = 0”, 2”, 4”, 6”, 8”
Mean 𝛉i = tilt
Variations 𝛉i
  rms ~ 30o (33 nm)
  correlated between neighboring holes
0
1
2
3
4
5
6
4” tilt
1,2
5,6
3
4

## Slide 16
Mean best fit plane: reproduce WF tilts to ~ 0.1” (5e-7 rad)
4
3

## Slide 17
Non-planar static metrology distortions seen up to 12 nm: repeatable between experiments to rms ~ 2 nm at each hole
Fitting higher order (Zernike) modes: 7-holes insufficient to constrain all but tip-tilt
Static non-planar metrology
Focus test: +/-400um focus change
Path-length pattern inverts
Pattern matches model predictions
Magnitudes difficult to model
+400
-400
0

## Slide 18
Variations adaptive optics: tip-tilt wave-front variations due to vibration
1ms exposures every 1 sec
Tilts up to 0.5”
Random frame-to-frame

## Slide 19
Dynamic range set by phase wraps => 1 wavelength between pairs of elements
  Fitting wavefront (Zernike) across mask could improve by factor few
  Add spectral axis => improve dramatically: eg. measurements separated by 5% in 𝛌 increase dynamic range by factor 20 (‘global fringe fitting’ in VLBI)
Aperture sampling is limited by requirement of non-redundant mask
  Use fibers, lens, micro-mirror array to fully sample aperture and generate series of non-redundant interferograms (w. one common reference hole)
  Use ’over-constrained’ nature of self-cal to limit analysis to non-redundant u,v samples
Noise, Precision, Dynamic Range, Sampling
Measured visibility phase rms after calibration = 1.2o
6 visibilities per gain solution => rms ~ 1.2o/root(6) ~ 0.5o => pathlength precision: 𝛅Lrms ~ 0.6 nm
Photon counting phase noise per visibility ~ 1/root(107) × 360o ~ 0.11o => shot noise limit to pathlength ~ 0.05 nm

## Slide 20
Mean phase = static pathlength differences to nm-precision (’metrology’)
Variations (millisec) = vibrations and turbulence (‘adaptive optics’)
Measure full shape of wavefront = total photon path-length to each aperture element relative to reference position
  Not ‘reference wave interference’ (Fizeau): no need for reference surface or source
  Not ‘1st derivative-based’ (Shack-Hartmann): no need for function fitting to gradient field
  Not generalized Foucault knife-edge (pyramid): no moving parts
  Not ‘phase diversity’ method: no need for out of focus measurements
  Agnostic to source shape: joint fit of source and element gains
Wavefront sensing via interferometric self-calibration
𝛅L = 𝛌 × 𝛉i/360o
‘The wavefront cannot be directly measured, because it is determined by phase,’ Yi et al Nature Comm 2021
US patent 12,104,901
US patent app. No. 18/878,488
US patent app. No. 19/079,876
arXiv:2503.10820
arXiv:2405.12090
arXiv:2409.11135
arXiv:2406.02114
JOSA-A 2024, 41, 1513
2022PASA...39...14T
JOSA-A 2022, 39, 2214