## Slide 1
Interferometric Imaging of the ALBA Synchrotron Light Source
Fourier Optics and Huygens Principle
Carilli (NRAO), Nikolic (Cavendish), ), Thyagarajan (CSIRO)
Torino, Iriso (ALBA)
Copyright © 2024 AUI, U. Cambridge, CELLS, CSIRO. All Rights Reserved

## Slide 2
ALBA Synchrotron Light Source, Barcelona, Spain
Circumference = 270m
Electron energy = 3 GeV
Photon energy up to 70 keV
Emittance = 4.5 nm-rad

## Slide 3
e- gun
Insertion Ring
Storage Ring
Bending magnet
Undulator or wiggler
Photon Beam lines = experiments
Radial acceleration at bending magnets
Doppler beaming
70keV
I𝛎 ∝ 𝛎𝞪

## Slide 4
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC
TEM
Cryo-EM
InCAEM
(in commissioning)
(in commissioning)
(in constr.)
(in constr.)
BL34 – Xanadu
Material Science Research
Life Science Research
Metrology Research
Accelerator Research
ALBA Today
Public Institution
  50% Spanish “Ministerio de Ciencia”
  50% Catalan “Department de Recerca & Universitats”
12 operating beam lines
2500 experiments/year in metrology, material, and life science

## Slide 5
  X-ray crystallography and tomography
  X-ray spectroscopy
  X-ray metrology (Athena)
  X-ray lithography
  Infrared spectroscopy
ALBA Synchrotron Research

## Slide 7
Key Performance Metric: Emittance
Measurement methods
X-ray pinhole camera
LOCO magnetic lattice analysis + beam position monitors
Optical synchrotron radiation interferometry (SRI)
Emittance = e- beam area x momentum vectors
Low emittance => concentrated and focused photon beam => higher brightness
Note: X-ray pinhole => highly Gaussian ~1012 e-

## Slide 8
Van Cittert – Zernike Theorem
ui,j = (Bi,j / 𝜆)
The cross-correlation, or coherence, between the electromagnetic voltages measured at spatially distinct locations (’apertures’) = Fourier transform of the intensity distribution
Image plane
Aperture plane
FT
Vi,j = Ai,j, 𝝓i,j
v
u
x
y
‘dirty image’
‘self-calilbration’

## Slide 9
Coherent amplification of voltages, E
Geometric delays set by electronics
Complex cross multiply and average (correlate) to visibilities
Images made from Fourier transform of visibilities
Note: negative surface brightnesses => unphysical due to lack of total power
Vi,j = Ei x Ej* = Ai,j, 𝝓i,j
Radio measurements are visibilities = aperture plane

## Slide 10
Aperture mask + coherent focus with lens (or mirrors)
Direct imaging of fringe pattern
Visibilities generated from FT(image)
V1,2 (Ai,j, 𝝓i,j) = FT(Image)
Optical measurements are images

## Slide 11
Earth rotation and bandwidth
Nuv = 351 x nt x nch > 105
Sidelobes ~ 0.03
Sidelobes ~ 0.3
Fourier = u,v coverage
PSF
FT
Quality of image depends on number of Fourier components:
Nuv = Nant((Nant-1)/2) = 351

## Slide 12
peak/rms ~ 100
Peak/rms ~ 105
= Wavefront sensor
R. Ekers

## Slide 13
Mask + lens
Magnifier, polarizer, color filter
Fast CCD
Xanadu: ALBA optical synchrotron radiation interferometry lab

## Slide 14
Rotated Two Hole Method: ‘Young’s slit’ w. Gaussian Fitting
Torino & Iriso w. Mitsuhashi method

## Slide 15
Multi-hole, 2D non-redundant mask SRI w. self-calibration
Experiments
Experiments w. 2, 3, 5, 6, 7 hole masks
Hole sizes = 2mm to 5mm
Wavelength = 400nm and 540nm
30 Frames = 0.3ms to 3ms every 1sec
Max baseline = 27mm at 400nm => 3” fringe
Source major axis = 60um at 15m = 0.8” (but ~107 photons/frame => very high S/N)
Processing
Center on Airy disk + bias subtraction
FT to Vij (Ai,j, 𝝓i,j)
Challenges: non-uniform illumination and phase fluctuations due to vibrations
  1. Gaussian fit Vamp w. Gamp self-cal
  2. Hybrid mapping w. Gamp & Gph SC

## Slide 16
Hole size => Airy disk = ‘primary beam’
FT => u,v ‘smearing’
3mm
5mm
0-1
1-2
0-2
u
v

## Slide 17
5 Hole non-redundant mask

## Slide 18
Sidelobes ~ 0.30
Nuv = 21
Non-redundant 7 Aperture Mask u,v coverage and PSF
FT
PSF
Template = JWST aperture mask (stretched)

## Slide 19
Amp
Phase
ALBA 7hole Dirty Image
FT

## Slide 20
Phases: rms ~ 15o
Vibrations and/or turbulence
[Closure phase 0o; rms < 1o ]
Visibilities: 30 exposures, 1ms every 1 sec
Stable visibility amplitudes: rms < 1%
𝛟12
𝛟31
𝛟23
𝛟123
A13
A05
A24
A12

## Slide 21
Phase stability and time averaging
‘Dropouts’
0-2 1ms rms~ 1%
0-2 3ms rms ~ 5%
Dictates short integration times
Necessitates non-redundant mask

## Slide 22
Method 1: Gaussian model fitting to Vis Amp w. Gamp Selfcal
Selfcal Gamp stable ~ 1%
Differ up to 30%
Coherences > 60%
Bmaj ~ 59.6 +/- 0.1 um
Bmin ~ 23.8 +/- 0.5 um
𝜎 = 60um

## Slide 23
Method 1: Gaussian model fitting to Vis Amp w. Gamp Selfcal

## Slide 24
Method 2: Image reconstruction via visibility Amp +Phase self-calibration and PSF deconvolution
DNR ~ 20
DNR ~ 2000
Image Restoration
𝛔maj ~ 0.85” = 60um
PA = 19o
But not quite Gaussian due to poor u,v coverage
Hybrid mapping

## Slide 25
Ap1 0.109, -78o
Ap2 0.121, -20o
Ap3 0.122, 12.6o
Ap4 0.117 -57o
Ap5 0.117 -114o
Ap6 0.129 -80o
Why Self-Calibration?
Hole-based gain solutions
Amp: illumination ~31% voltage difference => ~50% error in source size
Phase = msec timescale wavefront sensor: dL𝜸 = 𝝺 x (d𝞍/360o)
  gradient: tip/tilt
  Jitter: rms ~ 15o = 22nm
Ap0; 0.098, 0o

## Slide 26
Why non-redundant Mask (and not filled aperture)?
Decoherence on redundant baselines due to phase fluctuations across mask
rms for redundant samples ~ 6x non-redundant

## Slide 27
Summary
New SRI method for rapid (msec), accurate, non-invasive 2D beam characterization
Self-calibration corrects for non-uniform illumination
Non-redundancy avoids decoherence and image smearing
Self-cal phase solutions provide precise, rapid wave-front sensor (photon pathlength)
Higher resolution: shorter wavelengths
More holes: generalize to more complex sources
Beam monitor at other facilities: DESY (Germany), SPring8 (Japan)
Improved diagnostics in next-gen instruments (ALBA, Swiss Light Source…) with lower emittance
Future

## Slide 28
Possible Applications
The technique presented can be used for accurate, efficient, and rapid characterization of the size and shape of high-intensity light sources even after light propagation through an optical system that may produce phase and amplitude fluctuations in the electromagnetic radiation. Possible applications include:
Beam characterization in accelerator synchrotron light sources
Source shape of laser-induced plasma EUV light sources used in lithographic microchip manufacturing
Free Electron Laser beam characterization
Laser source characterization for fusion reactors
Gain solutions = precise wavefront sensor for optical systems

## Slide 29
5 Hole Mask
3 Hole Mask
Closure Phase in Image Domain
Shape-Orientation-Size conservation

## Slide 30
arXiv:2405.12176
arXiv:2406.02114
arXiv:2405.12090
2022PASA...39...14T
JOSA-A 2022, 39, 2214