## Slide 1
Tests of Image Domain Closure Phase Measurement using VLA data
3C 286 point source: calibrated vs. uncalibrated
9.4 GHz, 20sec, 20 MHz; 𝝈th/vis = 33 mJy
Triad baselines = 7km to 15km
Vis flux = 4.4 Jy
98% correlated flux on selected baselines => 𝝍cl ∼ 0
Cygnus A complex source: calibrated vs. corrupted
8.0 GHz, 8sec, 8 MHz; 𝝈th/vis = 82 mJy
Triad baselines ∼ 0.8km (equilateral)
Vis flux = 23 to 38 Jy
≤ 22% correlated flux on selected baselines => 𝝍cl ≠ 0
Sebokolodi ea.
Visibility phase (wrt reference point), sets fringe position in the image
Shape-Size-Orientation (SSO) Invariance theorem: for a closed triad, resulting image is a true representation of sky brightness, independent of element-based phase corruption (modulo translation)
Copyright © 2020 AUI/NRAO. All Rights Reserved.

## Slide 2
Three Fringes for 3C 286
Image individual baseline fringes, then sum of 3-fringe pattern on closed triad
Visibility phase error => shift perpendicular to fringe direction, w/o changing orientation or fringe spacing
Point source => 𝝍cl ∼ 0 => three fringes intersect in grid of points
calibrated
uncalibrated
Cal vs. uncal on closed triad: shift of pattern, but no change in structure
Copyright © 2020 AUI/NRAO. All Rights Reserved.

## Slide 3
Measurement consistent with zero, within errors
𝛔th of Vis. phase (= image position) ∼ N/S (in radians)
Image plane closure phase
Calibrated: 1.7 ± 1.3o
Uncalibrated: 2.0 ± 1.3o
Corollary: dominant phase corruption terms for VLA are factorizable into antenna-based corrections (ie. not baseline-based)
Aperture plane closure phase (vis. phases)
Calibrated: 2.6o ± 0.74o
Uncalibrated: 2.0o ± 0.74o
𝜹s’
calibrated
uncalibrated
Copyright © 2020 AUI/NRAO. All Rights Reserved.

## Slide 4
𝜹s’
Cygnus A: complex source
Grid-ish, but not point-like (no 3-fringe intersection) => non-zero 𝝍cl
Calibrated data, then corrupt phase one antenna by 80o
Shift occurs along uncorrupted baseline fringe
Image plane closure phase: 𝜹s’
Calibrated: 113.9o ± 1.5o
Uncalibrated: 112.9o ± 1.5o
Aperture plane closure phase (vis. phases)
Calibrated: 112.7o ± 0.3o
Uncalibrated: 112.7o ± 0.3o
Image plane closure phase: AA3 x AI3
Calibrated: 112.5o ± ??o
Uncalibrated: 113.7o ± ??o
corrupted
calibrated
Shift along uncorrupted fringe
Closure phase as visualized in the image plane!
SSO Invariance Theorem: for closed triad of array elements, image is a true representation of the sky brightness, invariant to antenna-based phase corruption (modulo translation).
Note: theorem will not hold for non-closing triad or for baseline-based phase corrutions.
Copyright © 2020 AUI/NRAO. All Rights Reserved.

## Slide 5
Coherent amplification of voltages, E1,2
Geometric delays set by electronics
Complex cross multiply and average (correlate) directly to aperture plane visibilities
Images made from fourier transform of visibilities w/o ’total power’
Coherence time ~ minutes ~ required calibration time
Coherent reflection by mirrors, beam splitters…
Geometric delays set by physical delay lines or primary mirror mask
Correlation via optics and interfere on focal plane, w. ‘total power’
Visibilities generated from FT(image)
Coherence time ~ tens millisec
E1 x E2*
‘airy disk’ = ‘primary beam’
(E1 + E2 )2 = E12 + E22 + (E1 x E2*)
Radio: direct product are visibilities = aperture plane
Optical: direct product is image plane
Copyright © 2020 AUI/NRAO. All Rights Reserved.

## Slide 6
Phase corruption of one element => change optical path-length to focus
Corresponds to a ‘tilt’ of the triad in aperture plane, leading so a shift of the fringe pattern in the image plane (three points define a plane)
Aperture Masking
X
Y
Z = to image plane
𝛅𝛟 ~ 𝝳𝓵 ~ 𝝳𝜏
Aperture plane
Copyright © 2020 AUI/NRAO. All Rights Reserved.