## Slide 1: Configuration
Chris Carilli, NRAO

## Slide 2: Emerging consensus config: ‘Southwest Array’ (memo 17)
350 miles
550km
Talk
General description
Challenge of tri-scale-array: Sensitivity vs. resolution vs. ‘imaging fidelity’
Options
Reconfiguration: not at loss of 18m antennas
Long baselines: TX to VLBA?
Short baselines: [45m dish + FPA] or [6m array + 18m total power]?
Location: U.S. South West, Mexico
Homogeneous array 214 x 18m, off-axis antennas
50% to core: b < 3km => 1” at 30GHz
80% to mid: b < 30km => 0.1”
100% to long: b < 1000km => 0.003”

## Slide 3
High, dry: Elevation Plains of San Augustin = 2200m
ALMA Test Facility: good 3mm testing conditions
Fast switching phase calibration: Site testing interferometer data over years
  30sec cycle at 3mm => reasonable coherence on longest baselines over most of the year (median rms phase < 40o), except summer day time
  Calibrator density: Typical distance to calibrator of 25mJy at 3mm ~ 2o => adequate to ensure that phase noise due to SNR is not a limiting factor for a 3sec integration
Southwest = Good 3mm site (memos 1 & 2)
<20% coherence loss on longest baselines
3mm rms residual w. 30s calibration cycle
rms residual w. 60s calibration cycle

## Slide 4
30 km
300 km
Science Use Case analysis (170 programs; Memo 18)
80% to 90% science can be done with 18m homogeneous SW array
Shortest spacing = 1.75 x 18m (off-set geometry limit)
Maximum spacing ~ 300km
1.75x18m

## Slide 5
3km
30km
550 km
Tri-Scale Array w. real-world constraints
Power, fiber, roads, access (Greisen & Owen memo in prep)
Monochromatic snapshot UV coverage not brilliant, but bandwidth synthesis with factor 2 to 3 band ratios fills-in holes effectively
Array core on north-edge of extended spiral => lots of sensitivity on long baselines (down-side: subarraying is less attractive)
VLA Y
Roads, Power, Fiber

## Slide 6
Tri-scale array => tri-scale beam
0.01”
0.1” to 0.2”
1” to 2”
NA beam at 30GHz
4 hour
Challenge: adjust uv-weighting (robust), cell size, taper to get ‘reasonable’ beam while maintaining reasonable sensitivity
Beam quality metric is NOT peak sidelobe, but minimizing broad skirts

## Slide 7
First Foray into parameter space: R, TA, Cell (Memo 16)
‘Reasonable beam’: skirts < 10% at R > 4x FWHM (see stress-tests)
Representative, not exhaustive, exploration of parameter space
Strongly science application-dependent => requires detailed simulations on case-by-case basis
Q: lose of sensitivity wrt Natural?
R= -0.2
Taper = 4mas
Cell = 1mas
FWHM = 10mas
R= 0.2
Taper = 25mas
Cell = 6mas
FWHM = 55mas
R= 0.5
Taper = 100mas
Cell = 30mas
FWHM = 240mas
R= 1
Taper = 500mas
Cell = 140mas
FWHM = 1400mas
0.05”
0.2”
1”
5”
0.1

## Slide 8
Off-center core => behavior wrt uv-weighting different relative to ALMA or VLA
ALMA: each config arranged to have ~ 20% changes in resolution and sensitivity going from NA to UN
VLA: exponential distribution => factor two changes in resolution and sensitivity going from NA to UN
ngVLA: roughly factor 2 sensitivity loss at all tapers
Note: conservative estimates. Multi-scale imaging algorithms under development should improve (Golap & Bhatnagar)

## Slide 9
Strength of the Core (memo 12)
ngVLA has ~ 10x number baselines wrt ALMA and VLA D-config resolution arrays
ALMA only rival ngVLA in the most compact config (max B = 150m)

## Slide 10
Stress-test @ 10mas, 25GHz: 1Myr Protoplanetary disk at 140pc
(memo 5, 11)
Inner gap optically thick at 100GHz
ngVLA: Image both gaps + annual motions (‘movies of planet formation’)
Circumplanetary disks: imaging accretion on to planets
Grain size stratification: Image poorly understood transition from dust to planetesimal to planets at 1AU resolution
0.1” = 13AU
ngVLA 100hr 25GHz
res = 10mas ~ 1AU
rms = 90nJy/bm = 1K
Saturn at 13AU
Jupiter at 6AU
Model
Isella Dust Model

## Slide 11
Stress-test @ 150mas, 38GHz: Imaging CO 1-0 in z=2 massive disk galaxy (memo 5, 13)
Resolution = 0.15” => 1kpc
Sensitivity = 12uJy (100 km/s, 10hr) => few 108 Mo at z ~ 2
Distributed gas dynamics: Fisher-Tully at z=2
1” = 7kpc
Narayanan Model
ngVLA, 10hr, 38GHz
z=2, CO1-0

## Slide 12
Parameter | Const. Premium | Ops Premium | Notes
"VLA" of Effective Collecting Area | 11.5% | 10.2% | A "VLA" worth of effective collecting area at 30 GHz. Equiv. to 28 x 18m ngVLA dishes.
Reconfigurability | 11.9% | 10.2% | Reconfigurability up to 30km roughly along existing VLA arms. ~4 configurations. One reconfiguration per year.
1000km Baselines | 4.1% | 0.1% | NOT increasing total collecting area, just reallocation of existing collecting area out to 1000km limit. Added 12 long-baseline stations. Strong dependence on LO and DTS concepts in practice.
Options: Reconfiguration of 30km array
SAC/SWG: Not at the expense of substantial loss of 18m antennas
Notes: Option / cost Delta / Description
Values in $ are in the materials for tomorrow.

## Slide 13
ngVLA integrated into a global scale array: eVLBI, phasing of core are ‘given’
Replace existing VLBA antennas/infrastructure with ngVLA technology, new stations?
Operation: HSA/GMVA (‘campaign-mode’), or dedicated array?
Design and implementation depend on primary science drivers: astrometry vs. imaging vs. time domain…
Long Baseline Options

## Slide 14
Short spacing option: fill-in below 1.75 x 18m
Short baseline array + 18m total power
Mason + Condon memo in prep
Fill in the hole w/o degrading surface brightness sensitivity
Current idea: 16 x 6m antennas, close-packed
Rough cost ~ $35-40M ~ 5 x 18m antennas
Additional costs
  Antenna + Rx design effort
  Software development
  Operations cost and complexity
Large single dish + Focal Plane Arrays
Frayer memo 14
45m plus > 20 element FPA ‘well matched’ to ngVLA core
Rough cost ~ 25 x 18m antennas
Additional costs
  Antenna + Rx design effort
  Software development
  Operations cost and complexity
model
SW array
SW array + 45m
Notes: Dynamic range: 90% cases require DR < 40 dB
0.2 uJy/bm in 10hr => 100% of all driving science cases and ~80% of all science cases submitted.
Note – current system at 30 GHz has
* ~0.25 uJy/bm per 10hr with (x2 imaging weights) => 80 nJy/bm ~100 hr
* ~85 uJy/bm/km/s per 10hr with x2 imaging weight. => 10 uJy/bm ~ 720hr
8 K/ 10 hr @ 30 GHz @ 6.4 mas
  => ~0.33 mK/ 10 hr @ 30GHz @ 1” (w/ x2 weights)
  => ~115 mK per km/s per 10hr @ 30 GHz at 1” (w/ 2x weights)

## Slide 15
Array Simulation Tools: working and improving
Debris disk 1cm, 10mas
CO dynamics z = 4.2
Configurations
  Southwest Configuration (214 x 18m; 1000km)
  Add VLBA (4000km)
  To come: short baseline array
CASA simulator
  Simobserve: generate mock.ms from FITS image cubes
  Add thermal noise
  Explore imaging capabilities (uv weights, subarrays..)
  Explore wide field mosaic
https://science.nrao.edu/futures/ngvla/documents-publications

## Slide 16: Emerging consensus design: ‘Southwest Array’ (memo 17)
350 miles
550km
Science Use Case driven
Includes real-world constraints (G&O)
Performs reasonably under limited stress-testing
On-going efforts
Imaging and UV-weighting parameter space as input to sensitivity calculator
Algorithmic development: multi-scale imaging
VLBI implementation
Short baseline options
Location: U.S. South West, Mexico
Homogeneous array 214 x 18m, off-axis antennas
50% to core: b < 3km => 1” at 30GHz
80% to mid: b < 30km => 0.1”
100% to long: b < 1000km => 0.01”

## Slide 17
www.nrao.edu
science.nrao.edu
public.nrao.edu
The National Radio Astronomy Observatory is a facility of the National Science Foundation operated under cooperative agreement by Associated Universities, Inc.

## Slide 18
Band 1
Band 2
Band 3
Band 5
Band 6
Band 4
30 km
300 km
Notes: How does frequency request look as a function of requested resolution (max baseline)
Conclusion – need both low and high frequency bands across the full angular scales supported by the array.
* Implies outfitting all antennas with full suite of receivers.

## Slide 19: Located in U.S. South West, Mexico
JVLA: Good 3mm site, elev. ~ 2200m
50% in core: b < 3km ~ 1” at 30GHz
80% in mid: b < 30km ~ 0.1”
100% in long: b < 300km ~ 0.01”
Potential Station Locations
350 miles