## Slide 1
A transformative new facility to replace the VLA and VLBA to tackle new Scientific Frontiers into the mid-Century:
Thermal imaging at milli-arcsec scales.
10x the sensitivity of the JVLA/ALMA
10x higher resolution than the JVLA/ALMA
1.2 - 116 GHz Frequency Coverage
244 x 18m + 19 x 6m offset Gregorian Antennas
    Centered at VLA site and concentrated in SW US.
    Fixed antenna locations across North America.
The next-generation Very Large Array (ngVLA)
Notes: Will be the next U.S. Flagship Radio Observatory.

## Slide 2
350 miles

## Slide 3
New Parameter Space for the mid-Century
Complementary suite from meter to submm arrays for the mid-21st century
> 120GHz: ALMA 2030 superb for chemistry, dust, fine structure lines
  1.0 - 116GHz: ngVLA superb for terrestrial planet formation, dense gas history, black holes
  < 15 GHz: SKA superb for pulsars, reionization, HI + continuum imaging
Notes: Snapshot comparison of effective collecting area for dish-arrays expected in the 2030’s.

## Slide 4
FoV at 1.4 GHz (half-power)
ngVLA: 1350 arcmin2
SKA: 2200 arcmin2
DSA2000: 17000 arcmin2
Limitation: source characterization
Polarization: good
Temporal: good
Spectral range: limited
Spatial resolution: limited
Requires ngVLA, SKA, ALMA… for broad band, high resolution follow-up
DSA2000 built for synoptic surveys
Excellent ‘finder scope’ for new cosmic phenomena

## Slide 5
ngvla.nrao.edu
Unveiling the Formation of Solar System Analogues on Terrestrial Scales
Probing the Initial Conditions for Planetary Systems and Life with Astrochemistry
Charting the Assembly, Structure, and Evolution of Galaxies Over Cosmic Time
Using Pulsars in the Galactic Center as Fundamental Tests of Gravity
Understanding the Formation and Evolution of Stellar and Supermassive BH’s in the Era of Multi-Messenger Astronomy
ngVLA Key Science Goals (SAC ngVLA memo #19)

## Slide 6
Gravitational Waves Sources: The multi-wavelength campaign that discovered the EM counter-part to the merging binary ~ 30 Mo black-holes, identified with a galaxy at z = 0.093.
KSG 5: New Windows on the Dynamic Universe
Hallinan ea. 2017
Optical Pan ea. 2017
DSA2000: expects to be targeting 10 to 20 LIGO events per year

## Slide 7
High resolution (mas), broad band radio follow-up was critical to determining the physical model for the source: a smothered, emerging relativistic jet
The radio light curve of GW170817 and VLBA imaging of the emerging relativistic jet from the merging binary black hole system. Right: schematic model for the EM counterpart to GW source: a wide angle jet which is trapped by the explosion debris (Dobie ea. 2018; Mooley ea. 2018).
ngVLA: 10x sensitivity over 1 GHz to 115 GHz, down to 80 uas resolution
v = 4c

## Slide 8
Movies of planet formation to sub-AU scales, 5-10 Earth masses
Detect complex pre-biotic molecules and determine the chemical initial conditions in forming solar systems and individual planets
KSG1,2 Development of Life in Cosmic: imaging formation of Solar-system Analogs and the Chemistry for Life
1Mo proto-star w. 0.1Mo PP disk w. forming Jupiter: Monthly obs. over few years at 100 GHz, 7mas resolution (1 AU at 140pc; L. Ricci)
B. McGuire
5AU
Notes: HD 163296
ALMA observation of HD163296 at 1mm along with a simulated 1 cm ngVLA observations (Ricci et al. 2019) of the innermost 24 au region at 1 au resolution for Jupiter-, Saturn-, and Neptune-like planets.
The distribution of exoplanets and young planets embedded in circumstellar disks: Then ngVLA will discover many hundreds of planets with orbital periods <10 yr.
The ngVLA will measure the orbital motion of planets and related features on monthly timescales:
Simulated 100 GHz ngVLA observations of a newborn planetary system comprising a Jupiter analogue orbiting at 5 AU from a Solar type star.

## Slide 9
M-dwarfs most likely stars to host habitable planets. But, M-dwarfs known to be very active, w. strong mag. fields:
  Strong flares: radio gyro-synchrotron emission => highly enhanced relativistic electron pressure wrt thermal coronal gas
  Exo-aurora (106 x Earth’s): cyclotron maser emission w. B ~ 2000 G
Star-planet magnetospheric interactions => deleterious effect on life: key term in Drake equation
DSA2000: Extreme Exospace Weather and Life
Howard et al. 2022
Left: Radio, X-ray flare on Prox. Centauri (Howard ea. 2022). X-ray flare power comparable to Sun, but radio 100x Solar, timescales secs.
Right: B field geometry giving rise to auroral radio emission from UV Ceti (Bastian ea. 2022)
DSA2000 expects to detect
106 flare stars events
105 stars in non-thermal coronal emission
103 stars in thermal coronal emission

## Slide 10: Stellar Radio Photospheres
ngVLA: can resolve and determine R, TB for > 10000 stars, incl. 500 MS stars of all spectral types: Radio ‘HR diagram’ at 85 GHz
Movies of extreme mass-loss in evolved stars
ngVLA imaging of ‘boiling’ AGB stars atmosphere (Akiyama & Mathews 2021)
  ngVLA @ 46 GHz; 1.5 mas ~ 0.04 stellar radii at d=150pc
  1.3 year pulse period observed every 2-3 weeks
Dominates late time mass loss in evolved stars
𝛼 Orionis M1 1A, 38 GHz
A2 V @ 50pc, 85 GHz Carilli
40mas
0.5mas
Notes: Simulated movies of the gas motions in the radio photosphere of an asymptotic
giant branch (AGB) star as observed with the ngVLA Main Array at 46 GHz. The
angular resolution is ~1.5 mas, corresponding to roughly 0.04 stellar radii.
Each movie covers a single 1.3-year pulsation period for a model AGB star,
assuming observations every 2-3 weeks. The adopted distance was 150 pc.
AGB star atmospheres are highly dynamic owing to a combination of radial
pulsations, shocks, and large-scale convective processes. These stars also shed
large amounts of matter through cool, dense winds. Radio waves are emitted from
a portion of their atmospheres that lie at a radius of roughly twice the
visible photosphere, and just interior to the wind launch region.
The adopted brightness distribution for the radio photosphere model (the
"ground truth model" shown in the left hand frame) was based on a 3D
hydrodynamic model of an AGB star atmosphere from Freytag et al. (2017). The
Freytag et al. model is not specific to millimeter wavelengths, but was adapted
here for illustrative purposes. The second frame shows the ground truth model
blurred with a Gaussian kernel.
The two frames on the right show image reconstructions of the model based
on simulated ngVLA Main Array observations. The integration time was 2
hours per frame and the assumed bandwidth was 10 GHz in dual
polarizations. The second frame from the right shows a multi-scale CLEAN
reconstruction, while the frame on the right shows the result of a
regularized maximum likelihood reconstruction using the SMILI package of
Akiyama et al. (2019). While both methods do well at reproducing many of
the key features of the model, the SMILI version achieves superior angular
resolution.
These results underscore that the exquisite sensitivity and resolution of the
ngVLA will enable studies of the physical properties and kinematics of the
atmospheres of evolved stars in unprecedented detail.
Credit: K. Akiyama and L. D. Matthews, based on models adapted from B.
Freytag.

## Slide 11
KSG3: Molecular gas – Fuel for Star Formation over 13 Gyr
ngVLA observations of SMG at z = 4.4; SFR ≈ 400 M⨀ /yr
Total molecular gas content largely missed by high-J lines
𝜃 ≈ 0.3”
𝜃 ≈ 0.3”
𝜃 ≈ 0.5”
The ngVLA will routinely detect molecular gas in “normal” galaxies at z=6 via low-J CO transitions
The ngVLA will provide >10x improvement in our knowledge of the cold molecular gas = fuel for star formation, back to cosmic reionization
Casey
Notes: 50 Mpc box cosmological hydrodynamic simulation of galaxy evolution

## Slide 12
4.5e6 HI detections to z ~ 1
Unresolved HI at high redshift (z ~ 0.2-1) N ~ 6.0e5
Resolved HI at low redshift (z < 0.2) N ~ 3.9e6
DSA2000: 𝛒HI over the epoch of ‘Cosmic Demise’
Shutting down of late-time accretion and cessation of star formation in the Universe?

## Slide 13
Project Timeline
2018
2021
2029
2035
Science Book
Astro2020 Report
NSF development funds
Prototype antenna at VLA Site
Construction
Early Science Operations (> VLA capabilities)
Full Science Operations
NSF/MREFC FDR
2023
2026
2019
Astro2020 submission
Construction full cost accounting: $2.3B [FY2018]

## Slide 14
First few years of DSA2000 operation: follow-up will still rely on VLA, VLBA, SKA, ALMA…
After 2028: ngVLA early science capabilities (>= VLA)
After 2034: ngVLA full science capabilities (10x VLA…)
DSA2000
SKAMid
ngVLA
Scaled Sensitivity
Full Operations
?

## Slide 15
Astro2020
ngVLA: high-priority large, ground-based facility; construction start this decade
DSA2000: high priority ‘midscale++’ for time domain/multi-messenger
DSA2000
Notes: ngVLA essentially checked off every box of Astro2020 scientific priorities.

## Slide 17
DSA2000
Notes: Snapshot comparison of effective collecting area for dish-arrays expected in the 2030’s.

## Slide 18
Terrestrial zone planet formation @ 140pc
DSA2000
Notes: Snapshot comparison of effective collecting area for dish-arrays expected in the 2030’s.