## Slide 1
Geometry of Closure Phase and
Image-plane Self-Calibration
I acknowledge the Traditional Owners of the land, sea and waters, of the area that we live and work on across Australia. I acknowledge their continuing connection to their culture and pay my respects to their Elders past and present.
Nithyanandan Thyagarajan (CSIRO)
Chris Carilli (NRAO)
Bojan Nikolic (U. Cambridge)

## Slide 2
Interferometric Fringes & Image Synthesis
Image Synthesis
Measurement
(Van Citterte-Zernike relation)
Fringe
Measured in Radio
Not measured in Optical
Synthesized in Radio
Intrinsic in Optical
Correlation in Radio
Inverse FT in Optical
Inverse Fourier
Series Summation
Image Credit: NRAO
Image Credit: C. Carilli

## Slide 3: Calibration: Standard approach
Frequent observations of reference radio sources of “known” structure, strength, and position
Determine element gains
Spatial and temporal interpolation
Apply to target visibilities

## Slide 4: Closure Phase
Provenance
Monnier+(2006)
Bispectrum: Vmabc = VmabVmbcVmca

## Slide 5: Discovery of Detailed Structures of Radio Galaxies: Double-lobed structure of Cygnus A
Jennison (1957)
Jennison (1959)
Jennison & Latham (1959)
First determination of core-jet morphology of quasar 3C147
First direct evidence of superluminal expansion (~10c) of relativistic jet in quasar 3C273
…
M87, Sgr A* black hole morphologies by EHT
Image Credit: C. Carilli

## Slide 6: Hybrid Mapping (Before self-calibration)
Wilkinson+(1977)
Pearson+(1981)
First determination of core-jet morphology of quasar 3C147
First direct evidence of superluminal expansion (~10c) of relativistic jet in quasar 3C273
Readhead+(1980)
N-1 unknown antenna phases
=> (N-1)(N-2)/2 closure phases
N unknown antenna amplitudes
=> N(N-3)/2 closure amplitudes
Iteratively estimate visibility phases
Not antenna phases

## Slide 7: Self-calibration
N antenna complex gains from N(N-1)/2 complex visibilities => powerful constraints
Works very well for large N
Antenna-based => inherently preserves closure quantities (not explicitly estimated)
Cornwell (1989)

## Slide 8: Image plane view of Closure Phase
Closure phase is independent of antenna-based gain corruptions*
Aperture-plane view straightforward
Image-plane view??
*Caveats apply: Baseline-dependent, direction-dependent and polarization leakage terms
can violate this relationship

## Slide 9
Geometry of Interferometric Fringes
Null Phase Curve (NPC):
Phase-position relation:
𝜹s12
𝜹s23
𝜹s31
Fringe Spacing
Δ Phase = 2π
Fringe Slope = -u/v
Fringe NPC (straight line): Fringe Phase = 0
NPC slope = -u/v (Fixed for a given baseline vector)
NPC offset encodes visibility phase and corruptions
Any phase corruption results in parallel displacement of fringe NPC
Visibility phase = (2π / fringe spacing) x perpendicular offset of NPC from phase center
Thyagarajan & Carilli, 2022, PASA, 39, 14

## Slide 10
3-element Interference Pattern: Antenna vs. Baseline errors
Thyagarajan & Carilli, 2022, PASA, 39, 14
JVLA 9 GHz, A-array
Point source => 𝝍3∼ 0 => three fringes intersect in grid of points
Shift of pattern but no change in the grid structure
Measured closure phase consistent with 0 using both image-plane methods as well as the well-known aperture-plane method
3C 286

## Slide 11
3-element Interference Pattern: Effect of Antenna Gain Errors
Thyagarajan & Carilli, 2022, PASA, 39, 14
Cygnus A
JVLA 8 GHz D-array
Extended structure
𝝍3 = 113o ± 1.5o from both image-plane methods and consistent with the aperture-plane method
Translation occurs along uncorrupted baseline fringe
SOS conservation verified
Shift along uncorrupted fringe

## Slide 12
Closure Phase in 3-element Interference
Thyagarajan & Carilli, 2022, PASA, 39, 14
Closure phase = Sum of three perpediculars from phase centre
Closure phase = triangle height normalized by fringe spacing
x
=

## Slide 13
Closure Phase Conservation
Ideal
Mis-calibrated
Translated
Shape, size, orientation (SOS) of fringe triangle preserved
Closure phase invariant to (mis-)calibration/translation
Triangle Shape-Orientation-Size (SOS) Conservation
Thyagarajan & Carilli, 2022, PASA, 39, 14

## Slide 14
Phase corruption of one element => change optical path-length to focus
Three points define a plane
Corresponds to a ‘tilt’ of the triad in aperture plane, leading so a shift of the fringe pattern in the image plane
Thyagarajan & Carilli, 2022, PASA, 39, 14
Every 3-element interference pattern (triangle) is a “good” observable (except for an arbitrary shift)
The shifts are different for each antenna triad
A Basis for Image-Plane Self-Calibration

## Slide 15
Closure Phase in the Image Plane
Shape-Orientation-Size Conservation
Image Plane Self Calibration
Chris Carilli, Nithya Thyagarajan, Bojan Nikolic
'A geometric view of closure phase in interferometry’, NT, CC 2022, PASA, 39, 14 [Shape-Orientation-Size Conservation]
’Image Plane Self-Calibration,’ CC, BN, NT 2022, JOSA-A, 39, 2214
Copyright © 2020 AUI/NRAO. All Rights Reserved.

## Slide 16
Coherent amplification of voltages, E1,2
Geometric delays set by electronics
Complex cross multiply and average (correlate) voltages to aperture plane visibilities
Images made from Fourier transform of visibilities (w/o ’total power’)
Coherent reflection by mirrors
Geometric delays set by physical delay lines or primary mirror mask
Correlation via optics and interfere on focal plane (w. ‘total power’)
Visibilities generated from FT(image) (but why bother?)
E1 x E2*
‘airy disk’ = ‘primary beam’
(E1 + E2 )2 = E12 + E22 + (E1 x E2*)
Radio: direct product is visibility (aperture plane)
Optical: direct product is an image
Copyright © 2020 AUI/NRAO. All Rights Reserved.

## Slide 17
SOS and Aperture Masking
Copyright © 2020 AUI/NRAO. All Rights Reserved.
2 apertures
3 apertures
Three points define a plane
Delay corruption of one element => change optical path-length to focus
Leads to ‘tilt’ of triad in aperture plane => shift of image plane: for 3 elements, no other corruption/decoherence is possible
Image plane basis for closure phase, eg. closure phase is shift invariant
If phase errors are element-based => all images made with 3 element interferometer are true images of the sky, modulo unknown shifts
‘piston delay’

## Slide 18
Triads 3, 4, … Ntriads
80o phase errors, no self-calibration
80o phase errors, after IPSC shifts.
+
+
+
+
Triads 3, 4, … Ntriads
=
=
80o errors, no self-calibration
80o errors plus self-calibration
Model: star/planet = 100/1
SOS Conservation => Image Plane Self-Calibration
Interferometer generates 3-element images = true images, but unknown relative shifts due to element-based delay errors
Cross correlate each triad image with model image to derive shifts
Sum shifted images => coherent image of source with full array

## Slide 19
Tests of IPSC
ALMA configuration, removing closest antennas (14 antennas)
Model: Bright point plus faint companion (100/1)
SIMOBSERVE and add antenna phase errors random over +/-10o
Make all 364 triad images (= ‘starting point’)
Spatial cross correlation w. model image, starting with point source
Iterate
Star = 1 Jy, planet = 10 mJy, no errors
10o errors, no Selfcal

## Slide 20
Aperture plane self-cal w. point-source model
Planet = 9.9 mJy
Rms = 0.09 mJy
Ghost = 0.20 mJy
Image plane self-cal w. point-source model
Planet = 6.3 mJy
Rms = 0.25 mJy
Ghost = 2.6 mJy
Image plane self-cal w. iteration
Planet = 9.0 mJy
Rms = 0.20 mJy
Ghost = 0.6 mJy

## Slide 21
1000/1, 10o, IPSC w. point source
Planet = 0.71 mJy
Rms = 0.15 mJy
Ghost = 0.025 mJy
10/1, 10o, IPSC w. point source
Planet = 65 mJy
Rms = 2 mJy
Ghost = 21 mJy
100/1 and 80o
Planet = 65 mJy
Rms = 2 mJy
Ghost = 21 mJy

## Slide 22
Image Plane Self-Calibration: an application of SOS conservation
IPSC converges, but APSC converges better (for large N)
  Lower rms
  Weaker ghost natural consequence of symmetrization in marginally constrained self-cal
Over-constraints = Nvis/(Nant - 1) = (Nant(Nant - 1)/2) / (Nant - 1) = Nant / 2
  APSC (14 ant) = 7
  IPSC (triad-based = 3 ant) = 3/2
IPSC will not work for
  1 fringe images: ‘baseline based calibration’ => turn source into model (under constrained)
  4+ apertures: no longer obey SOS
  Non-closing (Baseline-based) errors

## Slide 23
Large Interferometer for Exoplanets
When might SOS and/or IPSC be useful?
Basic measurements in image plane
Small N
Amplitude and baseline-based errors small
All typical in laboratory and optical astronomical interferometry
Astro Examples: small N arrays w. image plane detection
VLTI: 4x8.2m + 4 x 1.8m (only 4 at time)
LIFE: space near-IR 4 x 3m elements
VLTI

## Slide 24
Non-Astro examples
Synchrotron light source e– beam shape characterization: 3-slit mask gives 2D beam shape robust to ‘piston errors’ due to atmosphere and device jitter
Inertial fusion reactor laser profiling, Seismology, Ultrasonic imaging, Radar, X-ray crystallography…
VLTI
Spring-8 synchrotron light source (Masaki & Takano 2003)
ALBA synchrotron light source: fit Gaussian models to 2-slit fringe; rotate (Torino & Iriso 2018)

## Slide 25
Typical optical (and laboratory) imaging interferometers
2-element beam combination (pair-wise, or non-redundant beam combination) => fringe images on CCD
FT(fringe images) => visibilities: reconstruct images from amplitudes and closure phases
Direct imaging interferometers (Fizeau, homothetic)
All-to-one beam combination where pattern of apertures is preserved in scaled pupil => direct image creation on CCD
Requires active phasing system (adaptive optics for piston delays)
IPSC: hypothetical device
Generate 3-element images w. directing imaging beam combination
Self-calibrate using image cross correlation and sum
No need for adaptive optics
N=4 array requires 3 beam splits per element and 4 CCDS
Lardiere ea 2007

## Slide 26: Growing list of applications
Dust shells around stars
Optical Interferometry
Monnier+2007
EHT image of M87 SMBH, VLBI, EHT+2019
X-ray crystallography
21cm cosmology, Thyagarajan+2020
Invariance to element-based gain corruptions => very valuable in applications where calibration/phase determination is challenging
Seismic imaging/ Geophysics,
Schuster+2014

## Slide 27
Wilkinson+(1977)
Pearson+(1981)
First determination of core-jet morphology of quasar 3C147
First direct evidence of superluminal expansion (~10c) of relativistic jet in quasar 3C273
Image credit:
EHT collaboration
First as second scale imaging of event horizon of M87 black hole
First polarized imaging of magnetic structures inferring the presence of jet launch near the event horizon
BH parameters verifying GR
Scientific Motivation: VLBI Calibration Challenges

## Slide 28: Closure Phase generalized to N-polygons
“Phase-position” and “product of areas” relations extended to closed N-polygons
Thyagarajan & Carilli, 2022, PASA, 39, 14

## Slide 29: Connection to Crystallography
X-ray/electron/neutron Crystallography
Radiation scatters as it passes through crystal
Diffraction pattern (reciprocal space) is FT of electron density distribution (real space)
Need Fourier inversion to determine electron density distribution and atomic/molecular structure
But usually, only intensities of diffraction pattern available  |FH|2, and phases of FH are lost (called the “phase problem”)
Direct Fourier inversion not possible
Use structure invariants -- triplet and quartet phases (or closure phases)* -- to determine phases with a priori knowledge of symmetries and structures using forward-modeling
The geometric picture of closure phase is easily extended to 3D crystal structure analysis
* Nobel prize in chemistry awarded to Herbert Hauptman & Jerome Karle in 1985 "for their outstanding achievements in the development of direct methods for the determination of crystal structures” which relied heavily on the use of structure invariants
Diffraction
pattern
Electron
Density

## Slide 30: Connection to Seismic Imaging
Local velocity anomalies due to surface topography called “statics”
Statics affect time-delay measurements
Statics (seismic imaging)  Phase errors (radio interferometry)
Combining delays (phases) around a closed network of sources and receivers eliminate these statics
Source statics
Receiver statics
See Schuster+ 2014 for review
Thyagarajan & Carilli, 2020, arXiv 2012.05254

## Slide 31: Connection to Interferometric Synthetic Aperture Radar (InSAR) and Medical Imaging
Repeat-track interferometry (Same orbit)
InSAR great for studying topography and surface changes
Repeat-track interferometry provides stack of co-registered phase coherent E-field images
Phase difference interferogram could be phase-corrupted
Closure phase images between three different times (if non-zero) robustly measures structural changes
Coregistered phase-coherent images
(holographic images with phase information)
t1-t2
time
Closure phase image from three times
Mt. Etna (above)
but could be medical images!
t2-t3
t3-t1

## Slide 32: Connection to TDI in GW detection using LISA
Time Delay Interferometry (TDI) in GW  Time-dependent closure phase
LISA will detect GW from Galactic WD binaries at mHz frequencies
Three spacecrafts with arm lengths ~5 million km
Short wavelengths => Time dependence of spacecraft motion and Laser phases important
Laser phase noise is overwhelming source of noise (by >7 orders of magnitude)
Unequal and changing arm lengths need to be accounted for
Solution: Time Delay Interferometry (TDI)
TDI = linear combinations of time-delayed phases of laser beams on closed loops between spacecrafts
They cancel spacecraft motion effects and intrinsic phase noise
Critical for successful GW detection
Vallisneri (2005)

## Slide 33: Connection: Quantum Mechanics & Polarized Light
Phase of N-vertex Bargmann invariants
Bargmann invariants are gauge-invariant to any local phase factors affecting the quantum states
Closely resemble closure phase definition and properties
Phases of Bargmann invariants = Geometric phase = Berry phase = Pancharatnam Phase
On a cyclical path through multiple polarized states on the Poincare sphere, the geometric phase = (1/2) solid angle subtended by the path = change in vector angle during parallel transport
Related to the intrinsic curvature