## Slide 1
Thermal imaging on milliarcsecond scales at ~ 1cm
Effective area at 40GHz ~ 10x JVLA, ALMA
Resolution ~ 10x JVLA, ALMA
Frequency range: 1 – 50, 70 – 115 GHz
Science requirements to telescope specifications

## Slide 2
Science requirements: Community process to date (24 months!)
Jan 2015, Jan 2016: AAS community science meetings
April 2015, Dec 2015: Technology meetings (Pasadena, Socorro)
Dec 2015, Aug 2016: Kavli-sponsored RMS meetings (Chicago, Baltimore)
Nov 2015: Science working group science program reports (125 authors, 200 pages) http://library.nrao.edu/ngvla.shtml + arXiv
  Circle of Life (Isella, Moullet, Hull)
  Galaxy ecosystems (Murphy, Leroy)
  Galaxy assembly (Lacy, Casey, Hodge)
  Time domain, Cosmology, Physics (Bower, Demorest)
Reports conclude with itemized/prioritized list of key science programs
  Distill science reqs to telescope specs in ‘engineering-friendly’ format
  Iterate with SWGs (Feb-May)
Early times: Design and Science are ‘under construction’ – need your help!

## Slide 3
Next step: Sci. Requirements to Tel. Specifications
Goal | Science Requirement | Array Specification
Terrestrial zone | Optically thin | Freq ~ 15 to 50GHz
planet formation | 1AU at 130pc @ 30GHz | B ~ 300km
 | 1K in 10hrs @ 10mas, 30GHz | Afull ~ 300 x 18m; BW ~ 20GHz
Dense gas history | CO 1-0 to z=8 | Freq = 15 to 115GHz
of the Universe | Mgas = 109 Mo at z = 3 in 1hr | Amid ~ 70% to B ~ 30km
 | 500pc resolution at z = 3 (60mas) | 30km
 | Large volume surveys | Octave Band Ratio
Baryon cycle | TB < 0.2K (1hr, 10 km/s, 80GHz, 1”) | Acore ~ 30% to B ~ 2km
 | Continuum science | Octave BR; Linear pol to 0.1%
Time domain | Explosive follow-up (GRBs, GW/EM…) | Minute trigger response time
 | Blind discoveries (eg. FRBs) | millisec searches
 | Exo-space weather: 1uJy in 1min | Freq ~ 1 to 20GHz Afull ~ 300 x 18m Circular pol to few %

## Slide 4
Image terrestrial zone planet formation
AU-scale imaging 1Myr protoplanetary disk at 140pc distance
Frequency: need low optical depth on AU-scales => 30GHz
Resolution: need 1AU resolution at 130pc = distance to nearest star forming regions (eg. Taurus, Ophiucus) => 10mas
Sensitivity: need 1K brightness at full resolution => 10x VLA, ALMA
0.1” = 13AU
ngVLA 100hr 25GHz 10mas
rms = 90nJy/bm = 1K
Jupiter at 13AU Saturn at 6AU
model
Isella Dust Model

## Slide 5
ng-Synergy: Terrestrial zone exoplanets
Full Evolutionary sequence, from birth to maturity
ngVLA
Imaging formation of terrestrial planets
Pre-biotic chemistry
High Definition Space Telescope Terrestrial planets = top science goal
Direct detection of earth-like planets
Search for atmospheric bio-signatures

## Slide 6
Dense gas history of Universe
Imaging ’fuel for star formation’ during epoch of galaxy assembly
Frequency: need low order CO at z ~ 1 to 5 => 20 to 50GHz
Resolution: need ~ 1kpc => 0.15”
Sensitivity: need to reach few 108 Mo at z ~ 2 => 12uJy @ 100 km/s
FoV, BW: 100x JVLA, ALMA spectral deep field survey speed (1000’s vs 10’s of galaxies) => 18m antenna, 20GHz BW
1” = 7kpc
Narayanan Model
ngVLA
z=2, CO1-0

## Slide 7
ng-Synergies: Dense Gas History of the Universe
‘Missing half of galaxy formation’
SFR
Gas
ALMA
NGVLA
JWST, TMT
Decarli

## Slide 8
Science requirements spreadsheets
Built from SWG report summaries
Currently ~ 30 programs, med, high priority

## Slide 9
Science requirements to Telescope Specifications Spread Sheets
Engineering Friendly Format: spec, goal, design compliance

## Slide 10
Goal: PDR-level ‘proposal’ to 2020 Decade Survey for major D+D program
  Compelling science program
  Defensibly costed design of all major elements
Cost Model
Science Requirements
Telescope Specs
Closed loop for tradeoffs: science to telescope to cost

## Slide 11
‘Living Document’: need your help!
Broaden science program: what are we missing?
Areas to explore with testing and simulation
  Configuration and antenna
    Balance: Core (3km) vs. mid (30km) vs. long (300km) [some fraction reconfigurable?]
    FoV: 12m to 25m
    Need for total power (large single dish + camera)
    Full req range
  Phase Calibration: WVR, Cal. Array, Fast Switching
  VLBI implementation
Deep Dives
  Simulation tools are all tested and available (CASA and AIPS) to explore configuration and imaging sensitivity
  Goal: stimulate research publications by the community!

## Slide 12
Complementary suite from meter to submm, appropriate for the mid-21st century
< 3mm: ALMA 2030 superb for chemistry, dust, fine structure lines
3cm to 3mm: ngVLA superb for terrestrial planet formation, dense gas history of Universe, baryon cycle
> 3cm: SKA superb for pulsars, reionization, HI surveys
Radio facilities @ 2030
2030

## Slide 13
Thermal imaging on milliarcsecond scales at ~ 1cm
Effective area at 40GHz ~ 10x JVLA, ALMA
Resolution ~ 10x JVLA, ALMA
Frequency range: 1 – 50, 70 – 115 GHz
https://science.nrao.edu/futures/ngvla