## Slide 1
Optical Masking Interferometry using Radio Astronomy Techniques
Fourier Imaging, Deconvolution, and Self-calibration
C. Carilli (NRAO), B. Nikolic (Cavendish), L. Torino (CELLS/ALBA), U. Iriso (CELLS/ALBA), N. Thyagarajan (CSIRO)
Copyright © 2024 AUI, U. Cambridge, CELLS/ALBA, CSIRO. All Rights Reserved
Measuring the size and shape of extremely bright, micron-scale light sources: synchrotrons, free-electron lasers, plasma light source lithography…
Nano-meter wavefront sensing: metrology and manufacturing, ophthalmology, directed energy…
Fourier optics, Huygens principle, and Young’s two slits
US patent 12,104,901
US patent app. No. 18/878,488
US patent app. No. 19/079,876

## Slide 2
Light Source
Planar wavefront
v = B/𝛌
1-0
𝛉 = 𝛌/B
FT
u
v
rad
Aperture Mask Interferometry
Ai,j =
= Ai,j e-i𝝓i,j
Orientation and spatial frequency set by geometry of baseline
Position of fringe determined by phase
Strength determined by ‘mutual coherence’
FT

## Slide 3
Light Source
Self-Calibration
Propagation effects distort/attenuate wavefront
Solution: Joint fit complex voltage gains and source structure
Over-constrained: [𝑁(𝑁 − 1)]/2 Vis vs. Ngains + Msrc
Gain amp, ai = aperture plane illumination
Gain phases, 𝛉i ∝ photon path-length through system
𝛅L = 𝛌 x 𝛉i/360o = wavefront sensing
Generate new model (fitting / deconvolution)
Source Model Visibilities
Solve element gains
Correct visibilities
Measured Visibilities
VLA 8 GHz

## Slide 4
Circumference = 270m
Electron energy = 3 GeV
Synchrotron photons IR to X-ray
109 optical photons/millisec
ALBA Synchrotron Light Source, Barcelona, Spain

## Slide 5
e- gun
Insertion Ring
Storage Ring
Bending magnet
Undulator or wiggler
Photon Beam lines = experiments
Radial acceleration at bending magnets
Doppler beaming
Key performance metric: Gaussian e- beam size
smaller => better
X-ray crystallography
X-ray spectroscopy
X-ray metrology
X-ray lithography
Infrared spectroscopy
Optical interferometry
60um x 24 um
Xray pinhole

## Slide 6
Xanadu: ALBA optical synchrotron radiation interferometry lab
Experiments
2 to 7 hole masks
1mm diameter holes
Baselines 5mm to 24mm (3.5”)
Wavelength = 400nm
30 frames: 0.3ms every 1sec

## Slide 7
Non-redundant 7 hole Mask: JWST Template
u
v

## Slide 8
Selfcal Gamp stable ~ 1%
Voltage gains differ by up to 30%
1.11
1.23
1.24
1.19
1.19
1.31
1.00
Coherences > 60%
Stable < 1%
Gaussian model self-calibration in CASA
Amplitudes = illumination

## Slide 9
Real-time 2D Electron Beam Shape to 1% accuracy
Without SC 66 40 5o
mín = 11um
Vary beam coupling
Min size measured at ALBA = 11um
Hyper-resolution at very high S/N
  11um at 15m = 0.7mrad = 0.15”
  Min Fringe spacing = 3.5”

## Slide 10
Core-Halo problem: Imaging Double-Gaussian Beams
Critical issue for LHC and future HL-LHC: power going into ‘halo’?
Measure ’halo’ reliably down to ~1% bunch ratio
2D SRI currently being tested at LHC, and incorporated in HL-LHC design
X-ray pinhole Images
A
B
C
ALBA: Create double Gaussian beams using bunch-by-bunch system
Fit double Gaussian to 7-hole interferograms

## Slide 11
Selfcal Gain phase = nm-precision measure of photon pathlength
Mean = static pathlength difference (’metrology’)
Variations (millisec) = vibrations and turbulence (‘adaptive optics’)
Wavefront Sensing: measure surface of constant phase of EM wave
𝛅L = 𝛌 x 𝛉i/360o
0o
-140o
15o = 17nm
-15o
50o = 56nm
-125o = 138nm
𝛉vis
𝛉gain

## Slide 12
Tilting mirror tests
Reproduce WF tilts to ~ 0.1” (5e-7 rad)
Tests: 0”, 2”, 4”, 6”, 8” wavefront tilts around Y axis (= X tilt)
Accuracy ~ small fraction of wavelength 𝝺 (nm precision per millisec exposure)
Non-planar static metrology distortions seen up to 12 nm
Repeatable to rms ~ 2 nm at each hole
𝛅L
𝛅L

## Slide 13
Application on JWST 7-hole AMI system
Dusty Binary Star WR137 at 4.8um and 3.8um ~ 0.1” resolution
Self-calibration + CLEAN Deconvolution
Visibility time series
High S/N
Very stable (rms ~ 1%, 1o)
Gain solution time series
High S/N
Very stable (rms ~ 0.1%, 0.6o)
3%
FT

## Slide 14
Gain phase solutions => Mirror segment pistons to < 27nm
Similar to those derived with AMIGO forward-modeling (Desdoigts ea. 2025)
Selfcal
Standard closure phase modeling
Self-cal + CLEAN
Lau ea 2024
Reproduce structure to 300mas
Dynamic range source ~ 240
Dynamic range calibrator star ~ 1000
4.8um
3.8um
Application on JWST 7-hole AMI system
Dusty Binary Star WR137 at 4.8um and 3.8um ~ 0.1” resolution
Self-calibration + CLEAN Deconvolution

## Slide 15
Why RA Self-Cal not used in Optical Interferometry?
Paucity of photons: few source photons per coherence time
Employ model fitting to Closure phases + Vis Amplitudes
Closure phase is robust to element-based gain phases => allows for averaging of many low S/N measurements w/o loss of coherence
Our Laboratory Optical Interferometry
High S/N: millions of photons/vis/msec
Employ Vis phases and amplitudes + Selfcal per coherence time + deconvolution/model fitting
Advantages:
  More constraints: [N(N-1)/2] vs [N(N-1)/2 – (N-1)]
  Closure phase = measure source symmetry; Vis phase more general
  Employ myriad Vis-based deconvolution techniques
  Correct illumination and path-length = nm-precision wavefront sensing
JWST AMI: selfcal + deconvolution in optical astronomical interferometry
High Strehl ratio
Long Coherence time
Large collecting area
  => High S/N per coherence time allows for use of visibilities + selfcal
Possible in future ground based optical astronomical interferometry?
What’s new?

## Slide 16
arXiv:2510.13502
arXiv:2503.10820
arXiv:2405.12090
arXiv:2409.11135
arXiv:2406.02114
JOSA-A 2025, 42, 1261
JOSA-A 2024, 41, 1513
2022PASA...39...14T
JOSA-A 2022, 39, 2214
Real-time, non-invasive measurement of micron scale sources to < 1% accuracy
Wavefront sensing: nm precision on msec timescales
JWST AMI = first astronomical application
Source characterization using optical masking interferometry with radio astronomical techniques

## Slide 17
5 Hole Mask
3 Hole Mask
Closure Phase in Image Domain
Shape-Orientation-Size conservation

## Slide 18
Problems with JWST AMI
Under-sampling PSF by large pixels
Charge migration =? PSF smearing
Near-field optics of mask in reimaged aperture plane
=> large baseline-based errors that DO NOT obey closure and ARE NOT fixed by self-cal
Visibilities amplitudes should all = 1
Closure phases should all = 0
Closure amplitudes should all = 1

## Slide 19
No distortion
Focus
Astigmatism
30nm
-3nm
1nm
-30nm
Fitting higher order distortions: SRI modeling with Zernike Polynomials and 7 hole mask
Fit
Input

## Slide 20
Why non-redundant mask?
Decoherence on redundant baselines due to phase fluctuations across mask
Coherence for redundant samples lower by 5%
rms for redundant samples ~ 6x non-redundant

## Slide 21
Coherent amplification of voltages, E
Geometric delays set by electronics
Complex cross multiply and average to visibilities
Images made from Fourier transform of visibilities
Vi,j = Ei x Ej* = Ai,j e-i𝝓i,j
Radio measurements are visibilities = aperture plane