## Slide 1
Optical Interferometric Imaging of the ALBA Synchrotron Light Source using Astronomical Techniques
Fourier optics, Huygens principle, and Young’s two slits
Carilli (NRAO), Nikolic (Cavendish), Thyagarajan (CSIRO)
Torino, Iriso (ALBA)
Copyright © 2024 AUI, U. Cambridge, CELLS, CSIRO. All Rights Reserved

## Slide 2
Circumference = 270m
Electron energy = 3 GeV
Photon energy up to 70 keV
Emittance = 4.5 nm-rad
ALBA Synchrotron Light Source, Barcelona, Spain

## Slide 3
e- gun
Insertion Ring
Storage Ring
Bending magnet
Undulator or wiggler
Photon Beam lines = experiments
Radial acceleration at bending magnets
Doppler beaming
70keV
I𝛎 ∝ 𝛎𝞪

## Slide 4
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC
TEM
Cryo-EM
InCAEM
(in commissioning)
(in commissioning)
(in constr.)
(in constr.)
BL34 – Xanadu
Material Science Research
Life Science Research
Metrology Research
Accelerator Research
ALBA Today
Public Institution
  50% Spanish “Ministerio de Ciencia”
  50% Catalan “Department de Recerca & Universitats”
12 operating photon beam lines
2500 experiments/year in metrology, material, and life science

## Slide 5
  X-ray crystallography and tomography
  X-ray spectroscopy
  X-ray metrology (Athena)
  X-ray lithography
  Infrared spectroscopy
ALBA Synchrotron Research

## Slide 7
Key Performance Metric: Emittance
Measurement methods
X-ray pinhole camera
LOCO magnetic lattice analysis + beam position monitors
Optical synchrotron radiation interferometry (SRI)
Emittance = e- beam area x momentum vectors
Low emittance => concentrated and focused photon beam => higher brightness
‘quality of experiments depends on the knowledge of the e- beam shape’
X-ray pinhole => highly Gaussian ~1012 e-
e-

## Slide 8
Van Cittert – Zernike Theorem
The cross-multiplication, or coherence, between the electromagnetic voltages measured at spatially distinct locations (’apertures’) = Fourier transform of the intensity distribution
‘dirty image’ => deconvolution
‘self-calilbration’ = Wave Front Sensing
ui,j = (Bi,j / 𝜆)
Image plane
Aperture plane
FT
Vi,j = Ai,j, 𝝓i,j
v
u
x
y
Voltage gains

## Slide 9
Coherent amplification of voltages, E
Geometric delays set by electronics
Complex cross multiply and average to visibilities
Images made from Fourier transform of visibilities
Note: negative surface brightnesses => unphysical due to lack of total power
Vi,j = Ei x Ej* = Ai,j, 𝝓i,j
Radio measurements are visibilities = aperture plane

## Slide 10
Aperture mask + coherent focus with lens (or mirrors)
Direct imaging of fringe pattern
Visibilities generated from FT(image)
V1,2 (Ai,j, 𝝓i,j) = FT(Image)
Optical measurements are images

## Slide 11
Mask + lens
Magnifier, polarizer, color filter
Fast CCD
Xanadu: ALBA optical synchrotron radiation interferometry lab
𝛌 = 540nm

## Slide 12
Example 7 hole non-redundant mask

## Slide 13
Rotated Two Hole Method: ‘Young’s slit’ plus Gaussian Model
Torino & Iriso w. Mitsuhashi method
=
Limitations
Slow: cannot be done in real time
Relatively low S/N

## Slide 14
New method: Multi-hole, 2-Dimensional masking SRI
Astronomical innovations
Non-redundant mask
Self-calibration
Processing
Center on Airy disk + bias subtraction
FT image to Vij (Ai,j, 𝝓i,j)
Ai,j, 𝝓i,j = complex sum over area of u,v sample = #photons
𝛾12 =
Challenge: Auto = non-uniform illumination => requires self-cal
Joint fitting toVij obtain Gaussian source parameters and hole gains
Auto
v
u

## Slide 15
Hole size => Airy disk = ‘primary beam’
FT => u,v ‘smearing’ by primary beam
3mm
5mm
0-1
1-2
0-2
u
v

## Slide 16
Multi-hole, 2D non-redundant mask SRI w. self-calibration
Experiments
Experiments w. 2, 3, 5, 6, 7 hole masks
Hole sizes = 2mm to 5mm
Baselines to 24mm
Wavelength = 400nm and 540nm
30 frames = 0.3ms to 3ms every 1sec
Tests: real-time adjustment of beam size
5 hole non-redundant mask

## Slide 17
Non-redundant 7 hole Mask: JWST Template

## Slide 18
𝛟12
𝛟31
𝛟23
𝛟123
Phases: rms 1ms ~ 15o
Vibrations and/or turbulence
Closure phase 0o; rms < 1o
  aperture based errors
  point-symmetric source
0-2 1ms
rms~ 1%
0-2 3ms
rms ~ 5%,
<amp> lower by up to 5%
Why short tframe?

## Slide 19
Why non-redundant mask?
Decoherence on redundant baselines due to phase fluctuations across mask
Coherence for redundant samples lower by 5%
rms for redundant samples ~ 6x non-redundant

## Slide 20
Why Self-Calibration?
Ap1 0.109
Ap2 0.121
Ap3 0.122
Ap4 0.117
Ap5 0.117
Ap6 0.129
Ap0 0.098
Hole-based gain solutions
Amp: illumination ~25% voltage difference
=> ~50% power difference

## Slide 21
Why not a filled aperture?
Phase screen => image blurring = ‘seeing’ (filled aperture has infinite # of redundant baselines)
Diffraction limit => 𝛉source < PSF => requires deconvolution (model fitting)
  PSF of filled aperture is complex (diffraction edges, shutters… Not just airy disk)
  PSF of interferometer is (almost) mathematically deterministic (sinusoids)
7”
ALBA
e- beam FWHM = 141x56um @15m
  FWHMmaj = 1.9”
  FWHMmin = 0.8”
Lens/shutter PSF FWHM ~ 6” w. complex 20% diffraction wings
Mask longest baseline = 24mm => fringe spacing at 540nm ~ 5”,
but PSF is known precisely and S/N is very high (107 photons per vis) => facilitates model fitting

## Slide 22
Selfcal Gamp stable ~ 1%
Differ up to 30%
Coherences > 60%
Self-cal Method 1 w. 5 Hole data
Gaussian model fitting to Vis Amp w. Gamp Selfcal

## Slide 23
Method 1: Gaussian model fitting to Vis Amp w. Gamp Selfcal
Bmaj ~ 59.6 +/- 0.1 um
Bmin ~ 23.8 +/- 0.5 um
𝜎 = 60um
Coherences are high but so is S/N => can fit for model much smaller than PSF
Errors = rms of time series/root(30)
Minor axis is worse due to resolution

## Slide 24
Method 1: Gaussian model fitting to Vis Amp w. Gamp Selfcal
Without SC 66 40 5o

## Slide 25
Tests w. 7 hole mask: Changing e- beam size

## Slide 26
Method 2: Image model reconstruction via CASA complex gain calibration
7-hole mask w. 4 rotation angles
Start w. point source and GAINCAL for each rotation
Gaussian UVMODELFIT to all SC data
Use new Gaussian model in GAINCAL
Iterate
PSF
71%
PSF
30%

## Slide 27
Method 2: Image model reconstruction via CASA complex gain calibration
Converges quickly
Axes within ~ few um; PA within 1o of Method 1
Gain amplitudes within 1% of Method 1

## Slide 28
CLEAN deconvolution of 7-hole SC data (0o rotation)
FWHM CLEAN PSF 540nm = 4.6” x 2.8”
FWHM CLEAN PSF 400nm = 3.4” x 2.1”
Source FWHMmaj ~ 1.9”; FWHMmin ~ 0.8”
540nm not Gaussian due to poor u,v coverage and resolution
400nm does better on Bmaj but Bmin still ‘unresolved’
400nm
540nm
Model*PSF
400nm
540nm

## Slide 29
Summary
New SRI method for rapid (msec), accurate, non-invasive 2D e- beam characterization
Self-calibration corrects for non-uniform illumination
Non-redundancy avoids decoherence and image smearing
Self-cal phase solutions provide precise wave-front sensor
More experiments at ALBA
  generalize to more holes and more complex sources
  EUV: higher resolution
SRI beam monitor at DESY (Germany), SPring8 (Japan)
Improved diagnostics in next-gen synchrotron sources with lower emittance (Brookhaven NSLS-II, Argonne APS, ALBA-2, Swiss LS)
Free Electron and/or Fusion reactor laser beam characterization
EUV source shape of laser-induced plasma light sources used in lithographic microchip manufacturing (ASML)
Future

## Slide 30
arXiv:2405.12090
arXiv:2409.11135
arXiv:2406.02114
JOSA-A 2024, 41, 1513
2022PASA...39...14T
JOSA-A 2022, 39, 2214
US patent 12,104,901
US Provisional patents: RL 8127.306USPR, RL 8127.035.GBPR

## Slide 31
5 Hole Mask
3 Hole Mask
Closure Phase in Image Domain
Shape-Orientation-Size conservation

## Slide 32
0o
-41o
73o
179o
134o
Wave Front Sensor
Phase = millisec timescale wavefront sensor
  High accuracy: dL𝜸 = 𝝺 x (d𝞍/360o)
  Gradient: tip/tilt
  Jitter: rms ~ 15o = 22nm