## Slide 1
Optical Interferometry using Radio Astronomy Techniques
  New method real-time, non-invasive micron-size source characterization
  New method in wave-front sensing
Fourier optics, Huygens principle, and Young’s two slits
Carilli (NRAO), Nikolic (Cavendish), Thyagarajan (CSIRO), Torino, Iriso (ALBA)
Copyright © 2024 AUI, U. Cambridge, CELLS, CSIRO. All Rights Reserved

## Slide 2
Van Cittert – Zernike Theorem
The cross-multiplication, or coherence, between the electromagnetic voltages measured at spatially distinct locations (’apertures’) = Fourier transform of the intensity distribution
ui,j = (Bi,j / 𝜆)
FT
Aperture plane (complex)
v
u
Image plane
x
y
Vi,j = Ai,j e-i𝝓i,j
𝛉 = 𝛌/B = 1/u
Orientation and spatial frequency set by geometry of baseline
Strength determined by amplitude of visibility
Position of fringe determined by phase
Image

## Slide 3
Coherent amplification of voltages, E
Geometric delays set by electronics
Complex cross multiply and average to visibilities
Images made from Fourier transform of visibilities
Vi,j = Ei x Ej* = Ai,j e-i𝝓i,j
Radio measurements are visibilities = aperture plane

## Slide 4
Complex visibilities generated from FT(image)
  Autocorrelation = I0 + I1 = sum photons in image
  I01 = sum photons in u,v sample 0-1
  V01 = visibility or coherence = I01 / (I0 + I1)
Michelson 1891
  V01 = (Smax – Smin)/(Smax + Smin)
V1,2 (Ai,j, 𝝓i,j) = FT(Image)
Optical: aperture mask + focusing optics => image of fringe
𝛉 = 𝛌/B
v = B/𝛌
1-0
0
1

## Slide 5
3 Hole Mask
Auto = I0 + I1+ I2
V01 = I01 / (I0 + I1)
V12 = I12 / (I1 + I2)
V20 = I20 / (I2 + I0)
Auto
v
u
Challenge: to derive Vij need to know I0, I1, I2 separately

## Slide 6
5 Hole Mask
3 Hole Mask
Phase fluctuations: Decoherence
Closure Phase in Image Domain
Shape-Orientation-Size conservation

## Slide 7
Self-Calibration: Joint fit complex voltage gains and source structure
𝛅L = 𝛌 x 𝛉i/360o
(1)
Start with measurements, 𝑉mi,j and simple source model, 𝑉si,j
Invert equation (1) to derive complex element-based voltage gains, 𝐺i
Derive new source model from the gain-corrected 𝑉mi,j through model fitting or imaging and deconvolution
Iterate to convergence: more measurements than free parameters ([𝑁(𝑁 − 1)]/2 cross correlations vs. N gains plus source parameters)
VLA 8 GHz
Gain amp, ai = aperture plane illumination
Gain phases, 𝛉i ∝ photon path-length delay through system = 𝛅L: wavefront sensing!
Self-cal has never been done in optical interferometry!
Schwab 1981; Cornwell & Wilkinson 1981; Readhead & Wilkinson 1978

## Slide 8
Circumference = 270m
Electron energy = 3 GeV
Photons IR to X-ray
1010 optical photons/millisec
ALBA Synchrotron Light Source, Barcelona, Spain

## Slide 9
e- gun
Insertion Ring
Storage Ring
Bending magnet
Undulator or wiggler
Photon Beam lines = experiments
  X-ray crystallography
  X-ray spectroscopy
  X-ray metrology
  X-ray lithography
  Infrared spectroscopy
  Optical interferometry
Key performance metric: Gaussian e- beam size
smaller => better

## Slide 10
Xanadu: ALBA optical synchrotron radiation interferometry lab
Experiments
7 hole mask
2mm diameter holes
Baselines 5mm to 24mm (3.7”)
Wavelength = 400nm
30 frames = 0.3ms every 1sec

## Slide 11
Rotated Two Hole Method: ‘Young’s slit’ plus Gaussian Model
Torino & Iriso w. Mitsuhashi method
Limitations
Slow: cannot be done in real time
Modest accuracy (~ 6%)

## Slide 12
Non-redundant 7 hole Mask: JWST Template
u
v

## Slide 13
Selfcal Gamp stable ~ 1%
Voltage gains differ by up to 30%
1.11
1.23
1.24
1.19
1.19
1.31
1.00
Coherences > 60%
Stable < 1%
Gaussian model self-calibration in CASA: amplitudes = illumination

## Slide 14
Real-time 2D Electron Beam Shape to 1% accuracy
Without SC 66 40 5o
7ap 59.0±0.1. 23.5±0.3 16±0.2o
Gaussian model fit to coherences

## Slide 15
real-time adaptive optics to correct optical distortions (eg. laser communications, directed energy systems…)
metrology in ultra-precise (nanometer) manufacturing
medical ophthalmology (eg. guided LASIK)
Wavefront sensor used in ophthalmology
Wavefront Sensing: measure surface of constant phase of EM wave
Gradient-based (Shack-Hartmann 1904)
Generalize Foucault knife-edge (1858; ‘pyramid’)
Reference Beam (Fizeau 1851)

## Slide 16
1-6, 2-5
Before Self-cal
After Self-cal
rms = 28o = 31nm
rms ~ 1.2o = 1.3nm
[𝛔N𝛄 ~ 0.1% ~ 0.4nm]
Visibility Phases and Wavefront Sensing
Mean = static pathlength differences (’metrology’)
Variations (millisec) = vibrations and turbulence (‘adaptive optics’)
  𝛅𝚽 is correlated between baselines => systematic 𝛅L, not noise
  rms after self-cal much lower => measuring frame 𝛅L to high significance
= 𝛌 x 𝛉i/360o

## Slide 17
0
1
2
3
4
5
6
Gain Phase Solutions encode 𝛅L = 𝛌 x 𝛉i/360o
Rotating mirror tests
4” tilt
Tests: 0”, 2”, 4”, 6”, 8” wavefront tilts around Y axis (= X tilt)
Mean 𝛉i = (mostly) tilt
Variations: rms ~ 30o (33 nm); correlated between neighboring holes

## Slide 18
Best fit plane: reproduce WF tilts to ~ 0.1”

## Slide 19
Non-planar static metrology distortions seen up to 12 nm: repeatable between experiments to rms ~ 2 nm at each hole
Static non-planar metrology
Fitting higher order (Zernike) modes: 7-holes insufficient to constrain all but tip-tilt
Need better sampling of aperture plane (more holes)

## Slide 20
Adaptive optics: tip-tilt wave-front variations due to vibration
0.3ms exposures every 1 sec
Tilts up to 0.5”
Random frame-to-frame

## Slide 21
Mean phase = static pathlength differences to nm-precision (’metrology’)
Variations (millisec) = vibrations and turbulence (‘adaptive optics’)
Measure full shape of wavefront = total photon path-length difference to each aperture element relative to reference position
  Not ‘reference wave interference’ (Fizeau)
  Not ‘gradient-based’ (Shack-Hartmann)
  Not generalized Foucault knife-edge (pyramid)
Wavefront sensing via interferometric self-calibration
‘The wavefront cannot be directly measured, because it is determined by phase,’ Yi et al Nature Comm 2021
Dynamic range set by phase wraps => 1 wavelength between pairs of elements
  Fitting wavefront (Zernike) across mask could improve by factor few
  Add spectral axis => improve dramatically: eg. measurements separated by 5% in 𝛌 increase dynamic range by factor 20 (‘global fringe fitting’ in VLBI)
Aperture sampling is limited by requirement of non-redundant mask
  Use fibers or micro-mirror array to fully sample aperture and generate series of non-redundant interferograms
  Use ’over-constrained’ nature of self-cal to limit analysis to non-redundant u,v samples

## Slide 22
arXiv:2503.10820
arXiv:2405.12090
arXiv:2409.11135
arXiv:2406.02114
JOSA-A 2024, 41, 1513
2022PASA...39...14T
JOSA-A 2022, 39, 2214
US patent 12,104,901
US patent app. No. 18/878,488
US patent app. No. 19/079,876
Real-time, non-invasive measurement of micron scale sources to ~ 1% accuracy
Wavefront sensing: full WF shape with nm precision on msec timescales
Source characterization using optical masking interferometry with radio astronomical techniques

## Slide 23
Hole size => Airy disk = ‘primary beam’
FT => u,v ‘smearing’ by primary beam
3mm
5mm
0-1
1-2
0-2
u
v

## Slide 24
Why non-redundant mask?
Decoherence on redundant baselines due to phase fluctuations across mask
Coherence for redundant samples lower by 5%
rms for redundant samples ~ 6x non-redundant