## Slide 1
National Radio Astronomy Observatory
Jansky Very Large Array
Atacama Large Millimeter Array
Very Long Baseline Array

## Slide 2
ALMA 250GHz (Brogan ea.)
130AU = 1”
D ~ 12Glyr
42uas = 0.01 Lyr = 5.6 Rs
M87 EHT 230 GHz @ 20uas resolution
MSMBH = 6.5 x 109 Mo
Science: the Sun to the Big Bang

## Slide 3
244 x 18m
10x capabilities
1.2 - 116 GHz
The next-generation Very Large Array

## Slide 4
Optical Interferometry using Radio Astronomy Techniques
A new method for 𝛍m-size source characterization and wave-front sensing
Fourier optics, Huygens principle, and Young’s two slits
Carilli (NRAO), Nikolic (Cavendish), Thyagarajan (CSIRO), Torino, Iriso (ALBA)
Copyright © 2024 AUI, U. Cambridge, CELLS, CSIRO. All Rights Reserved
US patent 12,104,901
US patent app. No. 18/878,488
US patent app. No. 19/079,876

## Slide 5
Van Cittert – Zernike Theorem
The cross-multiplication, or coherence, between the electromagnetic voltages measured at spatially distinct locations (’apertures’) = Fourier transform of the intensity distribution
‘dirty image’ => deconvolution
‘self-calilbration’ = Wave Front Sensing
ui,j = (Bi,j / 𝜆)
FT
Aperture plane (complex)
v
u
Image plane
x
y
Voltage element gains
Vi,j = Ai,j e-i𝝓i,j
𝛉 = 𝛌/B = 1/u

## Slide 6
Coherent amplification of voltages, E
Geometric delays set by electronics
Complex cross multiply and average to visibilities
Images made from Fourier transform of visibilities
Vi,j = Ei x Ej* = Ai,j e-i𝝓i,j
Radio measurements are visibilities = aperture plane

## Slide 7
Aperture mask + focus with lens (or mirrors)
Direct imaging of fringe pattern
Complex visibilities generated from FT(image)
V1,2 (Ai,j, 𝝓i,j) = FT(Image)
Optical measurements are images
v = B/𝛌
𝛉 = 𝛌/B

## Slide 8
Earth rotation and bandwidth
Nuv = 351 x nt x nch > 105
Sidelobes ~ 0.03
Sidelobes ~ 0.3
Fourier = u,v coverage
PSF
FT
Quality of image depends on number of Fourier components:
Nuv = Nant((Nant-1)/2) = 351

## Slide 9
DNR ~ peak/rms ~ 100
Correct for element Gi
DNR ~ 105
= Wavefront sensor

## Slide 10
Self-Calibration: Joint fit of complex voltage gains and source structure
𝛅L
(1)
Start with measurements, 𝑉mi,j and simple source model, 𝑉si,j
Invert equation (1) to derive complex element-based voltage gains, 𝐺i, using an optimization criterion
Derive new source model from the gain-corrected 𝑉mi,j through model fitting or imaging (Fourier inversion) and deconvolution
Iterate: typically converges since there are more measurements than fitted parameters ([𝑁(𝑁 − 1)]/2 cross correlations vs. N gains plus source parameters)

## Slide 11
Gain amplitudes (ai) = aperture plane illumination
Gain phases (𝛉i) = photon path-length delay through system (wrt reference element) = wavefront sensor!
Self-Calibration: Wave-front Sensing
𝛅L = 𝛌 x 𝛉i/360o
𝛅L
(1)
VLA 8 GHz
‘The wavefront cannot be directly measured, because it is determined by phase,’ Yi et al 2021

## Slide 12
Circumference = 270m
Electron energy = 3 GeV
Photons IR to X-ray
ALBA Synchrotron Light Source, Barcelona, Spain

## Slide 13
e- gun
Insertion Ring
Storage Ring
Bending magnet
Undulator or wiggler
Photon Beam lines = experiments
  X-ray crystallography and tomography
  X-ray spectroscopy
  X-ray metrology
  X-ray lithography
  Infrared spectroscopy
  Optical interferometry
Performance set by Gaussian e- beam size
smaller => better

## Slide 14
Mask + lens
Magnifier, polarizer, color filter
Fast CCD
Xanadu: ALBA optical synchrotron radiation interferometry lab
Filter, polarizer, reimaging optics, CCD
Optical table
Lens
Mask

## Slide 15
Example 7 hole non-redundant mask
Experiments
7 hole mask (JWST design)
Hole diameter = 2mm
Baselines 5mm to 24mm (3.7”)
Wavelength = 400nm
107 photons/millisec
30 frames = 0.3ms every 1sec

## Slide 16
Non-redundant 7 hole Mask: JWST Template

## Slide 17
Selfcal Gamp stable ~ 1%
Voltage gains differ by up to 30%
=> Power differs > 50%
1.11
1.23
1.24
1.19
1.19
1.31
1.00
Coherences > 60%
Stable < 1%
Self-calibration Amplitudes = Illumination

## Slide 18
Electron Beam Size from Self-calibration
Without SC 280 12 15o
Maj = 59±0.1um
Min = 23±0.3um
PA = 16±0.2o

## Slide 19
1-6, 2-5
Before Self-cal
After Self-cal
rms = 28o = 31nm
rms ~ 1.2o = 1.3nm
[𝛔N𝛄 ~ 0.1% ~ 0.4nm]
Visibility Phases and Wavefront Sensing
Mean = static pathlength differences (’metrology’)
Variations (millisec) = vibrations and turbulence (‘adaptive optics’)
  𝛅𝚽 is correlated between baselines => systematic 𝛅L, not noise
  rms after self-cal much lower => measuring frame 𝛅L to high significance
= 𝛌 x 𝛉i/360o

## Slide 20
0
1
2
3
4
5
6
1,2,3
4,5,6
Gain Phase Solutions encode 𝛅L
    Mean 𝛉i can be large (+/-180o)
    Variations: rms ~ 20o (6nm); correlated between neighboring holes
𝛅L = 𝛌 x 𝛉i/360o
0 nm
-220 nm
28 nm
-167 nm
Subtract mean 𝛉i: frame residual ~ gradient

## Slide 21
Tip-tilt wave-front distortion due to vibration
Tilts up to +/-50 nm across mask (~1”); random frame-to-frame
rms deviation from plane ~ 4 nm = higher order WF corrugations + noise
Need more holes for fitting higher orders

## Slide 22
Measure total photon path-length difference for each element relative to reference position in aperture plane: not ‘reference wave interference’ (Fizeau) nor ‘angle-based’ (Shack-Hartmann) method
𝛅L = 𝛌 x 𝛉i/360o
Mean phase = static pathlength differences (’metrology’)
Variations (millisec) = vibrations and turbulence (‘adaptive optics’)
Precision: small fraction of wavelength
  rms per vis after cal ~ 1.3nm. 7 hole mask => 6 vis per Gi => 𝛅Lrms ~ 0.6nm per frame
  Precision for metrology average 30 frames => 0.1nm
Dynamic range set by phase wraps => 1 wavelength between pairs of elements
  Fitting wavefront (Zernike) across mask could improve by factor few (similar to S-H)
  Add spectral axis => improve dramatically: eg. measurements separated by 5% in 𝛌 increase dynamic range by factor 20 (‘global fringe fitting’ in VLBI = phase slope w. freq)
Aperture sampling is limited by requirement of non-redundant mask
  Use fibers or micro-mirror array to fully sample aperture and generate series of non-redundant interferograms
  Use ’over-constrained’ nature of self-cal to limit analysis to non-redundant u,v samples
Wavefront sensing via interferometric self-calibration

## Slide 23
arXiv:2503.10820
arXiv:2405.12090
arXiv:2409.11135
arXiv:2406.02114
JOSA-A 2024, 41, 1513
2022PASA...39...14T
JOSA-A 2022, 39, 2214
US patent 12,104,901
US patent app. No. 18/878,488
US patent app. No. 19/079,876
Are there similar methods in the field?
What are the current frontiers in WFS?
How might this technique fit-in?
Wavefront sensing via interferometric self-calibration

## Slide 24
Estimate precision via simulations
Insert horizontal tilt and ‘step’ functions to real data
Run self-cal: recover distortions with 𝛉i to < 1o

## Slide 25
Why not a filled aperture?
Phase screen => image blurring = ‘seeing’ (filled aperture has infinite # of redundant baselines)
Diffraction limit => 𝛉source < PSF => requires deconvolution (model fitting)
  PSF of filled aperture is complex (diffraction edges, shutters… Not just airy disk)
  PSF of interferometer is (almost) mathematically deterministic (sinusoids)
7”
ALBA
e- beam FWHM = 141x56um @15m
  FWHMmaj = 1.9”
  FWHMmin = 0.8”
Lens/shutter PSF FWHM ~ 6” w. complex 20% diffraction wings
Mask longest baseline = 24mm => fringe spacing at 540nm ~ 5”,
but PSF is known precisely and S/N is very high (107 photons per vis) => facilitates model fitting

## Slide 26
Why non-redundant mask?
Decoherence on redundant baselines due to phase fluctuations across mask
Coherence for redundant samples lower by 5%
rms for redundant samples ~ 6x non-redundant