## Slide 1: Radio Interferometry - Imaging
Urvashi Rau
National Radio Astronomy Observatory, Socorro, NM, USA
Notes: 1

## Slide 2: Imaging – Part 1
(1) Concepts
– Image Formation
– Measurement Process
– Data Analysis
(2) Build your own interferometer
(3) Imaging in practice
– Basic Imaging
– Imaging and Deconvolution
– How to use reconstruction algorithms
– Wideband, Wide-field and Mosaic imaging
Notes: 2

## Slide 3: An interferometer is an indirect imaging device
2D Fourier transform :
Image = sum of cosine 'fringes'.
b
Young’s double slit experiment
Each antenna-pair measures the
parameters of one 'fringe'.
Measured Fringe Parameters :
Amplitude, Phase
Orientation, Wavelength
Notes: 3

## Slide 4: Measurements
x
Measure the spatial correlation of the E-field incident at each pair of antennas
Notes: 4

## Slide 5: Measurements
x
Measure the spatial correlation of the E-field incident at each pair of antennas
Parameters of a Fringe :
Amplitude, Phase :
is a complex number.
Orientation, Wavelength :
(geometry)
Notes: 5

## Slide 6: Measurements
Measure the spatial correlation of the E-field incident at each pair of antennas
UV plane : Spatial Frequency Domain
Combine measurements from multiple ‘baselines’ (antenna pairs) on a UV grid.
Take the inverse Fourier Transform to construct an image.
Notes: 6

## Slide 7: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 2 antennas
Notes: 7

## Slide 8: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 5 antennas
Notes: 8

## Slide 9: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 11 antennas
Notes: 9

## Slide 10: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 27 antennas
Notes: 10

## Slide 11: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 27 antennas
over 2 hours
'Earth Rotation Synthesis'
Notes: 11

## Slide 12: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 27 antennas
over 4 hours
'Earth Rotation Synthesis'
Notes: 12

## Slide 13: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 27 antennas
over 4 hours, 2 freqs
'Multi-Frequency Synthesis'
Notes: 13

## Slide 14: Spatial Frequency (uv) coverage + Observed Image
Image of the sky
using 27 antennas
over 4 hours, 3 freqs
'Multi-Frequency Synthesis'
Notes: 14

## Slide 15: Image formed by an interferometer : Convolution Equation
You have measured the
Convolution of the True Sky
with the instrumental PSF.
Recovering True Sky
=
DE-convolution
PSF = Point Spread Function
The inverse
Fourier transform
of the
UV-coverage
The PSF is
--- the impulse-response of the instrument
( image of a point-source )
--- the intensity of the diffraction pattern
through an array of 'slits' ( dishes )
--- a measure of the imaging-properties
of the instrument
Notes: 15

## Slide 16: Image Formation
Multi-stage process. Linear. There are weblogs showing human readable information to use for diagnostics (numerical as well as procedural failures). QA system. Ability to 'restore' to any state for optimized re-processing. Standarized calibrated data and output image products for the archive.
: The 2D Fourier Transform (FT) of the sky brightness, measured at a spatial
frequency given by the geometry of the baseline (antenna pair) ij.
Imaging : Collect all samples onto a 2D spatial frequency grid, and do an iFT.
X
FT
iFT
True Sky
Brightness
True
Visibility
Function
Sampled
Visibility Function
is placed on
the grid at a location
given by geometry
of the ij baseline
Observed Image
Sampling Function
( UV coverage )
N antennas = N(N-1)/2 samples (for each timestep and channel)
Image Reconstruction
Notes: 16

## Slide 17: Data Analysis
But, the measured values are imperfect and incomplete
Notes: 17

## Slide 18: Data Analysis
But, the measured values are imperfect and incomplete
Flagging
Problem : Radio Frequency Interference (RFI)
Solution : Identify and discard corrupted data samples.
Notes: 18

## Slide 19: Data Analysis
But, the measured values are imperfect and incomplete
Flagging
Calibration
Problem : Radio Frequency Interference (RFI)
Solution : Identify and discard corrupted data samples.
Problem : Antenna electronics introduce complex gains
Solution : Numerically solve for antenna gains and apply corrections
- Observe a source where is known
- Use information from all ij to solve for
- Divide out from target data
Notes: 19

## Slide 20: Data Analysis
But, the measured values are imperfect and incomplete
Flagging
Calibration
Imaging
Problem : Radio Frequency Interference (RFI)
Solution : Identify and discard corrupted data samples.
Problem : Sampling of the 2D Fourier Transform is incomplete
( only N(N-1)/2 measurements per timestep and frequency channel )
Solution : Fit a model of the sky brightness to the measured data.
Problem : Antenna electronics introduce complex gains
Solution : Numerically solve for antenna gains and apply corrections
Notes: 20

## Slide 21: Data Analysis - Pipelines
Online flags
Auto-flag Cal
Tsys flag
Calculate Tsys
WVR correction
Flag low gains
Set Cal Model
Import data
from Archive
Bandpass Cal
Flag outliers
Flux Cal
Flag outliers
Time Cal
Apply solutions
Ant Pos Corr
Image Calibrator
Check size
Export Data/Images
To Archive
Flagging
Calibration
Imaging
Split target data
Continuum Sub
Image Continuum
Image Spectral
Quality Assurance
Export Images
to Archive
Observe
Data
Quality Assurance
Autoflag target
Web-Logs of results, diagnostic plots, QA metrics
Notes: 21

## Slide 22: Build Your Own Interferometer !
Multi-stage process. Linear. There are weblogs showing human readable information to use for diagnostics (numerical as well as procedural failures). QA system. Ability to 'restore' to any state for optimized re-processing. Standarized calibrated data and output image products for the archive.
Notes: 22

## Slide 23: Build Your Own Interferometer !
Multi-stage process. Linear. There are weblogs showing human readable information to use for diagnostics (numerical as well as procedural failures). QA system. Ability to 'restore' to any state for optimized re-processing. Standarized calibrated data and output image products for the archive.
( https://github.com/urvashirau/ImagingSimulator )
Notes: 23

## Slide 24: Build Your Own Interferometer !
Multi-stage process. Linear. There are weblogs showing human readable information to use for diagnostics (numerical as well as procedural failures). QA system. Ability to 'restore' to any state for optimized re-processing. Standarized calibrated data and output image products for the archive.
How does the antenna
layout and count affect
– UV-coverage
– Point Spread Function
Change relative orientation
of the array and the object
- Projection effects
Point sources versus
extended emission
- Spatial scales
- Point Spread Function
Effect of aperture Synthesis
Change time-ranges
Change bandwidth
Different weighting schemes
What features can be
emphasized ?
Effect of a compact versus
spread-out configuration
– Angular resolution
Notes: 24

## Slide 25: Imaging – Part 2
(1) Concepts
– Image Formation
– Measurement Process
– Data Analysis
(2) Build your own interferometer
(3) Imaging in practice
– Basic Imaging
– Imaging and Deconvolution
– How to use reconstruction algorithms
– Wideband, Wide-field and Mosaic imaging
x
Flagging
Calibration
Imaging
Notes: 25

## Slide 26: Imaging + Deconvolution
Data = Incomplete set of samples of the true signal
Image Reconstruction = Fit a model (of the sky) to the data
Notes: 26

## Slide 27
Basic Imaging :
Step 1 : Define image size and cell size
Step 2 : Gridding, data-weighting and FFT
Step 3 : Iterative deconvolution
Imaging in practice
Notes: 27

## Slide 28: Imaging in practice : Choosing image size, cell-size
– Choosing image 'cell' size : Nyquist-sample the main lobe of the PSF
PSF beam width : ( x to convert to degrees )
This is the diffraction-limited angular-resolution of the telescope
Ex : Max baseline : 10 km. Freq = 1 GHz. Angular resolution : 6 arcsec
Notes: 28

## Slide 29: Imaging in practice : Choosing image size, cell-size
– Choosing image 'cell' size : Nyquist-sample the main lobe of the PSF
PSF beam width : ( x to convert to degrees )
This is the diffraction-limited angular-resolution of the telescope
Ex : Max baseline : 10 km. Freq = 1 GHz. Angular resolution : 6 arcsec
– Choosing image field-of-view (npixels) : As much as desired/practical.
Field of View (fov) controls the uv-grid-cell size
- Antenna primary-beam limits the field-of-view ( 'slits' of finite width )
Notes: 29

## Slide 30: Imaging in practice : Choosing image size, cell-size
– Choosing image 'cell' size : Nyquist-sample the main lobe of the PSF
PSF beam width : ( x to convert to degrees )
This is the diffraction-limited angular-resolution of the telescope
Ex : Max baseline : 10 km. Freq = 1 GHz. Angular resolution : 6 arcsec
– Choosing image field-of-view (npixels) : As much as desired/practical.
Field of View (fov) controls the uv-grid-cell size
- Antenna primary-beam limits the field-of-view ( 'slits' of finite width )
– Gridding + FFT :
– An interferometer measures irregularly spaced points on the UV-plane.
– Need to place the visibilities onto a regular grid of UV-pixels, and then
take an FFT
Notes: 30

## Slide 31: Imaging in practice : Gridding and Weighting
-- Visibility data are placed onto a regular
grid before taking an i-FFT
– Convolutional Resampling
=> Use a gridding convolution function
=> Use weights per visibility
(weighted average of all data points per cell)
Notes: 31

## Slide 32: Imaging in practice : Gridding and Weighting
-- Visibility data are placed onto a regular
grid before taking an i-FFT
– Convolutional Resampling
=> Use a gridding convolution function
=> Use weights per visibility
(weighted average of all data points per cell)
An Image is a weighted-average of the data.
Natural
Weights
3
2
1
2
2
2
2
2
1
1
1
1
1
1
1
1
1
2
Uniform
Weights
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Notes: 32

## Slide 33: Imaging in practice : PSFs and Observed (dirty) Images
Robust 0.7
Bm : 4.0 arcsec
0.05 sidelobe
Uniform
Bm : 3.2 arcsec
+0.03,-0.08 sidelobe
Tapered Uniform
Bm : 8.0arcsec
0.01 sidelobe
Natural
Bm : 5.6 arcsec
0.1 sidelobe
Note the noise-structure. Noise is correlated between pixels by the PSF. Image Units (Jy/beam)
------ All pairs of images satisfy the convolution relation => Need to deconvolve them
PSF
OBSERVED
Notes: 33

## Slide 34: Imaging in practice : Weighting schemes
An Image is a weighted average of the data.
Weighting-scheme => modify the imaging properties of the instrument
=> emphasize features/scales of interest
=> control imaging sensitivity
 | Uniform/Robust All spatial frequencies get equal weight | Natural/Robust All data points get equal weight | UV-Taper Low spatial freqs get higher weight than others
Resolution | higher | medium | lower
PSF Sidelobes (VLA) | lower | higher | depends
Point Source Sensitivity | lower | maximum | lower
Extended Source Sensitivity | lower | medium | higher
Notes: 34

## Slide 35: Imaging in practice : Deconvolution
Image reconstruction is typically a “deconvolution” process.
Algorithms : Parameterized models + Iterative model fitting
( chi-square minimization )
CLEAN : Model the sky as a collection of delta-function ‘flux components’
MEM : Model the sky with delta-functions, and add a smoothness constraint
Multi-Scale-CLEAN : Model the sky as a collection of ‘blobs’ of different sizes
ASP Clean : Model the sky with a collection of best-fit Gaussians
Observed image = Instrumental Point-Spread-Function convolved with the true sky
Notes: 35

## Slide 36: Deconvolution – Hogbom CLEAN
Sky Model : List of delta-functions
(1) Construct the observed (dirty) image and PSF
(2) Search for the location of peak amplitude.
(3) Add a delta-function of this peak/location to the model
(4) Subtract the contribution of this component
from the dirty image - a scaled/shifted copy of the PSF
Repeat steps (2), (3), (4) until a stopping criterion is reached.
(5) Restore : Smooth the model with a 'clean beam' and
add residuals
The CLEAN algorithm can be formally derived as a model-fitting problem
– model parameters : locations and amplitudes of delta functions
– solution process : minimization via an iterative steepest-descent algorithm
( method of successive approximation )
Notes: 36

## Slide 37: Deconvolution – MultiScale (MS)-CLEAN
Multi-Scale Sky Model : Linear combination of 'blobs' of different scale sizes
- Efficient representation of both compact and extended structure (sparse basis)
A scale-sensitive algorithm
(1) Choose a set of scale sizes
(2) Calculate dirty/residual images
smoothed to several scales (basis functions)
– Normalize by the relative sum-of-weights
(instrument's sensitivity to each scale)
(3) Find the peak across all scales, update a single multi-scale model as well as all
residual images (using information about coupling between scales)
Iterate, similar to Classic CLEAN, and restore at the end.
The MS-CLEAN algorithm can also be formally derived as a model-fitting problem
using minimization and a basis set consisting of several 'blob' sizes.
Notes: 37

## Slide 38: Deconvolution – Comparison of Algorithms
CLEAN MEM MS-CLEAN ASP
Point source model
Point source model
with a smoothness
constraint
Multi-Scale model
with a fixed set of
scale sizes
Multi-Scale model
with adaptive best-fit
scale per component
Notes: 38

## Slide 39: Deconvolution – Comparison of Algorithms
Point source model
Point source model
with a smoothness
constraint
Multi-Scale model
with a fixed set of
scale sizes
Multi-Scale model
with adaptive best-fit
scale per component
CLEAN MEM MS-CLEAN ASP
Notes: 39

## Slide 40: How can you control the quality of image reconstruction ?
(1) Iterations and stopping criterion
'niter' : maximum number of iterations / components
'threshold' : don't search for flux below this level
– minor cycles can be inaccurate, so periodically trigger major cycles
(2) Using masks
Need masks only if the deconvolution is “hard”.
=> Bad PSFs with high sidelobes
=> Leftover bad data causing stripes or ripples
=> Extended emission with sharp edges
=> Extended emission that is seen only by very few baselines
Draw interactively (start small, and grow them) or supply final mask.
(3) Self-Calibration
Use your current best estimate of the sky ( i.e. the model image )
to get new antenna gain solutions. Apply, Image again and repeat.
Notes: 40

## Slide 41: Image Quality
Noise in the image : Measured from restored or residual images
– With perfect reconstruction,
The ideal noise level is :
– In reality, measure the RMS of residual pixel amplitudes
Model image
Restored image
Residual image
Notes: 41

## Slide 42: Image Quality
Noise in the image : Measured from restored or residual images
– With perfect reconstruction,
The ideal noise level is :
– In reality, measure the RMS of residual pixel amplitudes
Dynamic Range : Measured from the restored image
– Standard : Ratio of peak brightness to RMS noise
in a region devoid of emission.
– More truthful : Ratio of peak brightness to peak error (residual)
Model image
Restored image
Residual image
Notes: 42

## Slide 43: Image Quality
Noise in the image : Measured from restored or residual images
– With perfect reconstruction,
The ideal noise level is :
– In reality, measure the RMS of residual pixel amplitudes
Dynamic Range : Measured from the restored image
– Standard : Ratio of peak brightness to RMS noise
in a region devoid of emission.
– More truthful : Ratio of peak brightness to peak error (residual)
Image Fidelity : Correctness of the reconstruction
- remember the infinite possibilities that fit the data perfectly ?
- useful only if a comparison image exists.
Inverse of relative error :
Model image
Restored image
Residual image
Notes: 43

## Slide 44
Basic Imaging :
Narrow-frequency range, Small region of the sky
=> The 2D Fourier Transform relations hold
=> Convolution and deconvolution
Wide-Band Imaging :
=> Sky and instrument change across frequency range
Wide-Field Imaging
=> The 2D Fourier Transform relation breaks
Mosaic Imaging
=> Image an area larger than what each antenna can see.
Imaging with modern instruments
Notes: 44

## Slide 45: Wide-band Imaging – Sensitivity and Multi-Frequency Synthesis
Frequency Range : (1 – 2 GHz) (4 – 8 GHz) (8 – 12 GHz)
Bandwidth : 1 GHz 4 GHz 4 GHz
Bandwidth Ratio : 2 : 1 2 : 1 1.5 : 1
Fractional Bandwidth : 66% 66% 40%
1.0 - 2.0 GHz
1.0 GHz
1.5 GHz
2.0 GHz
UV-coverage / imaging properties change with frequency
=> combine
multi-frequency
measurements
during imaging
Sky Brightness can also change with frequency → model intensity and spectrum
Notes: 45

## Slide 46: Spectral Cube (vs) MFS imaging
3 flat-spectrum sources + 1 steep-spectrum source ( 1-2 GHz VLA observation )
Images made at different frequencies ( limited to narrow-band sensitivity )
Add all single-frequency
images (after smoothing
to a low resolution)
Use wideband
UV-coverage,
but ignore spectrum
( MFS, nterms=1)
Use wideband UV-coverage
+ Model and fit for spectra too
( MT-MFS, nterms > 1 )
Output : Intensity and Spectral-Index
2 GHz
1 GHz
Notes: 46

## Slide 47: Wide-Field Imaging – W-term
The ' w ' of a baseline can be large, away from the image phase center
The ' n ' for a source can be large, away from the image phase center
There are algorithms to account for this : Image Faceting, W-Projection.
Notes: 47

## Slide 48: Wide-Field Imaging – W-term
The ' w ' of a baseline can be large, away from the image phase center
The ' n ' for a source can be large, away from the image phase center
2D Imaging
Facet Imaging
W-Projection
Notes: 48

## Slide 49: Wide-Field Imaging – Primary Beams
Each antenna has a limited field of view => Primary Beam (gain) pattern
=> Sky is (approx) multiplied by PB, before being sampled by the interferometer
The antenna field of view :
D = antenna diameter
Compare with angular
resolution of the
interferometer :
But, in reality, P changes with time, freq, pol and antenna....
=> Ignoring such effects limits dynamic range to 10^4
=> More-accurate method to account for this : A-Projection
Notes: 49

## Slide 50: Wide-field Imaging -- Mosaics
Combine data from multiple pointings to form one large image.
Combine pointings either
before or after deconvolution.
Stitched mosaic :
-- Deconvolve each
pointing separately
-- Divide each image by PB
-- Combine as a weighted avg
Joint mosaic :
-- Combine observed images as a
weighted average
(or)
Grid all data onto one UV-grid,
and then iFFT
-- Deconvolve as one large image
One Pointing sees only part of the source
Notes: 50

## Slide 51: Wide-field Imaging -- Mosaics
Combine data from multiple pointings to form one large image.
Combine pointings either
before or after deconvolution.
Stitched mosaic :
-- Deconvolve each
pointing separately
-- Divide each image by PB
-- Combine as a weighted avg
Joint mosaic :
-- Combine observed images as a
weighted average
(or)
Grid all data onto one UV-grid,
and then iFFT
-- Deconvolve as one large image
Two Pointings see more.....
Notes: 51

## Slide 52: Wide-field Imaging -- Mosaics
Combine data from multiple pointings to form one large image.
Combine pointings either
before or after deconvolution.
Stitched mosaic :
-- Deconvolve each
pointing separately
-- Divide each image by PB
-- Combine as a weighted avg
Joint mosaic :
-- Combine observed images as a
weighted average
(or)
Grid all data onto one UV-grid,
and then iFFT
-- Deconvolve as one large image
Use many pointings to cover the source with approximately uniform sensitivity
Notes: 52

## Slide 53
Imaging – Algorithms and Options
Major Cycle
(Imaging)
DATA
GRIDDING
RESIDUAL
MODEL
iFFT
FFT
RESIDUAL IMAGE
MODEL IMAGE
DE-GRIDDING
Use Flags
and Weights
Image Definition
Minor Cycle
(Deconvolution)
Notes: 53

## Slide 54
Imaging – Algorithms and Options
Major Cycle
(Imaging)
DATA
GRIDDING
RESIDUAL
MODEL
iFFT
FFT
RESIDUAL IMAGE
MODEL IMAGE
DE-GRIDDING
Use Flags
and Weights
Solving for the sky model
(non-linear optimization)
Point sources, multiscale, etc.
Instrumental Corrections
(applied per visibility during gridding )
Wterm, primary beams, mosaics
Mapping of data to
Image Shape/Type
Spectral cube, continuum,
multi-term.
Image Definition
Minor Cycle
(Deconvolution)
Notes: 54

## Slide 55
Imaging – Algorithms and Options
Major Cycle
(Imaging)
DATA
GRIDDING
RESIDUAL
MODEL
iFFT
FFT
RESIDUAL IMAGE
MODEL IMAGE
DE-GRIDDING
Use Flags
and Weights
Clean ( Hogbom, Clark,
MultiScale, MultiTerm,
Asp, etc... )
Standard gridding, W-Proj
(WB)-A-Proj,
Joint Mosaics,
(Parallelization)
Cube, MFS, MT-MFS, MVC,
Faceting, Stokes,
Multi-Field, SD+INT
Stitched Mosaic
Image Definition
Minor Cycle
(Deconvolution)
https://casadocs.readthedocs.io/en/stable/notebooks/synthesis_imaging.html
Notes: 55

## Slide 56: Some points to remember …
How does an interferometer form an image ?
- Each antenna pair measures one 2D fringe.
Many antenna pairs => Fourier series
How do you get a model of the sky ?
- Solve the convolution equation via algorithms like Clean, MS-Clean, MT-Clean...
How do you make a raw image from interferometer data ?
- Assign weights to visibilities, grid them, take a Fourier transform
What does the raw observed image represent ?
- Observed Sky is the convolution of the true sky and the PSF
How do you choose the cell-size and image size for imaging ?
- Cell size = ( Resolution / 3 ). Image size = field-of-view / cell size
Notes: 56

## Slide 57: Some points to remember …
What is calibration ?
- Use calibrator data to solve for antenna gains, apply them to target data
How does wide-band data affect the imaging process ?
- Increased sensitivity, but the imaging properties and sky change with frequency
How do you image wide-band data ?
- Make a Cube of images, or Multi-Frequency-Synthesis with a spectral fit.
What is an antenna primary beam and what is its effect on an image ?
- Antenna power pattern. It multiplies with the sky,before convolution with the PSF
What is the w-term problem ?
- 2D Fourier transform approximations are invalid far away from the image center
Notes: 57