Scale sensitive deconvolution
S. Bhatnagar
NRAO, Socorro
Clean model
Asp-Clean model

---
Deconvolution
Deconvolution is a search for IM which solves the normal equation
Assuming N a gaussian R.V., c2 is the optimal estimator.
Deconvolution:
  - Update direction:
  - Update current model:
  - Compute
  - If IR does not satisfy stopping criteria, repeat
{color white bold{A^T V = A^T A I^M + A^T A N}}
{color white bold{I^D ~=~ PSF*I^M + PSF*I^N }}
{color white {Minimize: bold{%chi^2=[V-AI^M]^T %LAMBDA [V-AI^M]}}}
{color white {bold{nabla %chi^2 = -2 I^R_i nabla I^M}}}
{color white {bold{I^M_{i+1} = T(I^M_i, nabla %chi^2)}}}
{color white {bold{I^R_{i+1}=I^D - PSF*I^M_{i+1}}}}

---
Fundamental issues
Pixel-to-pixel noise is not independent
  - Neighboring pixels are not independent due to finite resolution
Extended emission naturally couples large number of pixels
Consequently, the effective number of degrees of freedom (DoF) are significantly less than the number of pixels with significant emission
  - This, when ignored, can lead to “over fitting”, or
  - Low level residuals
Pixelation
{color white bold{I^d = B*I^o + B*I^N}}

---
Scale-less deconvolution
Each pixel is treated as a DoF
Search space constraints by user supplied “boxes”
Clean (CS-Clean): A Steepest Descent algorithm
  - Dimensionality of the search space is equal to number of pixels in the “boxes”
  - Approx. update direction:
  - Iteratively take a step along the axis with the highest derivative:
MEM: Constrained minimization:
  - Minimize:
  - H is the Entropy function
{color white {I^M = sum_k A_K %delta(x_k)}}
{color white {bold{nabla %chi^2 = Residual Image (I^R)}}}
{color white {bold{I^M_{i+1}=I^M_i + g [max: I^R_i]}}}
{color white {bold{H - %lambda %chi^2} where %lambda is a Lagrange multiplier}}

---
Reconstructed images and residuals
CS-Clean MEM
Niter = 60K

---
Separation of signal and noise
{color white bold{I^d = B*I^o + B*I^N}}
The Dirty Image = True image corrupted by the PSF in a deterministic way + non-deterministic term
Peak value is used to separate the two terms
  - This works well in the regime where the first term dominates
With low level large scale emission, the peak of the two terms is comparable
Need to incorporate explicit prior knowledge to separates signal from noise.
Scale of emission fundamentally separates signal from noise:
  - All scales in IN < ~PSF Main-lobe
  - All scales in BITrue > ~PSF Main-lobe

---
Scale sensitive deconvolution
Incorporate the fact that scale of emission changes across the image explicitly in the algorithms
  - Discover the local scale
  - Compute its effect in the rest of the image
MS-Clean
  - Decompose the image using a fixed set of scales
  - Retains the shift-and-subtract nature of Clean algorithm
  - Matched filtering technique
  - However, assumes an orthogonal search space
    - No interaction between scales
Residual Image
Model image: ~15K comps.

---
Scale sensitive deconvolution
Search space is not orthogonal in general
Fixing the set of allowed scales is non-optimal.
Adaptive Scale Pixel (Asp)-Clean
  - Incorporate interaction between scales
  - Discover the local scale adaptively.
  - Use local scale as a the “size” of the logical “pixel”
Model image: ~1K comps.
Residual Image

---
Challenge
Incorporation of interaction between scales
  - Computing scales strongly with image complexity
Computing the effects for the entire image in each iteration is expensive
Acceleration methods
  - At each iteration, make a set of active Asps which have maximal impact in the current iteration
  - Restrict the search at each iteration to this sub-space
    - Keep the dimensionality of the search space in control

---
Asp-Clean acceleration
Fig 1: All Aspen are kept in the problem for all iterations. Scales all Aspen evolve as a function of iterations.
But note: Not all Aspen evolve significantly at all iterations.
Fig 2: The active-set is determined by thresholding the first derivative. Only those Aspen, shown by symbols, are kept in the problem which are likely to evolve significantly at each iteration.

---
Clean, MEM, MS-Clean, Asp-Clean
Id-BIM
Niter ~60K 15K 1K
 VTrue- VModel