Direction-dependent effects
S. Bhatnagar
NRAO, Socorro
RMS ~15mJy/beam
RMS ~15mJy/beam
RMS ~1mJy/beam

---
Direction dependent effects
- Instrumental
  - Primary Beam Effects
    - Time and frequency dependent
    - Polarization response
  - Pointing Errors
  - Non co-planar baselines (w-term)
  - FPA calibration/stability
- Sky
  - Stronger and more complex at low frequencies
    - Deconvolution errors, pixelation errors
  - Spectral index variations across the sky
Ionospheric/atmospheric

---
Measurement Equation
Generic Measurement Equation
Corruptions:
- Sky: Frequency dependence:
- Sky: Complex structure
    - Representation in a more appropriate basis
- Geometrical: W-term
The combined LHS determines “time constant” over which averaging helps
Data Corruptions Sky Geometry
{color white bold {I(bold s, %nu) = I(bold s, %nu_o) (%nu over %nu_o)^{%alpha(s,%nu)} }}
{color white bold {e^{%iota bold {s.b_{ij}}} = e^{%iota [u l + v m + w (sqrt{1-l^2 - m^2}-1)] }}}
{color white {V^{Obs}_{ij}(%nu) = J_{ij}(%nu,t) W_{ij} int J^S_{ij}(bold s,%nu,t)~I(bold s, %nu)~e^{bold {%iota s.b_{ij}}} ~d bold s}}
{color white {bold{J_{ij} = J_i otimes J_j^{{}*{}}}}} {color white {bold{J_{ij}^S = J_i^S otimes J_j^{S^{{}*{}}}}}}
Direction independent corruptions
Direction dependent corruptions

---
Challenges
- Unknowns
  - Jij, Jsij: Electronics, Primary Beams, antenna pointing, Ionosphere
    - Heterogeneous arrays (difference PB per baseline)
  - IM: Extended emission, spectral index variations
- Need efficient algorithms:
  - To solve parametrized ME (Curse of Dimensionality)
  - For known direction dependent corrections
  - Better parametrization of the sky (IM)
    - Including frequency dependence
  - Solver for the unknown DD effects (PB, ionosphere)
- Computing
  - Parallel computing & I/O
  - Software development costs

---
Algorithmic challenges
- Higher sensitivity ==> mode data + correction of more error terms
  - Imaging and calibration gets coupled
  - DD corrections can be as expensive as imaging
- More sophisticated parametrization required for the next generation telescopes
  - DD correction: PB(t, Freq, Pol.), atmosphere/ionosphere
  - Sky: Decompose the structure in scale sensitive basis
  - Sky: Parametrized for frequency and poln. Dependencies
- Physically motivated parametrization
  - Algorithmic performance-measure: SNR per DoF

---
Recent advances
{color yellow {bold{J^s_i(t) <> J^s_j(t)}}}
- (Pointing offsets, PB variations, etc.)
  - Corrections in the visibility plane
    - Scale sensitive deconvolution
      - Asp-Clean (2004), MS-Clean (2003)
    - Pointing SelfCal (2004)
    - Correction for Jsij during image deconvolution
      - W-Projection (2004)
      - AW-Projection (2005)
      - MS-MFS (2006-07)
  - Direct evaluation of the integral
    - Peeling (since ?)/ VLA Squint correction (2008)
{color white {V^{Obs}_{ij}(%nu) = J_{ij}(%nu,t) int J^S_{ij}(bold s,%nu,t)~sum_k I(x_k, y_k)~e^{bold {%iota s.b_{ij}}} ~d bold s}}

---
Primary beam effects
EVLA full-beam, full-band, full-pol imaging
PB variation across the band
EVLA: Sources move from main-lobe to side-lobes
PB rotation, pointing errors
Cross hand power
pattern
PB gain varies as a function time, frequency and direction in the sky

---
PB correction
AW-Projection algorithm
(Bhatnagar et al. A&A,487, 419, 2008)
  - Time and poln. Parametrization of the PB
  - No assumption about the sky emission
  - Scales well with imaging complexity
  - Straightforward to integrate with algorithms to correct for other errors (MFS, W-Projection, MS/Asp-Clean)
  - Requires a model for the Aperture Illumination

---
An example: EVLA @ 1.4 GHz

---
Example: Extended emission
- Stokes-V imaging of extended emission
  - Algorithms designed for point sources will not work
  - Need more sophisticated modeling of the extended emission

---
Example: PB effects in mosaicking

---
Antenna: AA vs Dishes
Simulation of LWA station beam
@50MHz
(Masaya Kuniyoshi, UNM/AOC)
EVLA antenna PB rotation with
Parallactic Angle

---
Full beam imaging limits
- Limits due to rotation of asymmetric PB
  - Error in PB model max. @ ~10% point
  - Max. in-beam error signal @ 50% point
  - DR of few x 104: 1
  - Errors higher in the first sidelobe
- Limits due to antenna pointing errors
  - In-beam max. error signal at 50% point
  - DR of a few x 104:1
  - Limits for mosaicking would be worse
    - Significant flux at half-power and side-lobes for many pointings

---
Pointing SelfCal: Solver
PB parametrized for pointing errors
Model image: 59 sources from NVSS.
Flux range ~2-200 mJy/beam
Typical antenna pointing offsets for VLA as a function of time
Over-plotted data: Solutions at longer integration time
Noise per baseline as expected from EVLA

---
Pointing SelfCal: Correction
No pointing correction:
RMS ~ 15μJy/b
After pointing correction:
RMS ~ 1μJy/b
(Bhatnagar, Cornwell & Kolap, EVLA Memo #84/paper in prep.)

---
Non-coplanar Baselines
color white {V(u,v,w)=G(u,v,w)*V(u,v,w=0)}
- E1=E’1(u,v,w) propagated using Fresnel diffraction
- Away from the phase center, sources are distorted
color white {where overline G(l,m,w)=func e^{2 %pi %iota left [ w left (sqrt{1-l^2-m^2} right ) right ]}}
(Cornwell, Kolap & Bhatnagar, EVLA Memo (2004), IEEE Special Issue on RA, (2008))

---
Example: VLA @ 74 MHz
- Coma cluster at 74 Mhz/VLA
- 30 arcsec resolution, RMS ~30mJy/beam
- Imaged using the W-projection algorithm (Golap)
15o

---
Ionospheric calibration
- Challenges:
  - W-term an issue for Bmax > 2-3Km & DR > 104
  - Ionospheric calibration: Even field based calibration fails for Bmax > 3Km

---
Computing
- Imaging scaling laws
  - Non co-planar baseline correction
    - W-Projection:
    - Faceting:
  - AW-Projection: N2GCF * Nvis
  - Peeling: Ncomp * Nvis * ?
- Scaling laws for DD solvers
  - FFT-based transforms: N2GCF * Nvis * Niter * Nparams
  - DFT-based transforms: Ncomp * Nvis * ? * Niter * Nparams
  - Nvis: 108-10 , N2GCF: 50-100 , Ncomp: 104-5
color white {(N^2_{wproj}+N^2_{GCF}) N_{vis}}
color white {N^2_{facets} N^2_{GCF} N_{vis}}

---
Near future data sizes
- Data I/O : Computing ~ 3:2 (at least)
- Expected average data rates about 10x larger
- Manual processing (data flagging, calibration and imaging) not an option
  - Need robust and efficient algorithms
  - Need robust heuristics
  - Need pipe line processing
  - Need all of this to run in a parallel computing environment
- Interoperability
  - Possible now via FITS
  - Data sizes is the problem!
  - Lower level software exchange is better
    - Sociological rather than technological problem!

---
Dominant DD Effects for SKA
- Station Power Pattern
  - AA vs. Dishes: Can we model the power patterns as a function of time, frequency and polarization?
  - Dishes: 2-axis vs 3-axis – Is the “software 3rd axis” sufficient?
- Sky Spectral Index variations
  - Must work with PB-correction
Sky and Beam polarization
- Ionosphere
  - Limits of existing techniques
Deconvolution of complex emission
Cross hand power
pattern
color white {S(%nu) prop left(%nu over %nu_o right)^{%alpha(%nu)}}