Imaging and deconvolution
S. Bhatnagar, NRAO

---
Plan for the lecture-I
Plan for the lecture-I
How do we go from the measurement of the coherence function (the Visibilities) to the images of the sky?
First half of the lecture: Imaging
Measured Visibilities <--> Dirty Image
<-->

---
Plan for the lecture-II
Plan for the lecture-II
Second half of the lecture: Deconvolution
Dirty image <--> Model of the sky
<-->

---
Imaging
Imaging
Interferometers are indirect imaging devices
For small w (small max. baseline) or small field of view (l2 + m2 << 1) and P(l,m)~1, I(l,m) is 2D Fourier transform of V(u,v)
bold color white {V^o(u,v,w) = iint P(l,m)I(l,m) e^{2 %pi %iota left[ ul + vm + w left( sqrt{1-l^2-m^2}-1 right) right]} {dl dm} over {sqrt{1-l^2-m^2}}}
bold color white {V^o(u,v) = iint I(l,m) e^{2 %pi %iota left[ul + vm right]} dl dm}
bold color white {V^o(u,v) dlrarrow I(l,m)}

---
Imaging: Ideal 2D Fourier relationship
Imaging: Ideal 2D Fourier relationship
Ideal visibilities(V ) True image(I )
FT
<-->
This is true ONLY if V is measured for all (u,v)!

---
Imaging: UV-plane sampling
Imaging: UV-plane sampling
With limited number of antennas, the uv-plane is sampled at discrete points:
= X
VM S Vo
bold color white {S(u,v) = sum_k %delta (u_k, v_k)}
bold color white {V^M(u,v) = S(u,v) V^o(u,v)}

---
Convolution with the PSF
Convolution with the PSF
Effect of sampling the uv-plane:
Using the Convolution Theorem:
The Dirty Image (Id) is the convolution of the True Image (Io) and the Dirty Beam/Point Spread Function (B)
B = FT-1(S)
In practice
Id = B*Io + B*IN where IN = FT-1(Vis. Noise)
To recover Io, we must deconvolve B from Id. The algorithm must also separate B*Io from B*IN.
bold color white {I^d(l,m) = ital{FT}^{-1} left[ V^o(u,v)S(u,v) right] }
bold color white {I^d(l,m) = B(l,m) * I^o(l,m) }

---
Convolution
Convolution
The PSF
= I(x0)B(x-xo) + I(x1)B(x-x1) + …

---
The Dirty Image
The Dirty Image
        FT
 The PSF <--> UV-coverage
        *
        The
        --> Dirty Image

---
Making of the Dirty Image
Making of the Dirty Image
Fast Fourier Transform (FFT) is used for efficient Fourier transformation. It however requires regularly spaced grid of data.
Measured visibilities are irregularly sampled (along uv-tracks).
Convolutional gridding is used to effectively interpolate the visibilities everywhere and then re-sample them on a regular grid (the Gridding operation)
VS= VM * C = (VoS) * C => Id . FT-1(C)
C is designed to have desirable properties in the image domain.

---
Dirty Beam: Interesting properties
Dirty Beam: Interesting properties
PSF is a weighted sum of cosines corresponding to the measured Fourier components:
Visibility weights (wi) are also gridded on a regular grid and FFT used to compute the Dirty Beam (or the PSF).
The peak of the PSF is normalized to 1.0
The 'main lobe' has a size dx ~ 1/umax and dy~1/vmax
This is the 'diffraction limited' resolution (the Clean Beam) of the telescope.
bold color white {B(l,m) = {sum_k W_k cos(u_kl + v_km)} over{ sum_k W_k} }

---
Dirty Beam: Interesting properties
Side lobes extend indefinitely
RMS ~ 1/N where N = No. of antennas

---
Close-in side lobes of the PSF
Close-in side lobes of the PSF
Close-in side lobs of the PSF are controlled by the uv-coverage envelope.
E.g., if the envelop is a circle, the side lobes near the main lobe must be similar to the FT of a circle: Bessel function/Radius

---
Close-in side lobes: VLA uv-coverage
Close-in side lobes: VLA uv-coverage

---
PSF forming: Weighting...
PSF forming: Weighting...
Weighting function (Wk) can be chosen to modify the side lobes
Natural Weighting
Wk=1/sk2 where sk2 is the RMS noise
Best RMS across the image.
Large scales (smaller baselines) have higher weights.
Effective resolution less than the inverse of the longest baseline.
bold color white {B(l,m) = {sum_k W_k cos(u_kl + v_km)} over{ sum_k W_k} }

---
...Weighting...
...Weighting...
Uniform weighting
Wk=1/uk,vk) where uk,vk) is the density of uv-points in the kth cell.
Short baselines (large scale features in the image) are weighted down.
Relatively better resolution
Increases the RMS noise.
Super uniform weighting:
Consider density over larger region.
Minimize side lobes locally.

---
...Weighting
...Weighting
Robust/Briggs weighting:
Wk = 1/[S uk ,vk) +sk2]
Parameterized filter – allows continuous variation between optimal resolution (uniform weighting) and optimal noise (natural weighting).

---
Examples of weighting
Examples of weighting

---
PSF Forming: Tapering
PSF Forming: Tapering
The PSF can be further controlled by applying a tapering function on the weights (e.g. such that the weights smoothly go to zero beyond the maximum baseline).
W'k=T(uk,vk) Wk(uk,vk)
Bottom line on weighting/tapering:
These help a bit, but imaging quality is limited by the deconvolution process!

---
The missing information
The missing information
As seen earlier, not all parts of the uv-plane are sampled – the 'invisible distribution'
1. “Central hole” below umin and vmin:
- Image plane effect: Total integrated power is not measured.
- Upper limit on the largest scale in the image plane.
2. No measurements beyond umax and vmax:
- Size of the main lobe of the PSF is finite
(finite resolution).
3. Holes in the uv-plane:
- Contribute to the side lobes of the PSF.

---
More on missing information
More on missing information
Missing 'central hole' means that the total flux, integrated over the entire image is zero.
Total flux for scales corresponding to the Fourier components between umax and umin can be measured.
In the presence of extended emission, the observations must be designed keeping in mind:
the required resolution ==> maximum baseline
the largest scale to be reliably reconstructed ==> minimum baseline
bold color white {V(u=0,v=0)=iint I^d(l,m) dl dm = 0 }

---
Recovering the missing information
Recovering the missing information
For information beyond the max. baseline, one requires extrapolation. That's unphysical (unconstrained).
Information corresponding to the “central hole”: possible, but difficult (need extra information).
Information corresponding to the uv-holes: requires interpolation. The measurements provide constraints – hence possible. But non-linear methods necessary.
Deconvolution = interpolation in the visibility plane.
If Z is the unmeasured distribution, then B*Z=0. If IM is a solution to Id=B*IM, then so is IM + aZ for any value of a.

---
Prior knowledge about the sky
Prior knowledge about the sky
What can we assume about the sky emission:
1. Sky does not look like cosine waves
2. Sky brightness is positive (but there are exceptions)
3. Sky is a collection of point sources (weak assertion)
4. Sky could be smooth
5. Sky is mostly blank (sometimes justifies “boxed”
deconvolution)
Non-linear deconvolution algorithms search for a model image IM such that the residual visibilities VR=Vo-VM are minimized, subject to the constraints given by the (assumed) prior knowledge.

---
Small digression: Vector notation
Small digression: Vector notation
Let
A = Measurement matrix to go from the image domain to the visibility domain (the measurement domain).
I = Vector of the image pixel values
V = Vector of visibilities
B = Operator (matrix) for convolution with the PSF
N = The noise vector
Then,
Id = BIo + BIN where BIN = ATAN
VM = AIM and Vo = AIo + N
VR = Vo – AIM

---
Some observations
Some observations
A is rectangular (not square) and is a collection of sines and cosines corresponding to only the measured Fourier components.
A is singular ==> A-1 does not exist
IM=A-1VM not possible ==> non-linear methods
needed
N is independent gaussian random process. Noise in the image domain = BIN
Pixel-to-pixel noise in the image is not independent

---
...more observations
...more observations
For successful recovery of Io given Id, prior knowledge must fundamentally separate BIo and BIN.
c2 is the optimal estimator. Deconvolution then is equivalent to:
Deconvolution is equivalent to function minimization
Algorithms differ in the parameterization of Pk, the type of constraints and the way the constraints are applied.
bold color white {Minimize: %chi^2 = left lline V^m - A I^M right rline^2 "where" I^M = sum_k P_k;~~P_k equiv "Pixel Model" }

---
Deconvolution algorithms
Deconvolution algorithms
Scale-less algorithms:
Popular ones: Clean, MEM and their variants
Scale-sensitive algorithms (new turf!):
Existing ones: Multi-scale Clean, Asp-Clean
Image plane corrections (in use)
Existing ones: w-projection, pb-projection
bold color white {P_k = A_k %delta(x - x_k) }
bold color white {P_k = A_k f left( Position, Scale right)}

---
The classic Clean algorithm (Hogbom, 1974)
The classic Clean algorithm (Hogbom, 1974)
Prior knowledge about the sky:
- is composed of point sources
- is mostly blank
Algorithm:
1. Search for the peak in the dirty image.
2. Add a fraction g (loop gain) of the peak value to IM.
3. Subtract a scaled version of the PSF from the position of the peak IRi+1= IRi – g B max(IRi)
4. If residuals are not “noise like”, goto 1.
5. Smooth IM by an estimate of the main lobe (the “clean beam”) of the PSF and add the residuals to make the “restored image”

---
Details of Clean
Details of Clean
It is a steepest descent minimization.
Model image is a collection of delta functions – a scale insensitive algorithm.
A least square fit of sinusoids to the visibilities which is proved to converge (Schwarz 1978).
Stabilized by keeping a small loop gain (usually g=0.1-0.2).
Stopping criteria: either the max. iterations or max. residuals some multiple of the expected peak noise.
Search space constrained by user defined windows.
Ignores coupling between pixels (extended emission) – assumes an orthogonal search space.

---
Clean: Model
Clean: Model

---
Clean: Restored
Clean: Restored

---
Clean: Residual
Clean: Residual

---
Clean: Model visibilities
Clean: Model visibilities
Model Vis.
Sampled Vis
Residual Vis.
True Vis.

---
Clean: Example
Clean: Example

---
Variants of the Classic Clean
Variants of the Classic Clean
Clark Clean – uses FFT to speed up
Minor cycle(inexpensive) : Clean the brightest points using an
approximate PSF to gain speed
Major cycle(expensive): Use FFT convolution to accurately remove
the point sources found in the minor cycle
Cotton-Schwab Clean: A variant of Clark Clean
Subtract the point sources from the visibilities directly.
Sometimes faster and always more accurate then Clark Clean.
Easy to adapt for multiple fields.

---
Deconvolution algorithms: MEM
Deconvolution algorithms: MEM
MEM is a constrained minimization algorithm.
Fast non-linear optimization algorithm due to Cornwell&Evans(1983).
Solve the convolution equation, with the constrain of smoothness via the 'entropy'
mk is the prior image – usually a flat default image.
Default image is a very useful in incorporating model images from other algorithms etc.
Naturally useful when final image is some combination of images (like mosaic images).
bold color white {H(I) = - sum_k I_k - log left( I_k/m_k right)}

---
MEM: Some points
MEM: Some points
Works better than Clean for extended emission.
Every pixel is treated as a potential degree of freedom – a scale insensitive algorithm.
Point sources are a problem, particularly along with large scale background emission – but can be removed with, say, Clean before hand.
Easier to analyze and understand.

---
MEM: Model
MEM: Model

---
MEM: Restored
MEM: Restored

---
MEM: Residual
MEM: Residual

---
MEM: Model visibilities
MEM: Model visibilities
Model Vis.
Sampled Vis
Residual Vis.
True Vis.

---
MEM: Example
MEM: Example

---
Role of boxes
Role of boxes
Limit the search for components to
only parts of the image.
A way to regularize the deconvolution process.
Useful when small no. of visibilities
(e.g. VLBI/snapshots).
Do not over-Clean within the boxes
(over-fitting).
Deeper Clean with no/loose boxes and lower loop gain can achieve similar (more objective) results.
Stop when Cleaning within the boxes has no global effect (insignificant coupling of pixels due to the PSF).

---
Fundamenal problem with scale-less decomposition
Fundamental problem with scale-less decomposition
Each pixel is not an independent degree of freedom (DOF).
E.g., a gaussian shaped source covering 100 pixels can be represented by 5 parameters.
Clean/MEM treats each pixel within a clean-box as an independent degree of freedom.
Scale fundamentally separates noise and signal.
-Largest coherent scale in BIN ~ the size of the resolution element.
-Physically plausible IM is composed of scales >= the resolution element (smallest scale is of the size of the resolution element).
Scale-sensitive reconstruction therefore leaves more noise-like (uncorrelated) residuals.

---
Scale Sensitive Deconvolution: MS-Clean
Scale Sensitive Deconvolution: MS-Clean
Inspired by the Clean algorithm (Cornwell & Holdaway).
Decompose the image into a pre-computed set of symmetric “blobs” at a few scales (e.g. Gaussians).
Algorithm
1. Make residual images smoothed to a few scales.
2. Find the peak among these residual images.
3. Subtract from all residual images a blob of scale corresponding to the scale of the residual image which had the peak.
4. Add the blob to the model image.
5. If more peaks in the residual images, goto 1.
6. Smooth the model image by the “clean beam” and add the
residuals.

---
MS-Clean details
MS-Clean details
Deals with compact as well as extended emission better (need to include a blob of zero scale).
Retains the scale-shift-n-subtract nature of Clean – easy to implement.
Reasonably fast (for what it does!)
Breaks up non-symmetric structures (as in Clean – but the errors are at larger scales than in Clean).
Ignores coupling between blobs.
Assumes an orthogonal space and steepest descent
minimization.

---
MS-Clean: Model
MS-Clean: Model

---
MS-Clean: Restored
MS-Clean: Restored

---
MS-Clean: Residual
MS-Clean: Residual

---
MS-Clean: Model visibilities
MS-Clean: Model visibilities
Model Vis.
Sampled Vis
Residual Vis.
True Vis.

---
MS-Clean: Example
MS-Clean: Example

---
Multi-resolution vs. Multi-scale Clean
Multi-resolution vs. Multi-scale Clean
Subtle difference between AIPS and AIPS++ implementations of scale sensitive
AIPS++: Each iteration of the minor cycle removes the optimal scale (one which reduces the residuals globally). Effectively, this achieves a “simultaneous” deconvolution at various scales [Multi-Scale Clean]
AIPS: A decision, based on a user defined parameter, is made at the start of each minor cycle about the optimal scale to deconvolve [Multi-resolution Clean].
MS-Clean naturally detects and removes the scale with maximum power
Removal of the optimal scale in MR-Clean strongly depends on the value of the user defined parameter.

---
Scale Sensitive Deconvolution: Asp-Clean
Scale Sensitive Deconvolution: Asp-Clean
Inspired by Pixon reconstruction (Puetter & Pina, 1994).
Decompose the image into a set of Adaptive Scale Pixel (Asp) model (Bhatnagar & Cornwell, 2004).
Algorithm:
1. Find the peak at a few scales, and use the scale with the highest peak as an initial guess for the optimal dominant scale.
2. Make a set of active-aspen containing Aspen found in earlier
iterations and which are likely to have a significant impact on
convergence.
3. Find the best fit set of active-Aspen (expensive step).
4. If termination criterion not met, goto 1.
5. Smooth with the clean-beam. Add residuals if it has systematics.

---
Asp-Clean details
Asp-Clean details
Deals with non-symmetric structures better.
Incorporates the fact that scale changes across the image. Residuals are more noise-like.
Incorporates the fact that search space is potentially non-orthogonal (inherent coupling between Aspen).
Aspen found in earlier iterations are not frozen.
Scales well with computing power.
Slower in execution speed.

---
Asp-Clean details: acceleration
Asp-Clean details: acceleration
Fig 1: All Aspen are kept in the problem for all iterations. Scales all Asp scales evolve as a function of iterations.
Not all Aspen evolve significantly for at all iterations.
Fig 2: The active-set is determined by thresholding the first derivative. Only those Aspen, shown by symbols, are kept in the problem which are likely to evolve significantly at each iteration.

---
Asp-Clean: Model
Asp-Clean: Model

---
Asp-Clean: Restored
Asp-Clean: Restored

---
Asp-Clean: Residual
Asp-Clean: Residual

---
Asp-Clean: Model visibilities
Asp-Clean: Model visibilities
Model Vis.
Sampled Vis
Residual Vis.
True Vis.

---
Asp-Clean: Example
Asp-Clean: Example

---
Clean, MEM, MS-Clean, Asp-Clean
Clean, MEM, MS-Clean, Asp-Clean
 Id-BIM Niter ~60K 50 ~15K ~1K
 VTrue- VModel

---
High Dynamic Range Imaing: Full beam Imaging
High Dynamic Range imaging
Full Beam Imaging
Direct dependent gains(e.g. Antenna Power Patterns P(l,m))
Rotation of PB on the sky + pointing errors gives time varying direction dependent gains (limits Mosaicking DR).
Antenna polarization response is azimuthally asymmetric
VLA polarization squint, full beam full Stokes imaging correction required even for moderate dynamic ranges
Sky and antenna response frequency dependent
EVLA: PB changes by a factor of 2!
color white bold {V^{obs}_{ij} = J_{ij} int J^{Sky}_{ij}(vec{S}) I(vec{S}) e^{2 %pi %iota vec{U}.vec{S}} d vec{S}}
color white {bold {J_{ij}} equiv "Direction independant gains"}
color white {bold {J^{Sky}_{ij}} equiv ""}
color white {%nu_max: %nu_min = 2:1}

---
Full beam imaging: Mathematical Framework
Mathematical Framework
If E is unitary (or approximately so), use as the inverse operator
Use for update direction (Minor Cycle)
Use for residuals computation (Major Cycle)
The modified transforms correct for image place errors
The W-Projection algorithm: Correction for non co-planarity
The PB-Projection algorithm: Correction for PB effects (pointing errors, poln., PB rotation)
color white {bold {V^{obs}} = bold{E A I}~"where " phantom A bold{E}=bold{A^T J^{Sky} A}}
color white {bold {A}^T bold{E}^T}
color white {bold {A}^T bold{E}^T}
color white {bold {EA}}

---
Wide field imaging
Wide field imaging
W-projection:
color white {"w-term" = e^{2 %pi %iota w left(sqrt{1-l^2-m^2}-1 right)}}
Errors not due to w-term
Limited by pointing errors/PB-rotation?
Errors in the first sidelobe due to PB-rotation

---
Primary Beam Rotation
Primary Beams
Stokes-I PB(PA)
PB(t) – Average PB

---
PB-Projection: Stokes-I
Simulations: Stokes-I
Stokes-I imaging with and without PB effects
(Polarization squint, Pointing offsets, PB rotation)
color white {V^{Obs}_{ij}=J_{ij} V^M_{ij}}
RMS ~15mJy/beam
RMS ~1mJy/beam

---
Full-beam full-Stokes imaging
Full-beam full-Stokes imaging
Full Stokes imaging requires full Sky Muller matrix
color white {{bold {J}}_i^p (vec{S}), {bold{J}}_i^q(vec{S}) equiv "Antenna voltage pattern in orthogonal polarization"}
color white {{bold {J}}_i^{pq} (vec{S}), {bold{J}}_i^{qp}(vec{S}) equiv "Leakage of polarization due to reflection from curved surface"}
color white {{bold {J}}_{ij} (vec{S}) "is not identity or even diagonal for DR>"10^4}

---
Structure of the Sky-Muller Matrix
J03
J00
J00-J11

---
References
References
Synthesis Imaging in Radio Astronomy II; Imaging and deconvolution.
High Fidelity Imaging of Moderately Resolves Sources; Briggs, D. S., PhD Thesis, New Mexico Tech., 1995
Understanding radio polarimetry. I,II,III; Hamaker, J., P., Bregman, J.D., & Sault, R.J. A&A, 117,137, 1996
Scale sensitive deconvolution of astronomical images: I-Adaptive Scale Pixel (Asp) model; Bhatnagar,S. & Corwnell,T.J., A&A, 426, 747-754, 2004 (astro-ph/0407225).
W Projection: A New Algorithm for Non-Coplanar Baselines; Cornwell,T.J., Golap,K., & Bhatnagar,S., 2003, EVLA Memo 67
Solving for the antenna based pointing errors; Bhatnagar,S., Cornwell,T.J., & Golap,K., 2004, EVLA Memo 84
Corrections of errors due to antenna power patterns during imaging; Bhatnagar,S., Cornwell,T.J., & Golap,K., 2006, EVLA Memo 100