Wide-band (wide-field) imaging
Goal : Make images at the wide-band sensitivity level
Outline :
        – Bandwidth and bandwidth-ratio
        – Frequency-dependent sky and instrument
        – Methods to reconstruct intensity and spectra
        – Wide-field effects of wide-band imaging
        – Wide-band self-calibration
Flagging + RFI
Goal : Discard data unusable for imaging
Outline :
        – Flagging based on data-selection
        – Automatic RFI identification and flagging
Urvashi Rau (NRAO) EVLA Data Reduction Workshop, NRAO, Socorro,NM 24 Feb 2012

---
Bandwidth and bandwidth-ratio
color white { {%nu_{max}} - %nu_{min} }
Instantaneous bandwidth :
   VLA = 50 MHz
   EVLA = 1 GHz at L-Band, 4 GHz at C-band, upto 8 GHz at higher bands.
   Currently, maximum bandwidth is 2 GHz => ( x 6 )
Broad-band receivers => Higher 'instantaneous' continuum sensitivity
Bandwidth Ratio ( ) or Fractional Bandwidth
Higher BWR ( 2:1 at L,S, C bands ) => Stronger frequency-dependent effects
        within the band (sky and instrument)
color white { %sigma_{continuum} ~=~ {%sigma_{%delta %nu}} over {sqrt{ ({%nu_{max} - %nu_{min}}) / {%delta %nu} }} ~=~ {%sigma_{chan}} over {sqrt{N_{chan}}} }
color white { {{%nu_{max}} - %nu_{min}} over %nu_{mid} }
color white { {%nu_{max}} : %nu_{min} }

---
Frequency-dependence of the instrument and sky
Multi-Frequency UV-coverage
1.0 GHz
1.5 GHz
2.0 GHz
- UV-coverage (angular resolution)
- Primary-beam (field-of-view)
- Sky-brightness distribution
    ..... all change with frequency
Average Primary Beam
1.0 GHz
Multi-Frequency Primary Beams
1.5 GHz
2.0 GHz
50%
90%
'Spectral Index' of PB
20%

---
Wideband Imaging Options
(2) Combine all frequencies
       during imaging
        ( MFS : multi-frequency synthesis )
      - Signal-to-noise ratio : all SPWs
      - Angular resolution is given by
        the highest frequency
      - Imaging fidelity is given by
        the combined uv-coverage
When do you need MFS ?
    - Single channel / SPW sensitivity is too low
    - Complicated fields where single-SPW
       uv-coverage gives non-unique solutions
    - Need high angular-resolution images
        (intensity and spectral index)
(But, need to model / reconstruct spectra too... )
(1) Make images for each
     channel / SPW separately.
    - Signal-to-noise ratio : one SPW
    - Angular resolution varies
        with SPW (smooth to lowest)
    - Imaging fidelity may change
       across SPWs
When will this suffice ?
    - Sources have sufficient SNR in
        a single channel / SPW
    - UV-coverage per SPW gives
        un-ambiguous reconstructions
    - You don't need the highest-possible
        angular resolution for spectra

---
Comparison of single-SPW imaging with MFS - Intensity
Data : 20 VLA snapshots at 9 frequencies across L-band + wide-band self-calibration
MS-MFS (3 terms)
Single SPW Imaging
Peak residual = 100 mJy
Off-source rms = 30 mJy
Peak residual = 150 mJy
Off-source rms = 50 mJy
=> Similar results
        - both methods reconstruct plausible intensity images.
        - both have similar residual errors due to deconvolution.
( MS-MFS : Multi-Scale Multi-Frequency Synthesis : models intensity and spectrum (Taylor polynomial) )

---
Comparison of single-SPW imaging with MFS – Spectral Index
Data : 20 VLA snapshots at 9 frequencies across L-band + wide-band self-calibration
Spectral Index from single-SPW images
MS-MFS Spectral Index
Restored Continuum Image
Limited in resolution + deconvolution errors
- Limited to resolution of the lowest frequency
- Shows effect of insufficient single-frequency uv-coverage
- Shows imaging fidelity due to multi-scale deconvolution
- Shows expected structure with errors < 0.2
Two-point spectrum (1.4 – 4.8 GHz)
=> It helps to use the combined uv-coverage and solve for sky spectra.
Can often extract more information from your data, compared to traditional methods, but not always.
“Multi-Scale Multi-Frequency Synthesis”
 C.Carilli et al, Ap.J. 1991.
(VLA A,B,C,D Array at L and C band)

---
Multi-Scale MFS : as implemented in CASA
Sky Model : Collection of multi-scale flux
        components whose amplitudes
        follow a polynomial in frequency
Image Reconstruction : Linear least squares + Deconvolution
User Parameters : Imaging mode : mode='mfs'
        Number of Taylor-polynomial coeffs. : nterms=2
        Reference frequency : reffreq = '1.5GHz'
        Set of spatial scales (in units of pixels) : multiscale=[0,6,10]
Data Products : Taylor-Coefficient images
        - Interpret in terms of a power-law : spectral index and curvature
        (Or, evaluate the spectral cube (for non power-law spectra) )
color white { I^{sky}_%nu = sum_{t} I_{t} {left({%nu - %nu_0}over{%nu_0}right)^t} }
color white { I_t = sum_{s} [I^{shp}_s * I_{s,t}] }
( 2011A&A...532A..71R , arXiv:1106.2745 )
color white { I_0, I_1, I_2, ... }
color white { I_0 = I_{%nu_{0}} ~~~~ I_1 = I_{%nu_{0}} %alpha ~~~~ I_2 = I_{%nu_{0}} left( {%alpha(%alpha-1)} over {2} + %beta right) }

---
Dynamic Range (vs) NTERMS – 3C286 field (point sources)
( I=14.4 Jy/bm, alpha = -0.47, BW=1.1GHz at Lband )
NTERMS = 2
Rms :
1 mJy -- 0.2 mJy
DR :
 10,000 -- 17,000
NTERMS = 1
Rms :
 9 mJy -- 1 mJy
DR :
   1600 -- 13000
NTERMS = 3
Rms :
 0.2 mJy -- 85 uJy
DR :
 65,000 -- 170,000
NTERMS = 4
Rms
0.14 mJy -- 80 uJy
DR :
>110,000 -- 180,000

---
Error estimates : Bandwidth-ratio vs 'nterms' (high SNR)
If spectra are ignored
=> larger BWR gives
     larger errors
If there is high SNR,
=> more terms gives
     smaller errors
Note : These plots are for one point-source at the phase center, with very high signal-to-noise levels.
In practice, use nterms>2 only if there is high SNR (>100), and if you can see spectral artifacts in the image with nterms=2

---
Multi-Scale vs Point-Source model for wideband imaging
    MFS
(4 terms)
Intensity Image
multi-scale
point-source
color white {%I_{0}}
color white {%I_{0}}
{color white{ %alpha = +1}}
{color white{ %alpha = -1}}
%alpha
%alpha
Spectral
Turn-over
{color white{ %alpha = -2}}
Gradient in Spectral Index
color black {%delta %alpha < 0.05 }
Average Spectral Index
color black {%delta %alpha approx 0.5 }
%alpha
color white {%beta}
color white {%beta}
color white {%beta}
color white {%delta %beta approx 0.5 }
color white {%delta %beta < 0.2 }
=> For extended emission,
        –> a multi-scale model gives better spectral index and curvature maps

---
Separating regions/sources based on spectral index structure
( 2011ApJ...739L..20B , arXiv:1106.2796 )
color white {%I_{0}}
%alpha
color white {%I_{0}}
%alpha
color white {%I_{0}}
%alpha
color white {%I_{0}}
%alpha
Initial results of a pilot survey ( EVLA RSRO AB1345 ). These examples used nterms=2, and about 5 scales.
 => Within L-band and C-band, can tell-apart regions by their spectral-index
      ( +/- 0.2 ) if SNR>100.
 => These images have a dynamic-range limit of few x 1000
Raw Data Sizes : ~ 7 hour run and 1-sec integration, and 2 MHz channel-width : 300 GB.
Target source data size after calibration and 10-sec averaging ~ 10 to 20 GB.
Image-reconstruction time (single node) ~ 3 hours

---
Small spatial-scales - moderately-resolved sources
Can reconstruct the spectrum at the angular resolution of the highest frequency (only high SNR)
color yellow {}
1.0 GHz
2.8 GHz
Restored Intensity image
color white {I}
1.6 GHz
3.4 GHz
Spectral Index map
color white {%alpha}
2.2 GHz
4.0 GHz

---
Very large spatial scales - without short-spacing data
The spectrum at the largest spatial scales is NOT constrained by the data
Amplitude vs UV-dist
    Data
color white {I}
Data +
Model
( Wrong )
color black {%alpha}

---
Very large spatial scales – with short-spacing data
External short-spacing constraints help ( visibility data, or starting image model )
color white {I}
Amplitude vs UV-dist
    Data
Data +
Model
( Correct )
color black {%alpha}

---
Spectral Curvature : VLA data : M87 1.1-1.8 GHz
Data : 10 VLA snapshots at 16 frequencies across L-band
        = -0.52
        = -0.62
        = -0.42
        = -0.52, =-0.48
color black {%alpha}
color black {%alpha}
color black {%alpha}
color black {%alpha}
color black {%beta}
color white {I}
color black {%alpha = -0.52}
color black {%DELTA %alpha approx 0.2}
color black {%alpha}
From existing P-band (327 MHz), L-band(1.42 GHz)
and C-band (5.0 GHz) images of the core/jet
      P-L spectral index : -0.36 ~ -0.45
      L-C spectral index : -0.5 ~ -0.7
color black {%beta}
=> Need SNR > 100 to fit spectral index variation ~ 0.2 ( at the 1-sigma level ... )
        => Be very careful about interpreting
color white {%beta}

---
Wide-Field issues : Wide-band Primary-Beam
3C286 field , C-config , L-band
Without PB Correction
Total Intensity Image
{color black{ %alpha = -1.21}}
{color black{ %alpha = -0.47}}
With PB Correction during imaging
{color black{ %alpha = -0.65}}
Verified spectral-indices by pointing directly at one background source.
→ compared with 'corrected'
Obtained = 0.05 to 0.1 for SNR or 1000 to 20
color white {%alpha_{off.center}}
color white {%alpha_{center}}
{color black{ %alpha = -0.47}}
color white {%delta %alpha}
Also verified via holography observations at two frequencies
PB-correction + MS-MFS not yet available in 'clean', but approximate correction is possible with a python script.

---
IC10 dwarf-galaxy : spectral-index : Wideband PB correction
        + angular resolution offered by MS-MFS
Before PB-correction
After PB-correction
50% of PB
( 2011ApJ...739L..23H , arXiv:1108.0401 )
  Result of post-MS-MFS wide-band PB-correction (CASA)
   For comparison, spectral-index map made by PB-correcting single-SPW images smoothed to the lowest resolution (AIPS).
This post-deconvolution correction assumes that the primary-beam does not vary / rotate during the observation, and that all points are weighted equally....

---
Choices that effect errors during wide-band imaging
- Artifacts in the continuum image due to too few Taylor-terms.
      Very high signal-to-noise,point-sources : use a higher-order polynomial.
      Otherwise, use 2 or 3 terms to prevent over-fitting.
- Error in spectral index/curvature due to too many Taylor-terms.
      Low signal-to-noise : use a linear approximation.
      Again, nterms=2 or 3 is safer for low signal-to-noise extended emission.
- Error propagation during the division of one noisy image by another.
      Extended emission : use multiple spatial scales to minimize this error (see output error map)
      Choice of scale sizes : by eye, and verifying that the total-flux converges
- Flux-models that are ill-constrained by the measurements
      Choose scales/nterms appropriately. For very large scales, add short-spacing information.
- Wide-field errors : Time and Frequency-variability of the Primary Beam
      Use W-projection, A-projection along with MS-MFS (software in progress)
Remember : Increased imaging sensitivity (over wide fields), high-fidelity high dynamic-range reconstructions of both spatial and spectral structure.

---
Choices that effect performance (current MS-MFS implementation)
- Major Cycle runtime x (and size of dataset)
   – N_Taylor residual images are gridded separately; N_Taylor model images are 'predicted'.
   – Wide-field corrections are applied during gridding (A-W-Projection, mosaicing).
- Minor Cycle runtime x
- Minor Cycle memory x
Rate of convergence : Typical of steepest-descent-style optimization algorithms : logarithmic. Can control 'loop gain', 'cleaning depth'
    Some source structures will handle loop-gains of 0.3 to 0.5 or more (0.3 is safe).
Runtimes reported by different people have ranged from 1 hr to several days.
      => Different choices of parameters => Choose only what you really need.
color white {N_{taylor}}
color white {N_{taylor} N_{scales} N_{pixels}}
color white { left[ 0.5 left(N_{taylor} N_{scales}right)^2 + N_{taylor} + N_{taylor} N_{scales} right] N_{pixels}}

---
Example : SNR G55.7+3.4
7 hour synthesis, L-Band, 8 spws x 64 chans x 2 MHz, 1sec integrations
Due to RFI, only 4 SPWs were used for initial imaging ( 1256, 1384, 1648, 1776 MHz )
( All flagging and calibration done by D.Green )
Imaging Algorithms applied : MS-MFS with W-Projection
     (nterms=2, multiscale=[0, 6, 10, 18, 26, 40, 60, 80] )
Peak Flux : 6.8 mJy
Extended flux : ~ 500 micro Jy
Peak residual : 65 micro Jy
Off-source RMS : 10 micro Jy (theoretical = 6 micro Jy)

---
Only MS-Clean

---
MS-Clean +
W-Projection

---
MS-MFS +
W-Projection
Max sampled spatial scale : 19 arcmin (L-band, D-config)
Angular size of G55.7+3.4 : 24 arcmin
MS-Clean was able to reconstruct total-flux of 1.0 Jy
MS-MFS large-scale spectral fit is unconstrained.

---
MS-MFS +
W-Projection +
MS-Clean model

---
Wide-field effects of wide-band imaging
{color black{ 4 %sigma}}
{color black{ 1 %sigma}}

---
G55.7+3.4 : within the main lobe of the PB
{color white{ %alpha = -2.7}}
{color white{ %alpha = -1.1}}
{color white{ %alpha approx -2.9}}
{color white{ %alpha = -0.9}}
{color white{ %alpha approx -3.2}}

---
Wide-band Self-calibration ( using MS-MFS wideband model )
        In CASA, 'clean' saved a wide-band model (calready=True). Or, use 'ft'.
Peak residual = 32 mJy/bm
Off-source rms = 6 mJy/bm
Peak residual = 65 mJy/bm
Off-source rms = 18 mJy/bm
Amplitudes of bandpass gain solutions......
5 chans x 7 spectral-windows
- Can use MS-MFS on your calibrators too, if you don't know their spectra.
- Can also use this wide-band model for continuum subtraction.

---
Flagging + Examining your data for RFI
Flagging Modes :
        – operator logs of known bad antennas and time-ranges / online flags
        – shadowing between antennas (elevation-dependent)
        – elevation-dependent flags
        – known frequency ranges with bad RFI
        – exact zeros (from the correlator) , clip very high points, 'automatic flagging '
At L-Band, can use ~500 MHz with very rough flagging, ~800 MHz if done carefully.
One way to examine your data, is to run 'autoflag' and look at flag counts
– Inspect uncalibrated data to identify 'clean' regions
– Get an estimate of the fraction of total bandwidth usable for imaging.
– Obtain a flagversion to use as a starting point (first calibration/imaging pass).
– Run it on RFI monitoring data – feed-back information about un-documented RFI

---
Automatic RFI identification and flagging
TFCrop : Detect outliers on the 2D time-freq plane.
  – Average visibility amplitudes along one dimension
  – Fit a piece-wise polynomial to the base of RFI spikes
        -- calculate 'sigma' of data - fit.
  – Flag points deviating from the fit by more than N-sigma
  – Repeat along the second dimension.
  – Grow/extend flags along time, frequency, polarization
Can operate on un-calibrated data + one pass through MS
'testautoflag' in CASA 3.3. 'tflagdata' in CASA 3.4
RFLAG : Detect outliers using a sliding-window rms in time
   – For each channel,
     – Calculate rms of real and imag parts of visibilities across a
        sliding time window.
     – Calculate the mean-rms across time, and deviations of these
        rmss from the mean.
     – Search for outliers
        (local rms > N x (median-rms + median-deviation)
   – For each timestep,
     – Calculate a median-rms across channels, and flag points
        deviating from this median.
   – Grow/extend flags (pol, time, freq, baselines)
Needs calibrated data + two passes through data.
“RFLAG” in AIPS. 'tflagdata' in CASA 3.4

---
Visualize Data/Flags at run-time ( testautoflag in CASA 3.3, tflagdata in CASA 3.4 )

---
Example 1 (with extension along frequency, and statistics-based flagging)

---
Example 2 (an example where it is better to flag more than less..)

---
Example 3 (with broad-band RFI)

---
RFI identification strategies
– RFI is in-general frequency and direction-dependent (satellites / local/ … )
   => Inspect and decide flagging strategies separately per SPW / IF and Field.
   => Inspect baseline groups (short, mid, long... ), especially at higher frequencies
– Choose which correlations to operate on (extend flags to others)
   => RL, LR have higher RFI signal-to-noise, and RR and LL have stronger band-shape information (depends on what you're looking for)
– Operate on bandpass-corrected data
   => Do a bandpass calibration in a separate step, or use methods that account for uneven bandpass levels.
– Hanning Smoothing
   => when there is very strong RFI with ringing in nearby channels.
        ( for weak RFI, this can spread the RFI to more channels )

---
Summary
Broad-band receivers
        => better sensitivity
To achieve this sensitivity
    => Careful RFI removal
    => Spatial and spectral image reconstructions along with corrections for wide-field instrumental effects.
User choices (start simple ):
   - Will single-SPW imaging suffice ?
   - If not, then use MS-MFS :
        N-terms ( is there enough SNR ? )
        Multi-scales ( measured vs desired )
   - Wide Field-of-view ?
        W-term, Primary-beam
Imaging results so far (high SNR) :
 - Point sources : OK
 - Extended emission : DR of few 1000,
 - Spectral-index accuracy : 0.02 ~ 0.2
 - Wideband PB-correction : Upto HPBW
 - RFI at L-Band : Lose 200 ~ 500 MHz
Image from
Frazer Owen
(NRAO)
Abell-2256 : intensity-weighted spectral-index
Ongoing work : HPC methods + more software integration + more efficient minor-cycle algorithms + uncertainty estimates, improving autoflag......